## Slide 1
Protection using MU-RTS/CTS
Date: 2016-01-18
Authors:

## Slide 2: Background
Current SFD supports MU-RTS/CTS exchange for DL and UL MU transmissions [1]:
  The spec shall define a frame that solicits simultaneous CTS responses from multiple STAs to protect DL MU transmission.
  MU-RTS/CTS frame exchange may be used for protection of MU transmissions during that TXOP.
  The CTS sent in response to a frame that solicits simultaneous CTS shall be transmitted on one or more 20 MHz channels.
However, there are still issues to overcome.

## Slide 3: Issue
TXOP holder (AP) cannot identify STAs that sent CTS frame in response to MU-RTS.
  Multiple STAs’ CTS frame transmission is combined together.
  Multiple STAs use the same frame format.
  As different STA has different path loss and transmission power, an AP cannot estimate the transmitter(s) of CTS frame based on received power.
  Even though an AP can allocate different transmission bandwidth of CTS frame for different STA, most likely more than one STA may send CTS frame in any 20 MHz channel that MU-RTS frame occupies.
After receiving CTS frame, if the AP schedules DL/UL MU transmission without knowing that target STAs are ready, it will end up with scheduling unnecessary resource to STAs that are not ready.

## Slide 4: DL/UL MU Transmissions
For efficient DL/UL MU transmission, an AP may need further information prior to actual data transmission.
  For UL transmission, the AP needs to know if target STAs have buffered data to send.
    For this purpose, an AP may need to poll Buffer Status Report frames to candidate STAs.
  For DL power save STAs, the AP needs to know if target STAs are in active state and ready to receive.
    For this purpose, an AP may need to schedule PS-Poll frame transmission.
  The AP needs to know frequency selective channel status information of target STAs for better OFDMA scheduling.
  The AP needs to have channel sounding for MIMO/BF weight matrix calculation.

## Slide 5: Proposed Mechanism
After MU-RTS/CTS frame exchange, an AP is recommended to check which STA has responded its MU-RTS frame by requesting short response frame before actual data exchange.
  AP schedules actual data frame exchange only to those STAs that responded the short frame.
  As these short frames are necessary for other purposes, this frame exchange does not give additional protocol overhead.
  As these response frames are short, UL MU transmission may be preferable (but not limited to).
  Multiple different types of short frame exchange are available, e.g.,
    Buffer-status report, PS-Poll, OFDMA/MIMO sounding

## Slide 6: Operation Examples
UL MU transmission
  After MU-RTS/CTS frame exchange, AP sends a Trigger frame that solicits UL Buffer Status Request (BSR) frames.
    Target recipients of the Trigger frame may be identical to that of MU-RTS frame.
  Those STAs that responded CTS frame sends a short frame including Buffer Status information.
  Based on BSR, the AP schedules UL MU data frame transmission and sends corresponding Trigger frame.
AP1
STA1
STA2
MU-RTS
CTS
Trigger
BSR
ACK/
Trigger
STA3
BSR
CTS
DATA
ACK
DATA

## Slide 7: Operation Examples
DL MU transmission
  After MU-RTS/CTS frame exchange, AP sends a Trigger frame that solicits PS-Poll frame for power save STAs.
    Target recipients of the Trigger frame may be identical to that of MU-RTS frame.
  Those STAs that responded CTS frame sends the PS-Poll frame.
  Based on PS-Poll reception, the AP transmits DL MU data frames.
AP1
STA1
STA2
MU-RTS
CTS
Trigger
PS-Poll
ACK
STA3
PS-Poll
CTS
DATA 1 & DATA 3
ACK
ACK

## Slide 8: Operation Examples
Other possible cases:
  Other short frame exchanges can also be used to check which STA has responded its MU-RTS frame:
    Short data frame exchange
    Sounding procedure for beamforming and/or OFDMA scheduling
  For response to a Trigger frame for BSR, responding STA may also include data MPDU as long as it fits into the allocated RU.
  Details on criteria for defining short frame exchange is TBD.

## Slide 9: Summary
An AP cannot identify which STA responded to MU-RTS frame transmission.
This presentation recommends a mechanism for an AP to figure out which STA has sent back CTS frame as a response to MU-RTS frame.
  After MU-RTS/CTS frame exchange, an AP is recommended to check which STA has responded its MU-RTS frame by requesting short response frame.
As these short frames are necessary for other purposes, this can solve the mentioned issue without having additional protocol overhead.

## Slide 10: SP
Do you agree to add to the TG Specification Framework:
  4.y.z After MU-RTS/CTS frame exchange, an AP should trigger short frame exchange to check which STA has responded to the MU-RTS frame.
    Examples of such frames are Buffer Status Request, PS-Poll, etc.
    Details on definition for short frame are TBD.

## Slide 11: References
[1] 11-15-0132r13, “Specification Framework for TGax"