## Slide 1: Fragmentation for MU frames – Follow up on acks
Name | Affiliation | Address | Phone | Email
Alfred Asterjadhi | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alice Chen |  | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Date: 2016-01-17

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tao Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | ttian@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 4
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Zhou Lan |  |  |  | Zhou.lan@mediaTek.com
Russell Huang |  |  |  | russell.huang@mediatek.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Peter Loc | Huawei |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  |  | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  |  | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 8: Authors (continued)
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | mfischer@broadcom.com
Matthew Fischer |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 9: Introduction
The concept of allowing fragments in A-MPDUs for 11ax was discussed in [1]
  “The spec shall support fragmentation negotiation in A-MPDUs for HE STAs.”
The concept of negotiating different fragmentation levels was discussed in [2]
  “The 11ax fragmentation negotiation shall allow the following fragmentation types (levels) to be indicated:
    Level 0: No support for fragments
    Level 1: Support for a fragment in a “VHT” single MPDU only
    Level 2: Support for up to one fragment per MSDU in an A-MPDU
    Level 3: Support for multiple fragments of an MSDU per A-MPDU”
We propose to finalize the ack. procedures for these negotiated levels
  Using baseline fragmentation/defragmentation signalling for fragments in A-MPDUs
Note: Assumption is that fragments of an MSDU in an A-MPDU have different lengths
MPDU
AP
STA1
STA2
F-MPDU
Trigger
MU TXOP 1
F-MPDU
MPDU
Trigger
MU TXOP 2
…
BA
F-MPDU
SN = 2
FN = 0
MF = 0
SN = 3
FN = 1
MF = 1
SN = 3
FN = 0
MF = 1
…
SN = 4
FN = 0
MF = 0
SN = 5
FN = 0
MF = 1

## Slide 10: Acknowledgement rules
Fragmentation – Level I
  Originator may aggregate one fragment of an MSDU in a “VHT” single MPDU[2]
  Recipient responds with an Ack to the eliciting “VHT” single MPDU
  Acknowledgement rule:
    Recipient shall respond with an Ack frame to a fragment carried in a “VHT” single MPDU that solicits an immediate response
Fragmentation – Level II
  Originator may aggregate up to one fragment per MSDU in an A-MPDU [2, 4]
  Recipient responds with Ack (if “VHT” single MPDU) or Compressed BA (C-BA)
    Each bit in the BA Bitmap indicates successful RX of the received MSDU’s fragment or the MSDU
    No changes to the BlockAck frame format.
  Acknowledgement rule:
    Recipient shall respond with:
      Ack frame to a fragment carried in a “VHT” single MPDU that solicits an immediate response
      C-BA frame to an A-MPDU (non-“VHT” single MPDU) that solicits an immediate response
        Each bit in BA Bitmap indicates successful reception of the carried fragment or of the full MSDU

## Slide 11: Acknowledgement rules (2)
Fragmentation – Level III
  Originator may aggregate more than one fragment per MSDU in an A-MPDU [5]
  Recipient responds with Ack (if “VHT” single MPDU), C-BA (if no fragments), or “dedicated” C-BA (if fragments)
Acknowledgement rules:
  Recipient shall respond with:
    Ack frame to a fragment carried in a “VHT” single MPDU soliciting immediate response
    C-BA frame to an A-MPDU not containing fragments and soliciting immediate response
    “Dedicated” C-BA frame format to A-MPDU containing fragments and soliciting immediate response
      “Dedicated” C-BA frame signals RX state for each of the multiple fragments of an MSDU
Next slide provides some more details on “Dedicated” C-BA frame format

## Slide 12: “Dedicated” BA frame
Currently the Fragment Number subfield in all defined BA frames is 0
  Propose to use a nonzero value of the Fragment Number subfield to indicate an X number of fragments of each MSDU for which the BA Bitmap field carries the receive state
    It enables fragment ack signaling with any BA format (Multi-TID, Multi-STA, Compressed)
Acknowledgement by using the “Dedicated” C-BA frame
  Assume each MSDU has X fragments at most, that means the dedicated C-BA can ack. 64/X MSDUs
    Every X bits in the BA Bitmap are used to acknowledge the MSDU or its fragments.
      Each bit in the BA Bitmap acknowledges the successful RX of a single MSDU in the order of SN, with the first X bits of the BA Bitmap corresponding to the MSDU with the SN that matches that of the SSN subfield
  For unused fragment numbers of an MSDU, the corresponding bits in the bitmap are 0.
  Since the overhead increases with # of fragments, we prefer that max number of fragments is 4 (i.e., X=4)
    Note: Though a preference, this is not strictly necessary, since more than one value of the FN can be used to indicate the max number of fragments (e.g., a value of FN=1 indicates X=2, a value of FN=2 indicates X=4, etc.)
2
8
Octets
Fragment Number
Starting Sequence Number (SSN)
BA Starting Sequence Control
BA Bitmap
Starting SN
SN + 1
SN + 15
…
4 bits
12 bits

## Slide 13: Summary
We discuss the ack. procedure for 11ax fragmentation
  Using baseline fragmentation/defragmentation procedure for signaling fragments
  Using Ack, BlockAck frames to acknowledge A-MPDUs carrying fragments
    I.e., no need for using Basic BlockAck frames
  Allowing seamless use of 11ax fragmentation with BA sessions using Compressed BA, multi-STA BA, and multi-TID BA frames.

## Slide 14: Straw Poll 1
So you support to add to the SFD:
  11ax STAs shall use the baseline (de-)fragmentation for signaling 11ax fragmentation within an A-MPDU
    The SN identifies the MSDU/MMPDU, and the FN identifies the fragment of an MSDU/MMPDU

## Slide 15: Straw Poll 2
Do you support to add to the SFD:
  Under 11ax fragmentation, the following acknowledgement rules apply:
    Fragmentation – Level I
      Recipient shall respond with an Ack to a fragment carried in a “VHT” single MPDU soliciting immediate response
    Fragmentation – Level II
      Recipient shall respond with:
        Ack frame to a fragment carried in a “VHT” single MPDU soliciting immediate response
        C-BA frame to an A-MPDU soliciting immediate response
          Each bit in BlockAck Bitmap indicates successful reception of the carried fragment or of the full MSDU

## Slide 16: Straw Poll 3
Do you support to add to the SFD:
  Under 11ax fragmentation, the following acknowledgement rules apply:
    Fragmentation – Level III
      Recipient shall respond with:
        Ack frame to a fragment carried in a “VHT” single MPDU soliciting immediate response
        C-BA frame to an A-MPDU that does not carry fragments and soliciting immediate response
        “Dedicated” C-BA frame to an A-MPDU carrying fragments and soliciting immediate response
          Each bit in BlockAck Bitmap indicates successful reception of each of the carried fragments
          The max number of fragments for which the BA frame signals the receive status is contained in a nonzero value of the FN subfield of the BA frame
      Maximum number of fragments per MSDU in the eliciting A-MPDU transmitted by the originator shall be 4

## Slide 17: References
[1] C. Ghosh (Intel) et.al., 11-15-1102r0 Fragmentation with MU operation
[2] A. Asterjadhi (Qualcomm Inc.) et. al., 11-15-1318-00-00ax-Fragmentation for MU frames-Follow up