## Slide 1: Modelling of Spatial Separation in the 11ay Channel Model
Date: 2016/01/17
Authors:

## Slide 2: Abstract
This contribution summarizes the existing proposal for the extension of legacy IEEE 802.11ad channel models to cover future MIMO use cases in 802.11ay. Further concepts are proposed for modelling spatial separation of phased array antennas (PAA).

## Slide 3: Introduction
The 11ay channel model shall support multiple hybrid MIMO configurations [1]
  Configurations to be supported
    1 PAA, single pol., 2 SS
    1 PAA, dual pol., 2 SS
    2 PAA, single pol., 2 SS
    2 PAA, dual pol., 4 SS
    1 PAA, dual pol., 1 SS
  Spatial separation
    Configurations 1, 2, 5 feature a single PAA ()
    Configurations 3, 4 feature two PAAs with
  How to model channel for Config. 3, 4?
    Target: Reuse mature 11ad SISO-Model as much as possible
    Focus here on Config. 3, Config. 4 is a straightforward extension

## Slide 4: Review of submission [1] (Intel)
Channel model in Configuration 3
Properties
  Channel derived from a single omnidirectional channel-impulse-response (CIR) tap realization
  model antenna responses at RX and TX of a single PAA
  and () model antenna weight vectors (AWVs)
  Assumptions
    distance between PAAs is assumed to be zero, i.e.
    all PAAs “see” the same channel
from [1]:

## Slide 5: Review of submission [2] (InterDigital)

## Slide 6: Direct link based approach
Channel model for
Properties
  Channel derived from (here two) independent omnidirectional CIR tap realizations and
  approximates PAA response by Gaussian gain pattern as in 11ad [3]
  Assumptions
    distance between PAAs is large, i.e.
      actually two independent SISO links
    no control of

## Slide 7: Comparison of channel models
Scenario:
Conference Room STA-AP, NLOS, 2x2 MIMO, 90° beamwidth → 49 beams per TX / RX, equal seeds for both graphs, SNR=20dB
Direct link based approach:
→ micro structure macro structure
Intel [1]:
→ micro structure macro structure

## Slide 8: Options for modeling spatial separation
Channel model
Options
  Modify and
    Consider response of complete array of subarrays, instead of response of a single subarray
      e.g., for an antenna with two ULAs, inter-ULA separation and intra-ULA separation (equal for TX & RX) and number of total sub-elements
    Amplitudes of rays + polarization, AoAs and AoDs can be reused from .11ad model
    and shaped to fit the dimensions of and

## Slide 9: Options for modeling spatial separation
Channel model
Options
  Modify and (cont.)
    For 2 rectangular arrays
The phase variations for elements of first PAA
The phase variations for elements of second PAA
With the phase variations as above, the phasors can be written as in [1]
the number of subantenna elements of the first PAA
Figure from [1]

## Slide 10: Options for modeling spatial separation
Channel model
Options
  2. Use different channel realizations (here 4)
    , i.e. dependent on the inter-PAA distances
    Requires simple raytracing algorithm within the channel model
      Simple raytracing based geometric reflections
      More precise control over the amplitudes, AoA/AoDs of all rays
    Low complexity alternative: Definition of quasi-static set of TX / RX positions and raytracing results for comparability
      → no need for raytracer implementation within channel model

## Slide 11: Conclusion
Analysis of different approaches of the .11ay channel model with respect to spatial separation
  all PAAs “see” the same omnidirectional channel (Intel) [1]
  independent CIRs and angular rotation (InterDigital) [2]
  independent CIRs (direct link based approach)
Proposal of further options to model spatial separation
  phase variations
  different channel realizations
  combination of 1 and 2
Recommendation
  Have a clear specification regarding modelling of inter-PAA distance
  Option 2 seems reasonable

## Slide 12: References
A. Maltsev et al, “Extension of Legacy IEEE 802.11ad Channel Models for MIMO and Channel Bonding”, IEEE doc. 11-15/1356r1.
R. Yang and A. Sahin, “Feasibility of SU-MIMO under Array Alignment Method”, IEEE doc. 11-15/1333r0.
A. Maltsev et al, “Channel Models for 60 GHz WLAN Systems”, IEEE doc. 11-09/0334r8.

## Slide 13: Appendix

## Slide 14: Comparison of approaches
InterDigital [2]:
Intel [1]:
Direct link based Approach:
red: changes with respect to 11ad SISO channel model implementation