## Slide 1: On the Channel Model for Short Range Communications
Date: 2016-01-18
Authors:

## Slide 2: Abstract
The usage scenarios for 11ay include short range communications in mmWave.
The channel model for IEEE802.11ay should capture those scenarios accurately.
In this presentation, we suggest some changes in the current channel model document [2] to meet this requirement.

## Slide 3: Background (1/3)
Nine different usage scenarios are identified for TGay in reference [1]. The link distances for five of those scenarios are less than 10 meters. For ultra short range (USR) communications, the link distance can be less than 10 cm.
# | Applications and Characteristics | Propagation Conditions
1 | Ultra Short Range (USR) Communications: -Static,D2D, -Streaming/Downloading | LOS only, Indoor <10cm
2 | 8K UHD Wireless Transfer at Smart Home: -Uncompressed 8K UHD Streaming | Indoor, LOS with small NLOS chance, <5m
3 | Augmented Reality and Virtual Reality: -Low Mobility, D2D -3D UHD streaming | Indoor, LOS/NLOS <10m
4 | Data Center NG60 Inter-Rack Connectivity: -Indoor Backhaul with multi-hop* | Indoor, LOS only <10m
5 | Video/Mass-Data Distribution/Video on Demand System: - Multicast Streaming/Downloading - Dense Hotspots | Indoor, LOS/NLOS <100m
6 | Mobile Wi-Fi Offloading and Multi-Band Operation (low mobility): -Multi-band/-Multi-RAT Hotspot operation | Indoor/Outdoor, LOS/NLOS <100m
7 | Mobile Fronthauling | Outdoor, LOS <200m
8 | Wireless Backhauling with Single Hop: -Small Cell Backhauling with single hop -Small Cell Backhauling with multi-hop | Outdoor, LOS <1km <150m
9 | Office docking | Indoor LOS/NLOS < 3 m
Video/audio clip, magazine, newspaper, etc.
Train Station
Movie, video/audio clip, magazine, newspaper, etc.
Office docking with multiple wireless links
Kiosk

## Slide 4: Background (2/3)
The IEEE 802.11ay channel model [2] is built on the IEEE 802.11ad channel model and it considers the calculations of the i-th ray channel phasor vector at the transmitter and the receiver, i.e., and , by using the angle-of arrival (AoA) and the angle-of-departure (AoD) information.
  The IEEE 802.11ad channel model [3] generates the AoA and the AoD of each ray from one point to another point in 3-D.
[Using 2D model as an example]

## Slide 5: Background (3/3)
In 11ay channel model document [2], five different SU-MIMO configurations are proposed for 802.11ay.
In those configurations, Configuration #3 and Configuration #4 consider two physically separated PAAs at transmitter and receiver.
Configuration #3
Configuration #4

## Slide 6: MIMO Channel Model for Physically Separated PAAs (1/3)
The channel matrix of i-th ray for Configuration #3 is expressed as
where
Using the same channel space matrix in all elements of the above matrix implies that the channel phasor vectors of different PAAs at the receiver [transmitter], i.e., [], are generated based on the same AoA [AoD] information of the ray.
The same observation can be obtained for
Configuration #4.
Same

## Slide 7: MIMO Channel Model for Physically Separated PAAs (2/3)
In practice, especially for the use cases with short link distances and LOS scenario, the AoAs to the two Rx PAAs may not be assumed the same. And, AoDs from the two Tx PAAs may not be assumed the same.
The current SU-MIMO model may lead misleading performance results for those use cases.
Current SU-MIMO model
SU-MIMO model with the exact LOS direction

## Slide 8: MIMO Channel Model for Physically Separated PAAs (3/3)
To measure the performance of SU-MIMO for Configuration #3 and #4 accurately, we propose to use different AoAs [AoDs] for the rays impinging to [departing from] physically separated PAAs at the receiver [transmitter].
The channel matrix of i-th ray for Configuration #3, for example, will be
where is the receive channel phasor vector of i-th ray with AoA between j-th transmit PAA and k-th recevie PAA and is the transmit channel phasor vector of i-th ray with AoD between j-th transmit PAA and k-th receive PAA.

## Slide 9: An Example for STA-STA & LOS Scenario
We consider the same deployment scenario as that given in reference [4,5] with the following parameters:
Both TX PAA and RX PAAs have the same geometry of elements ().
Distance between the geometrical centers of TX/RX PAAs (Antenna Distance):
Distance between TX and RX devices (Link Distance):
It is assumed that TX PAA 1 beamforms with RX PAA 1 and TX PAA 2 beamforms with RX PAA 2.
The output power of each TX PAA is dBm. The noise figure is dB [6].
No polarization is assumed.
The simulation setup
PPA 2
TX
PPA 1
PPA 2
PPA 1
RX
Interfering links
Direct link
Direct link

## Slide 10: Result: Angle and Channel Gain Differences Between LOS Paths
The angle difference between LOS paths on the direct link and the interfering link may be large depending on the antenna separation.
The complex gain on the LOS paths may also be significantly different. For example, when m and m.
Significant phase rotation
PPA 2
TX
PPA 1
PPA 2
PPA 1
RX
Interfering links
Direct link
Direct link
The angle difference between LOS paths

## Slide 11: Result: Received Signal Strength (1/2)
The received signal strength (RSS) results derived with our simulation model follow the theoretical and measurement results provided in reference [4] as the exact LOS directions for the interfering and the direct links are considered.
Results from using accurate model
Data from [4]

## Slide 12: Result: Received Signal Strength (2/2)
As the current SU-MIMO model assumes that the LOS paths of interfering link and direct link parallel to each other, the RSS on the LOS paths on the interfering links and direct links are always the same.
On the other hand, the RSS results on the direct and interfering link may be significantly different for short link distances when the exact LOS directions are taken into account.
Current SU-MIMO model may not be valid for short link distance.
RSS results on the direct and interfering link with current SU-MIMO model
RSSs on the
Interfering links
RSSs on
direct links
Current SU-MIMO model is valid for long link distance.

## Slide 13: Result: Capacity
Since the LOS paths of interfering link and direct link parallel to each other in the current model, the rank of the channel is always 1 with the SU-MIMO model.
On the other hand, MIMO capacity can be achieved if the accurate AoA and AoD of the LOS paths are considered.
Current SU-MIMO model
The channel capacity when exact LOS directions are considered.

## Slide 14: Conclusion
In this study, we show that the directions of the rays departing from [arriving to] different PAAs, particularly the ones on the LOS paths, should not be assumed the same when the link distance is short.
For Configuration #3 and Configuration #4 in [2], the SU-MIMO channel models should be updated to capture the impact of the physical separation of the PAAs at the devices accurately.

## Slide 15: References
R. Sun, et al, “IEEE 802.11 TGay Use Cases”, IEEE doc. 11-15/0625r3
A. Maltsev, et al, “Channel models for IEEE 802.11ay,” IEEE doc. 11-15/1150r1.
A. Maltsev, et al, “Channel Models for 60 GHz WLAN Systems,” IEEE doc. 11-09/0334r8.
A. Maltsev, et al, “Experimental Measurements for Short Range LOS SU-MIMO,” IEEE doc. 11-15/0632r1.
R. Yang and A. Sahin, “Feasibility of SU-MIMO under Array Alignment Method,” IEEE Doc. 11-15/1333r1
G. Venkatesan, et al, “TGay Evaluation Methodology,” IEEE doc. 11-15/0866r1.

## Slide 16: Straw Poll 1
Do you agree that Equation 3.24 in the Channel Model Document [2] should be changed as follows:
where is the receive channel phasor vector of i-th ray with AoA between j-th transmit PAA and k-th recevie PAA and is the transmit channel phasor vector of i-th ray with AoD between j-th transmit PAA and k-th receive PAA.
Y/N/A:

## Slide 17: Straw Poll 2
Do you agree that Equation 3.25 in the Channel Model Document [2] should be changed as follows:
where is the receive channel phasor vector of i-th ray with AoA between j-th transmit PAA and k-th recevie PAA and is the transmit channel phasor vector of i-th ray with AoD between j-th transmit PAA and k-th receive PAA.
Y/N/A: