## Slide 1: 11ay Features and Design Principles
Date: 2016-01-17
Authors:
Name | Company | Address | Phone | Email
Carlos Cordeiro | Intel |  |  | Carlos.Cordeiro@intel.com

## Slide 2: Purpose
Outline core design principles and assumptions in the design of the 11ay standard
Focus is on core features of the standard; as such, this presentation is not meant to be an exhaustive list

## Slide 3: Operation with legacy
11ay shall be backwards compatible with 11ad
Any DMG STA shall be able to determine the duration of any EDMG PPDU
Absent valid technical reasons, 11ay MAC should reuse as much as possible from 11n/ac MAC
  11n/11ac have developed channel bonding and MIMO concepts which may be applicable to 11ay

## Slide 4: Channelization
Bandwidth-wise, two approaches for channelization are possible: non-overlapping and overlapping
Propose that:
  11ay adopts a non-overlapping channelization (also used in 11n/ac)
  Channel numbers are assigned in such a way that if further 60 GHz spectrum is opened, channels are numbered sequentially

## Slide 5: Channel bonding (1/2)
11ay should support channel bonding
Along these lines, 11ay should adopt the concept of primary channel as in 11n/11ac
Primary channel is the common channel of operation of all STAs in the BSS
To enable backward compatibility with non-EDMG STAs, in an EDMG BSS:
  The BTI, A-BFT and ATI shall be present on the primary channel of the BSS
  The channel width of the primary channel of an EDMG BSS is 2.16 GHz

## Slide 6: Channel bonding (2/2)
Transmissions using channel widths different than 2.16 GHz can only take place during the DTI access period
An EMDG STA shall be able to determine the primary channel and occupied bandwidth from any EDMG PPDU it receives
  Will help with scanning, coexistence and finding of nearby BSSs

## Slide 7: SU and DL MU MIMO
In addition to channel bonding, 11ay shall support both SU and DL MU MIMO
  DL MU MIMO enables distribution of capacity to multiple non-AP/non-PCP STAs
Frame format needs to accommodate scenarios for SU, DL MU MIMO and channel bonding
  PLCP structure must be in such a way that the signaling and channel estimation are placed in the proper location in the header to deal with all these scenarios

## Slide 8: Summary
We have outlined the proposed key features for 11ay ad their design principles
We expect to use these principles and assumptions to guide future submissions on such topics
We welcome comments and feedback towards enhancing this proposal

## Slide 9: Straw polls/motions
Insert the following in section 7.2.4 of the SFD “The channelization used by EDMG STAs is shown in Figure 2 (see slide 4). The circumstances in which a channel can be used in a regulatory domain is determined by local regulatory rules and any additional rules prescribed by the 11ay specification.”
Insert the following in section 4 of the SFD “To enable backward compatibility with DMG STAs, in an EDMG BSS the BTI, A-BFT and ATI is always present on the primary channel of the BSS. The channel width of the primary channel of an EDMG BSS is 2.16 GHz.”
Insert the following in section 6.1 of the SFD “The 11ay specification shall support:
  SU-MIMO
  Downlink MU-MIMO
  Channel bonding of at least two 2.16 GHz channels”
Insert the following in section 4 of the SFD “An EMDG STA shall be able to determine the primary channel and occupied bandwidth from any EDMG PPDU it receives.”