## Slide 1: 1x/2x/4x OFDM Symbol in HE SU PPDU with BCC
Date: 2016-01-18
Authors:

## Slide 2: Background
PHY padding and signal extension were included in SFD [1].
  The pre-FEC padding, post-FEC padding and packet extension methods were included.
  Both pre-FEC and post-FEC padding bits fill up the last OFDM symbol with 12.8us (4x) duration.
  For packets with LDPC, the existing methods looks reasonable approach.
By adjusting the duration of the last OFDM symbol, e.g., 1x, 2x, and 4x OFDM symbol, the padding inefficiency in terms of throughput can be reduced.
Heejung Yu, Yeungnam Univ./NEWRACOM

## Slide 3: Padding Efficiency
Information bits need to be in units of NDBPS.
4x more tones in 11ax results in 4x time larger NDBPS.
Short packets (such as TCP/IP ACK) suffer the most.
Quick SU transmissions from STAs suffer the most.
  In case of MU, it is possible to use smaller RU allocation and multiplex with other packets to reduce down the overall overhead efficiency. (OFDMA is an optional feature.)
Therefore, focus on improving padding efficiency in HE SU PPDU and with 20MHz transmission.
  Short packets will not typically require larger transmission BW such as 40/80/160MHz.

## Slide 4: Proposed Method
Identical to 1x, 2x, and 4x HE-LTF, the duration of the last OFDM symbol is adjusted depending on the number of information bits (Excess information bits) in the last OFDM symbol.
Limit the use of 1x/2x/4x last OFDM symbol to 20MHz SU transmission.
  Focus on resolving the biggest padding inefficiency.
  No changes to the packet padding and packet extension operations in [5].
Further limit the use of 1x/2x/4x OFDM symbol to BCC.
  Small size packets have smaller gain with LDPC.
  Do not need special processing for LDPC codeword size matching (i.e. puncturing/repetition). Simpler design.

## Slide 5: Proposed PSDU_LENGTH Calculation
Time
…
NCBPS
NCBPS
Data Payload
EOF Padding
PHY Padding
PSDU_LENGTH
APEP_LENGTH
Last OFDM Symbol
TOO MUCH!
Time
…
NCBPS
NCBPS,last
Data Payload
EOF
PSDU_LENGTH
APEP_LENGTH
Last OFDM Symbol
2x OFDM Symbol
4x OFDM Symbol
PSDU_LENGTH is approximately calculated to the nearest 1/4, 1/2, or 1 times NCBPS
Proposed Method
11ac PSDU_LENGTH calculation rules

## Slide 6: Proposed Frame Structure for HE SU PPDU
1x OFDM symbol duration
2x OFDM symbol duration
4x OFDM symbol duration
CP
CP
4x OFDM symbol (12.8us)
1x OFDM symbol
3.2us
TX
waveform
CP
CP
4x OFDM symbol (12.8us)
2x OFDM symbol
6.4us
TX
waveform
CP
CP
4x OFDM symbol (12.8us)
4x OFDM symbol
12.8us
TX
waveform
1x/2x OFDM symbol only applied to the last OFDM symbol.
…
…
…

## Slide 7: PSDU_LENGTH Calculation Process
Calculate the numbers of OFDM symbols and bits in the last symbol (NSYM, NDbit,last).
Determine the number of data subcarrier in the last symbol (NSD,1x, NSD,2x, NSD,4x) and NDPBS,last, NCBPS,last.
Calculate the number of padding bits Npad.
Details and examples shown in Appendix

## Slide 8: OFDM modulation
Cases of NSD,4x
  Normal operation as in other OFDM symbols
Cases of NSD,2x
  The even tones(2k, k=1, 2, 3,…) are used.
  The output of IDFT has two repeated waveform. The first half is transmitted.
Cases of NSD,1x
  The every 4th tones(4k, k=1, 2, 3,…) are used.
  The output of IDFT has 4 repeated waveform. The first half is transmitted.

## Slide 9: The strong points
Our proposal, support of 1x/2x/4x OFDM symbol, targets small payload transmissions in OFDM transmissions. (20MHz with BCC)
  In 2.4GHz operations, 20MHz OFDM transmissions are useful due to channel assignment and legacy operations.
  Direct link operations
We reduce amount of EOF padding performed and transmit air-time.
In a STBC case, we can reduce the symbol duration of last two OFDM symbols.

## Slide 10: Conclusion
By exploiting the repeated waveform in 1x, 2x symbol duration cases, we can achieve throughput gain as shown in [3].
The proposed method can be applied to 20MHz BCC OFDM packet transmission where the existing method may not be effective in terms of padding efficiency (or throughput).

## Slide 11: Straw poll
Do you support to add the following text in SDF?
  For HE SU-OFDM packets using BCC in 20MHz bandwidth, the symbol duration of 3.2us, 6.4us and 12.8us (without CP) in the last mSTBC OFDM symbols is optionally supported depending on the number of data bits.
  Details are TBD.

## Slide 12: REFERENCES
[1] 11-15-0132-13-00ax-Specification Framework for Tgax
[2] 11-15-0572-01-00ax-PHY inefficiency of 256FFT per 20MHz
[3] 11-15-0887-03-00ax-effcient padding for last OFDM symbol
[4] 11-15-1092-00-00ax-support of 1x 2x 4x ofdm symbol in he su ppdu
[5] 11-15-0810-00ax-HE PHY Padding and Packet Extension

## Slide 13: Appendix: encoding process

## Slide 14: PSDU_LENGTH and PHY Padding Calculation
Definition of variables
Calculate NSYM.

## Slide 15: PSDU_LENGTH and PHY Padding Calculation
Calculate the number of data bits in the last OFDM symbol.
Define NSD,1x , NSD,2x , and NSD,4x (=NSD).
  NSD is defined in 11ax . Use of above parameters result in re-use of agreed BCC interleaver parameters.
 | NSD,1x | NSD,2x | NSD,4x
20MHz | 48 | 102 | 234

## Slide 16: PSDU_LENGTH and PHY Padding Calculation
If 0 <NDbit,last mSTBC  NDBPS,1x, (1x OFDM symbol duration)
  NDBPS,last = NDBPS,1x (NCBPS,last = NCBPS,1x)
  BCC case: interleaver size = NSD,1x
  Data subcarrier with 4k (k=1,2…) indices excluding DC and pilot tones are used.
If mSTBC  NDBPS,1x <NDbit,last mSTBC  NDBPS,2x, (2x OFDM symbol duration)
  NDBPS,last = NDBPS,2x (NCBPS,last = NCBPS,2x)
  BCC case: interleaver size = NSD,2x
  Data subcarrier with 2k (k=1,2…) indices excluding DC and pilot tones are used.
If mSTBC  NDBPS,2x <NDbit,last mSTBC  NDBPS,4x , (4x OFDM symbol duration)
  NDBPS,last = NDBPS,4x(=NDBPS) (NCBPS,last = NCBPS,4x(=NCBPS))
  BCC case: interleaver size = NSD,4x(=NSD)
  Data subcarrier with k (k=1,2…) indices excluding DC and pilot tones are used.

## Slide 17: PSDU_LENGTH and PHY Padding Calculation
PSDU_LENGTH
Calculation of the number of PHY padding bits (0~7 bits)