## Slide 1: Congestion control for UL MU random access
Date: 2016-01-18
Authors:

## Slide 2: Abstract
Discussing performance boundary UL MU random access
Proposing to use transmission probability as a congestion control parameter (included in TF-R) for random access
Providing simulation results that shows the effect of the transmission probability in terms of network throughput

## Slide 3: Random Access (RA) for MU transmission
A STA with OBO decremented to 0 randomly selects any one of the assigned RUs for random access and transmits its frame.
  [MU Motion 27, September 17, 2015, see [1]]
RA prevents excessive overhead caused by point-to-point transmission control for UL MU
  Expected to be used for many applications such as Buffer Status Report (BSR), control frame, UL data

## Slide 4: Acceptance rate of RA
The acceptance rate of RA has analytical boundary
  Resemblance with slotted ALOHA
  Defined by the number of active STAs (OBO=0, Nt.STA) & assigned RUs (NRU)
Maximum rate: ≈ 37%
  When Na.STA = NRU
  The performance of RA keeps decreasing from the maximum value as the number of active STAs increases
    Assigned RUs are occupied by collisions
  RA has the same RU utilization with SU when Na.STA is near 30

## Slide 5: Throughput analysis with Random Access BSR (RA BSR) [2]
Measuring network throughput (1 BSS, 20 MHz)
Repeating RA BSR, UL MU transmission
  Simple integer RU allocation without frequency selectivity
  Comparing to basic access SU transmission
MU transmission with RA shows better throughput when congestion level is low
HOWEVER, MU throughput drops much faster than SU
The network throughput of SU is maintained by congestion control (exponential backoff)

## Slide 6: Congestion control parameter for RA
An HE AP is allowed to broadcast a TBD parameter in the trigger frame to the STAs so that STAs can initiate the random access process after the trigger frames.
  [MAC Motion 41, September 17, 2015, see [3]]
The TBD parameter can be used for enhancing the efficiency of RA
  Congestion control
  E.g., CWOmin or CWOmax, transmission probability
We prefer to adopt transmission probability

## Slide 7: Transmission probability pt for RA
AP broadcasts pt with trigger frame for RA
  Optimal pt*: min(NRU, Na.STA)/Na.STA
Each STA attempts a Bernoulli trail with pt
  Only STAs with 0 OBO attempt the trial, and if fail, do not transmit (regarded as collision)

## Slide 8: Comparison between CWO control and pt
CWO control
  CWO cannot be applied to STAs that already have OBO
    Once a STA draws its OBO, it won’t be affected by following CWO controls
  The effect of CWO will kick in the next RA
pt
  Currently delivered pt is used for the following response
    pt instantaneously affects current access behavior
  pt can be applied to every active STAs every time AP sends it
We find pt is more immediate and fairer

## Slide 9: Calculating pt
In order to calculate pt, AP requires the number of active STA (Na.STA)
Finding the approximated Na.STA
  Tracing event history
    # of collision, success, no-access
  Measuring RSSI level of RA or simultaneous CTS
Several solutions can be applied for implementation

## Slide 10: Performance analysis with pt
Measuring throughput enhancement of pt, and observing the effect of Na.STA estimation error
Repeating the same simulation on slide 5 with different pt values
  pt = min(NRU, α∙Na.STA)/ α∙Na.STA α: error scaling
  pt helps to maintain the throughput of MU RA near maximum regardless of increase of the number of active STAs
  pt still enhances the throughput of MU RA even with large amount of estimation error

## Slide 11: Conclusion
In order to fully take advantage of UL MU random access, a proper congestion control mechanism is necessary
‘a TBD parameter’ in TF can be used for congestion control of RA
Simulation results shows that transmission probability successfully control the network congestion

## Slide 12: Strawpoll
Do you agree to add to the TG Specification Frame work document?
4.5 UL OFDMA-based random access
  An HE AP is allowed to broadcast transmission probability, pt,, in the trigger frame to the STAs so that STAs can initiate the random access process after the trigger frames.
  Each STA with zero OBO attempts a Bernoulli trial with probability pt. If it fails the trial, it shall not transmit its frame, and reselect its OBO.

## Slide 13: References
[1] 15/1105r0 UL OFDMA-based Random Access Procedure
[2] 15/1369r1 Random access based buffer status report
[3] 15/1137r1 Triggered OFDMA Random Access Observations