## Slide 1
NAV cancellation issues on MU protection
Date: 2016-01-17
Authors:

## Slide 2: Introduction
TG specified Trigger frame variant MU RTS frame and Simultaneous CTS frame in SFD [1]
  The spec shall define a frame that solicits simultaneous CTS responses from multiple STAs to protect DL MU transmission
  MU RTS may request STAs to send non-HT CTS immediate response
  The MAC format of MU-RTS is a variant of trigger frame format
MU RTS frame and Trigger Frame would be interpreted as a normal data frame for legacy 11 devices to set a NAV by its duration field

## Slide 3: MU RTS/CTS procedure
DL MU and UL MU procedure is initiated by AP
  UL MU procedure is initiated by trigger frame of AP
  DL MU procedure is initiated by DL MU PPDU of AP
  DL and UL MU RTS/CTS procedure is also initiated by MU RTS frame of AP
DL MU RTS/CTS procedure
UL MU RTS/CTS procedure

## Slide 4: Recap : RTS NAV reset
RTS frame is sent by transmitter to set a NAV and to solicit CTS frame
STAs which received RTS frame set a NAV if there are no detection of PHY-RXSTART.indication during (2 × aSIFSTime) + (CTS_Time) + aPHY-RX-START-Delay + (2 × aSlotTime) [2]
If there are no response to the RTS frame, RTS NAV is reset due to the RTS timer

## Slide 5: Idle NAV problem on MU RTS NAV
MU RTS NAV is set by Duration field of M-RTS
  Legacy STAs cannot recognize MU RTS, they recognize MU RTS as a Data Frame
  NAV from Data Frame cannot be reset itself
  RTS NAV reset would not be performed in MU RTS / Simultaneous CTS exchange even though there are no CTS response and Data transmission

## Slide 6: Idle NAV problem on Trigger Frame
MU RTS NAV is set by Duration field of Trigger Frame
  TF - UL Data - BA(M-BA) is basic process of UL MU transmission
  Trigger Frame set long NAV for UL Data but transmission time of Trigger Frame is relatively short
  Hidden nodes cannot recognize absence of UL transmission
  Idle NAV problem would be happened if the trigger frame is failed

## Slide 7: Idle NAV problem
Idle NAV problem could degrade channel usage and it might be worse in dense scenario
  OBSS cannot transmit its data due to its NAV duration even though there are no data transmission on original BSS
  If there are many APs in original BSS area, more performance degradation might be observed due to idle NAV problem

## Slide 8: Solution 1 : MU RTS reset
Similar to conventional RTS reset, MU RTS reset could be adopted to solve MU RTS Idle NAV problem
11ax STAs which update its NAV setting based on MU RTS reset its NAV if no PHY-RXSTAT.indication primitive is detected from the PHY during MU RTS timer duration

## Slide 9: Solution 1 : MU RTS reset
MU RTS reset mechanism cannot solve the M-RTS NAV problem of conventional STAs
  Conventional STAs cannot recognize M-RTS
  Fairness problem between 11ax STAs and legacy STAs

## Slide 10: Solution 2 : CF-END procedure for NAV reset
CF-END frame could reset NAV of receiver STAs
If AP cannot receive simultaneous CTS so that AP would not transmit its DL MU PPDU or Trigger Frame after transmit MU RTS Frame, AP transmits CF-END frame after trigger timer to reset MU RTS NAV

## Slide 11: Solution 2 : CF-END procedure for NAV reset
Idle NAV problem on Trigger type frames could be solved by CF-END procedure for NAV reset
CF-END procedure with trigger timer could be applied on other trigger type frame not only MU RTS to reset NAV

## Slide 12: Conclusion
MU RTS could cause Idle NAV problem
Idle NAV problem is also occurred in Trigger based UL transmission
Using MU RTS reset timer (Solution 1) is a basic solution with no cost
To solve Idle NAV problem on legacy STAs and Trigger Frame case, CF-END Procedure for NAV reset (Solution 2) also needs to be considered as a 11ax feature

## Slide 13: StrawPoll 1
Do you agree to add to the TG Specification Frame work document?
  Spec shall define a MU RTS reset timer to reset the NAV set by MU RTS frame. After receiving MU RTS, if a STA can not detect any signal during the MU RTS reset timer duration, the STA shall reset the NAV set by MU RTS frame at the expiry of the MU RTS timer.
    Y
    N
    A

## Slide 14: StrawPoll 2
Do you agree to add to the TG Specification Frame work document?
  AP may transmit CF-END frame after MU RTS Frame if AP cannot detect the (Simultaneous) CTS frame(s). On the reception of CF-END frame, STAs shall reset the NAV set by MU RTS frame.
  CF-END frame may be transmitted after Trigger Frame if AP cannot detect the UL response(s). On the reception of CF-END frame, STAs shall reset the NAV set by the Trigger Frame.
    Y
    N
    A

## Slide 15: References
[1] 15/0132r9 “Spec Framework”
[2] IEEE Std 802.11-2012