## Slide 1: Channel bonding proposals
Date: 2016-01-18
Authors:

## Slide 2: Abstract
This document describes the basics of channel bonding medium access, discusses issues and proposes a solution to them.

## Slide 3: TXOP extensions for channel bonding (1/2)
Use RTS and DMG CTS frames to allow EDMG STAs to negotiate channel bandwidth and be compatible with legacy STAs
The RTS is transmitted on available channels and indicates which channels are intended to be used by initiator
  Recognized by legacy devices
  A device can be open only to a single channel and receive all the information
Data and ACK frames are transmitted in channel bonding format, but with legacy header.
Example 1:
Example 2:
CTS
TXOP duration
DATA
BACK
CTS
RTS
RTS
CF
-
End
CF
-
End
RTS
CTS
-
to
-
self
TXOP duration
DATA
BACK
CTS
-
to
-
self

## Slide 4: TXOP extension for channel bonding (2/2)
DMG CTS shall be sent in a subset of the channels in which the RTS was sent
  The CTS frame contains an indication of which channels it is sent on
DMG CTS is sent over channels which were available before the RTS was sent (more in the next slide)
  Sent on primary channel if NAV is 0 in the responder
  Sent on a non-primary channel if there was no energy in that channel
As in 11ac, this requires DMG CTS transmitter to be exposed to secondary channel carrier sense enough time to indicate idleness of the channel
Encourage use of CF-End to reset NAV on third party STAs

## Slide 5: Carrier sense considerations
Current 2.4/5GHz requirement is to perform full carrier sense (physical and virtual) on primary channel and energy detection only on non-primary channels
  NAV behavior only applies to primary channel
  Energy detection threshold for non-primary channel is 20dB higher
11ay might want to use this same approach and also consider aspects such as better sensitivity
  Consider approaches such as GI or CP detection in order respect signals that are around sensitivity and not 20dB above it
Current 2.4/5GHz requires PIFS idleness on non-primary channels to enable channel bonding transmission
  11ay should consider using a sensing period that is at least PIFS long
11ay might want to consider aspects of directivity impact on decision about secondary channel availability
  Consider approaches like energy pattern detection

## Slide 6: What is the CCA level
Maintaining NAV on more than one channel is problematic
The standard only specifies CCA energy level and how long the energy has to be there for detection
  Also missed detection probability
CCA level for non-primary channel:
  sensitivity
  sensitivity + XdB
  sensitivity + 20dB (current level for energy detection, range reduced by a factor of 10)
CCA level can be decreased by using methods (implementation) such as GI detection and CP correlation. These become harder when there is a range of GI and CP lengths.

## Slide 7: Channel bonding wakeup?
To support channel bonding, the responder needs to be open over multiple channels before the transmission of the RTS so that it can obtain a valid CCA
It is undesirable for a device to be open for long periods over multiple channels
  Higher power consumption
  Susceptibility to interference from the non-primary channels
We propose to transmit a control frame (e.g., Grant frame) to indicate intent to perform channel bonding transmission
  Receiver could choose to only open to multiple channels after receiving such frame
  Transmitted at most x microseconds before the RTS/DMG CTS exchange

## Slide 8: Grant frame for channel bonding wakeup
If using Grant frame, could use control trailer (11-16/105r0) to indicate intended bandwidth and timing of channel bonding
  Aside from this, rules for Grant/Grant Ack frame transmission would largely remain the same as in 11ad

## Slide 9: Summary
Summarized the basic principles of channel bonding so that they can be formally captured in the SFD
Proposed MAC concepts to enable channel bonding while keeping backward compatibility with DMG operation
Proposed a channel bonding wakeup mechanism to allow for better power saving

## Slide 10: Straw polls / motion
Insert the following in the SFD:
“For 11ay channel bonding, the following apply:
  1) Full carrier sense (physical and virtual) shall be maintained on primary channel
  2) An EDMG STA may transmit a frame to a peer EDMG STA to indicate intent to perform channel bonding transmission to the peer STA. This allows an EDMG STA to choose to operate over multiple channels only after receiving such a frame, thus saving power.”