## Slide 1: High Efficiency Medium Access via Rosters
Date: 2016-01-18

## Slide 2: Abstract
Using rosters reduces medium access overhead, by providing 11ax devices with predictable and unique backoff slots [1, 2].
This presentation provides further information on roster operation, including: A—fundamentals of roster operation and contrast with polling methods; B—effect of OBSS hidden nodes and a contrast with OFDMA; and C—ensuring legacy fairness

## Slide 3: Abstract
Using rosters reduces medium access overhead, by providing 11ax devices with predictable and unique backoff slots [1, 2].
This presentation provides further information on roster operation, including: A—fundamentals of roster operation and contrast with polling methods; B—effect of OBSS hidden nodes and a contrast with OFDMA; and C—ensuring legacy fairness

## Slide 4
43
23
20
15
52
15
44
16
356
16
68
43
22
133
15
AIFS
Backoff
CCA
+IFS
. . .
AIFS
Backoff
CCA
+IFS
RTS
SIFS
CTS
SIFS
A-MPDU
SIFS
BA
Motivation—I
Cf. [1]

## Slide 5
Motivation
Baseline EDCA medium access overhead = the lower of the two quantities shown
Both quantities are usually significant [1]
It is possible to achieve much lower medium access overhead than either of these, by re-using well-proven components that are already part of the protocol

## Slide 6: Approach
Arrange matters so that each STA may obtain a unique backoff slot
Build a roster
Use the roster
Two phases:

## Slide 7: Using a roster
④ AP invokes a roster (now in usage mode):
NAV set for legacy devices (say 5 ms)
Roster invoked:
Roster number
Roster length
Current NAV
Offset within roster length
STA / traffic stream uses its assigned slot(s) modulo offset within roster length
If the assigned slot is reached
within TXOP, STA may transmit
Other devices set NAV and
freeze countdown as usual
Depicted STA will have frozen
its own countdown for each
preceding transmission by
others
AP
STA
…
…
[2, slide 9]
(A)

## Slide 8: Using a roster
At beginning, other devices do not know duration of PPDU
On detecting L-STF during 9 ms
slot time, other devices freeze
backoff decrement and prepare
for rest of PPDU
AP
STA
…
…
Fundamental operation, step 1/3:
?
(A)

## Slide 9: Using a roster
Other STAs read further and extract duration from L-SIG, set NAV
AP
STA
…
…
Fundamental operation, step 2/3:
(A)

## Slide 10: Using a roster
STA transmits for signaled duration, and other device defer
AP
STA
…
…
Fundamental operation, step 3/3:
(A)

## Slide 11: Using a roster
AP takes care of order only; STA will announce duration later
AP
STA
…
…
Corollary 1: No duration scheduling required at AP
?
(A)

## Slide 12: Using a roster
STA’s turn arrives but no data to transmit
STA doesn’t start transmitting
AP
STA
…
…
Corollary 2: No data to transmit causes only  9 ms loss
Other STAs continue countdown
May transmit when their turn arrives, earliest  9 ms later
(A)

## Slide 13: Summary—A
A—Fundamentals of roster operation and differences with polling methods:
Polling methods require specific duration in advance
Polling methods waste airtime (for the full polled duration) if the polled device has no data to transmit
Polling methods require extra PPDU(s) when allocated duration is insufficient, wasting airtime from extra preambles & other overhead
Rosters have none of these drawbacks

## Slide 14: Abstract
Using rosters reduces medium access overhead, by providing 11ax devices with predictable and unique backoff slots [1, 2].
This presentation provides further information on roster operation, including: A—fundamentals of roster operation and contrast with polling methods; B—effect of OBSS hidden nodes and a contrast with OFDMA; and C—ensuring legacy fairness

## Slide 15: Hidden nodes from OBSS
A-MPDU / Block Ack
VIFS + slot time
(if AP bitmap signaled 0)
VIFS + CTS time + SIFS + slot time
(if AP bitmap signaled 1)
STA
Later slot:
VIFS = Vestigial IFS, say 4 ms: for CCA, Rx-to-Tx and Tx-to-Rx turnaround times
(after a busy slot)
[2, slide 15]
AP
(B)

## Slide 16: Hidden nodes from OBSS
A-MPDU / Block Ack
VIFS + slot time
(if AP bitmap signaled 0)
VIFS + CTS time + SIFS + slot time
(if AP bitmap signaled 1)
STA
Later slot:
VIFS = Vestigial IFS, say 4 ms: for CCA, Rx-to-Tx and Tx-to-Rx turnaround times
(after a busy slot)
AP
CCA checks for OBSS hidden nodes
STA gives up slot if CCA high
(B)

## Slide 17: Using a roster
STA’s turn arrives but CCA is high: OBSS hidden node
STA doesn’t start transmitting
AP
STA
…
…
Corollary 3: OBSS hidden node causes only  9 ms loss
Other STAs continue countdown
May transmit when their turn arrives, earliest  9 ms later
(i.e., VIFS + 9 ms later)
(B)

## Slide 18: Summary—B
B—Effect of OBSS hidden nodes and a contrast with OFDMA:
Roster methods automatically reallocate airtime if there is an OBSS hidden node
Roster methods lose only a minimum airtime (IFS + slot time) when OBSS hidden node transmits
Roster moves on to next roster slot—which may not have CCA high
OFDMA loses full allocated duration with OBSS hidden node

## Slide 19: Abstract
Using rosters reduces medium access overhead, by providing 11ax devices with predictable and unique backoff slots [1, 2].
This presentation provides further information on roster operation, including: A—fundamentals of roster operation and contrast with polling methods; B—effect of OBSS hidden nodes and a contrast with OFDMA; and C—ensuring legacy fairness

## Slide 20: Legacy fairness
Previously a method was provided to ensure that devices participating in the roster do not achieve an unfair advantage over legacy devices
―devices defer for an appropriate time after roster use in order to equalize medium access [2, slide x2]
Question arose on how the fairness works at AP
―how does the AP judge when to use roster mode? Using roster mode without guidelines would disadvantage legacy devices
―key is to have roster mode itself defer after use
(C)

## Slide 21
Microseconds
Subtract 40 ms for 24 Mbps Control Rate (RTS 28 ms vs. 52; CTS 28 ms v. 44)
[1, slide 9]
(C)

## Slide 22
Microseconds
Backoff time quickly converges to a mean of 21-22 ms
(C)

## Slide 23: Legacy-fair operation
Rosters access the medium under EDCA rules, with high priority
  VI access category
  Low CWmax
  Low retry limit (say 4)
Every use of any roster by that AP falls under a single state for EDCA access purposes
After a successful roster use, AP defers next use
  AP does not use any new roster until N x 2.5 backoff slots have expired
  N = AP’s estimate of number of legacy devices that should be allowed to transmit, to equalize channel access
(C)

## Slide 24: References
[1] IEEE doc. 11/15-1114r1, “Airtime Analysis of EDCA”, S. Coffey, D.Z. Liu (Realtek), September 2015
[1] IEEE doc. 11/15-1115r1, “High Efficiency in Accessing the Medium”, S. Coffey, D.Z. Liu (Realtek), September 2015