## Slide 1: TG ax Adjustment of Sensitivity and/or CCA Threshold levels
Date: 2016-01
Authors:

## Slide 2: Background
Previous presentations have analyzed DSC and the various scenarios:
Dense Apartments 13/1487r2, 14/0328r2
Airport capacity 13/1489r5
Pico Cell 14/0058r1
E_Education 14/0045r2
Enterprise Scenario 15/0548r0
DSC and Roaming 15/0025r0
DSC Practical Usage 14/0779r2
DSC Channel Select and Legacy sharing 14/0294r0
Dynamic Sensitivity Control 13/1012r4, 13/1290r1
Outdoor Enterprise Scenario and DSC 15/0804r0
DSC Summary 15/0807
Simulations 15/0552, 15/0371, 15/0371

## Slide 3
It has been shown that in every scenarios DSC can improve spatial re-use and improve the throughput.
DSC is NOT fixing the sensitivity/CCA Threshold, it is dynamic and takes care of itself enhancing not only frequency re-use and throughput but also roaming.
DSC is most efficient when changing the sensitivity threshold as no time is wasted looking at the header. The CCA Threshold is effectively changed if sensitivity threshold is higher that CCA Threshold.

## Slide 4: Discussion
Already in the Spec framework is :
“The amendment shall include one or more mechanisms to improve spatial reuse by allowing adjustments to one or more of the CCA-ED, 802.11 Signal Detect CCA, OBSS_PD or TXPWR threshold values. The constraints on selecting threshold values are TBD”
Note that TX power level is included.
Proposal is to add sensitivity threshold.

## Slide 5: Straw Poll
Do you agree to edit clause in Clause 5.1 to the Spec Framework Document as follows:
“The amendment shall include one or more mechanisms to improve spatial reuse by allowing adjustments to one or more of the CCA-ED, 802.11 Signal Detect CCA, OBSS_PD, or TXPWR threshold or receive sensitivity values. The constraints on selecting threshold values are TBD.”