## Slide 1: 160/80+80 MHz channel width signaling
Date: January 19, 2016
Authors:
Name | Company | Address | Email
Menzo Wentink | Qualcomm | Straatweg 66, Breukelen, The Netherlands | mwentink@qti.qualcomm.com
Allert van Zelst | Qualcomm |  | 
Brian Hart | Cisco |  | 
Sigurd Schelstraete | Quantenna |  | 
Sean Coffee | Realtek |  | 
Robert Stacey | Intel |  | 
Vinko Erceg | Broadcom |  | 
Chao-Chun Wang | Mediatek |  | 
Lei Wang | Marvell |  | 

## Slide 2: Problem statement
Many 80 MHz capable VHT devices in the field do not correctly parse 160 or 80+80 MHz BSS channel widths
  The issues vary from no association, repeated reassociation, association at 20 or 40 MHz, etc.
  The BSS channel width is signaled through the VHT Operation element, which is included in Beacons, Association Response, Reassociation Response and Probe Response
0 = 20/40 MHz
1 = 80 MHz
2 = 160 MHz -> broken
3 = 80+80 MHz -> broken
Current Channel Width subfield encoding:
CCFS0
CCFS1

## Slide 3: Proposed solution
The proposed solution is to signal 160 and 80+80 MHz channel width through a non-zero CCFS1 at Channel Width = 1
0 = 20/40 MHz
1 = 80 MHz (CCFS1=0)
1 = 160 MHz (CCFS1 40 MHz away from CCFS0)
1 = 80+80 MHz (CCFS1 >40 MHz away from CCFS0)
2 = 160 MHz (deprecated)
3 = 80+80 MHz (deprecated)
CCFS0
CCFS1
Proposed Channel Width subfield encoding:

## Slide 4: Proposed solution (cont.)
Current VHT Operation Information field parsing |  |  | 
Channel Width | Channel Center Frequency Segment 0 (CCFS0) | Channel Center Frequency Segment 1 (CCFS1) | ¦ CCFS0 - CCFS1 ¦
0: 20/40 MHz | 0 | 0 | 
1: 80 MHz | center 80 | 0 | 
2: 160 MHz | center 160 | 0 | 
3: 80+80 MHz | center primary 80 | center secondary 80 | > 40 MHz
Proposed VHT Operation Information field parsing |  |  | 
Channel Width | Channel Center Frequency Segment 0 (CCFS0) | Channel Center Frequency Segment 1 (CCFS1) | ¦ CCFS0 - CCFS1 ¦
0: 20/40 MHz | 0 | 0 | 
1: 80 MHz | center 80 | 0 | 
1: 160 MHz | center primary 80 | center 160 | 40 MHz
1: 80+80 MHz | center primary 80 | center secondary 80 | >40 MHz
2: 160 MHz | center 160 | 0 | 
3: 80+80 MHz | center primary 80 | center secondary 80 | > 40 MHz

## Slide 5: Test results
Non-zero CCFS1 at Channel Width = 1 was extensively tested with 80 MHz devices
  no issues have emerged
No existing APs were found which have a non-zero CCFS1 at Channel Width = 1

## Slide 6: Proposed normative text
Proposed normative test can be found in
  11-15-1530-01-000m-vht160-operation-signaling-through-non-0-ccfs1