## Slide 1: 60 GHz Focus Area
Date: 2016-01-19
Authors:

## Slide 2: 60 GHz Focus Area -- Goals
Define functional requirements for improved accuracy for NGP
Agree on assumptions
Agree on functional requirements
Develop a framework for specifying a protocol that would satisfy the agreed upon functional requirements
Specify the protocol

## Slide 3: Motivation for .11az & 60 GHz
Location Based Services (LBS) are very important (today and will be even more in future)
Current Indoor Location performance is not satisfactory
If Indoor Location performance is improved then LBS use and importance will increase!
60GHz standards (existing 11ad & future 11ay) have the potential to significantly increase Indoor Location performance and usability
Achieve positioning accuracy of <1cm
Achieve AOA (AZ&EL) accuracy of 1-5deg (depending on # of elements and calibration)
Provide also 3rd rotation axis (ROLL), in addition to AZ&EL (e.g. by using polarization diversity).
Provide location using single AP (with lower accuracy)

## Slide 4: Assumptions for .11az
In 60GHz Ranging and AoA measurement to be completed in one TxOP.
Optimize 11az also for 11ay (support what’s possible with 11ad)
TGaz protocol in 60 GHz should reuse the same ranging/positioning protocols as 2.4G and 5G as much as possible. A 60 GHz device need not be 2.4G and 5G capable.

## Slide 5: Functional Requirements for .11az (to support good positioning using 11ad & 11ay)
Decrease units of Min Delta FTM to reduce latency
Allow for smaller Burst Duration
Allow for STA’s multi-channel operation (in 60GHz)
  Each STA “remembers” beamforming parameters before switching
  STAs can do FTM exchange with unassociated APs.
Extend protocol to support angular measurements and report
Allow for Range and Angular measurements using same messages (measurements inherently possible in 11ad and 11ay)
Allow for Positioning using any number of APs (1 or more) and any additional information (e.g. AOA: AZ, EL)
The protocol shall reduce effect of drift by defining TOD at end of packet and TOA at beginning of packet.

## Slide 6: Straw-Poll/Motion: Do you agree to adopt the following functional requirements?
Decrease units of Min Delta FTM for 60 GHz while maintaining backwards compatibility
Allow for smaller Burst Duration for 60 GHz while maintaining backwards compatibility
Add additional rotational angle (ROLL) to measurement reports
Define TOD at end of packet and TOA at beginning of packet to reduce effect of drift on ranging computation