## Slide 1: Spatial Sharing Enhancement for MIMO Operation
Date: 2016-03-14
Authors:

## Slide 2: 11ad SPSH
SPSH mechanism allows a candidate SP to be scheduled concurrently over the same channel with an existing SP.
DMG STAs involved in candidate SP need to perform measurement before achieving SPSH. DMG STAs involved in existing SP also need to perform measurement if possible.
  Before performing measurement, DMG STAs involved in candidate SP and existing SP need to be BF trained with each other.
  DMG STA shall carry out the measurement employing the same RX antenna configuration as is used when receiving the single spatial stream from the target DMG STA

## Slide 3: 11ad SPSH (cont.)
Directional Channel Quality request/report
  Operating Class and Channel Number fields together specify the measurement channel.
  AID field indicates the target DMG STA.
  Measurement Method field is set to ANIPI (Average Noise plus Interference Power Indicator).
  Measurement for Time Block fields are set to the ANIPI value measured during each measurement unit, which is the ratio of Measurement Duration to Number of Time Blocks.
Measurement Request field format for Directional Channel Quality request
Measurement Report field format for Directional Channel Quality report
 | Operating Class | Channel Number | AID | Reserved | Measurement Method
Octets: | 1 | 1 | 1 | 1 | 1
 | Measurement Start Time | Measurement Duration | Number of Time Blocks | Optional Subelements
Octets: | 8 | 2 | 1 | Variable
 | Operating Class | Channel Number | AID | Reserved | Measurement Method | Measurement Start Time
Octets: | 1 | 1 | 1 | 1 | 1 | 8
 | Measurement Duration | Number of Time Blocks | Measurement for Time block 1 | … | Measurement for Time block M | Optional Subelements
Octets: | 2 | 1 | 1 |  | 1 | Variable

## Slide 4: Problem Statement
11ay SU-MIMO operation
  An EDMG STA with multiple TX antennas can transmit multiple streams to a peer EDMG STA with multiple RX antennas
  An antenna is typically used with a single antenna configuration at a time for transmission or reception of a stream
  Multiple TX/RX antenna configuration combinations for SU-MIMO operation can be obtained via MIMO BF training [1]
  Problem: 11ad SPSH does not consider existing or candidate SP with SU-MIMO transmission.
EDMG STA 1
EDMG STA 2
Blocker
Reflector
Reflector

## Slide 5: Proposal
  EDMG PCP/AP sends an enhanced Directional Channel Quality Request to EDMG STA to request it to perform multiple measurements concurrently employing multiple RX antenna configurations as are used for receiving multiple streams from the target EDMG STA.
    Each of multiple RX antenna configurations corresponds to a specific RX antenna.
    All of concurrent measurements are based on the same measurement configuration (e.g., Measurement Method, Measurement Start Time, Measurement Duration, Number of Time Blocks, etc.).

## Slide 6: Example Frame Format (cont.)
 | Number of RX Antenna Configurations | Reserved
Bits: | TBD | 
 | Operating Class | Channel Number | AID | Reserved | Measurement Method | Measurement Start Time
Octets: | 1 | 1 | 1 | 1 | 1 | 8
 | Measurement Duration | Number of Time Blocks (N) | Measurement for Time block 1 | … | Measurement for Time block N | Optional Subelements
Octets: | 2 | 1 | 1 |  | 1 | Variable
Modifying the measurement report field format for Directional Channel Quality report (Clause 9.4.2.22.15 in P802.11REVmc D5.2) as follows:
  The Number of RX Antenna Configurations field indicates the number of RX antenna configurations used by the EDMG STA to perform concurrent measurements.
    Measurement results corresponding to the first RX antenna configuration are carried in the Measurement for Time Blocks fields of Measurement Report field.
    Measurement results corresponding to the remaining RX antenna configurations are carried in an Extended Measurement Report subelement of Measurement Report field.

## Slide 7
 | Subelement ID | Length | Data
Octets: | 1 | 1 | Variable
 | Measurement for Time Block 1 | … | Measurement for Time Block N | … | Measurement for Time Block 1 | … | Measurement for Time Block N
Octets: | 1 |  | 1 |  | 1 |  | 1
Extended Measurement Report subelement
Example Frame Format (cont.)
N*(Number of RX antenna configurations-1) fields
N*(Number of RX antenna configurations-1) fields

## Slide 8: Summary
11ad spatial sharing mechanism should be enhanced for 11ay to support SU-MIMO transmission in candidate SP and existing SP.
  It is proposed that an EDMG STA can be requested by EDMG PCP/AP to perform multiple measurements concurrently employing multiple RX antenna configurations as are used for receiving multiple streams from the target EDMG STA based on the same measurement configuration.
  The proposed modifications on the Directional Channel Quality Report frame format is backward compatible with 11ad.

## Slide 9: Straw Poll
Do you agree to insert the following text into 11ay SFD?
  The EDMG spatial sharing mechanism shall enable an EDMG STA to perform concurrent measurements employing multiple RX antenna configurations as are used for receiving multiple streams from the target EDMG STA based on the same measurement configuration.
  Yes:
  No:
  Abstain: