## Slide 1: BATS: Network Coding for Wireless Relay Networks
Date: 2016-03-14
Authors:

## Slide 2: Highlights
BATS code stands for ‘BATched Sparse code’
The most advanced network coding technology for wireless networks
Significantly improves the multi-hop relay throughput, and/or reduces delay
Throughput benefits in the following applications:
  Multi-hop transmission
  Multicast
  Content distribution
  Internet of things

## Slide 3: Outline
Introduction to BATS Code
Protocol Design
Implementations
Applications in Wireless Relay Networks

## Slide 4: 1. Introduction to BATS code

## Slide 5: Loss & Relay are Inevitable
WLAN has more and more interference in both 2.4GHz and 5GHz
  Higher loss due to interference
Higher frequency in millimeter wave spectrum, e.g., 60 GHz to be adopted in 802.11AD and 5G
  Higher loss due to obstacles
  Relay for non-line-of-sight transmission
Low power transmission in IoT
  Higher loss due to power constraints
  Relay for long distance transmission

## Slide 6: Multi-hop Networks with Packet Loss
S
T
R1
R2
R3
All links have a packet loss rate 10%
Intermediate Operation | Maximum Rate
Forwarding | 0.9 n
Network coding | 0.9
n is number of hops.

## Slide 7: Random Linear Network Coding
High encoding/decoding complexity
High intermediate node caching/recoding complexity
High coefficient vector overhead

## Slide 8: Low Complexity Linear Network Coding
BATS codes [YY11, YY14]
  Combine fountain codes with random linear network coding
  Rateless codes
Coding-based chunked codes [Tang12, MAB12, YT14]
  Using LDPC codes to construct random linear network coding
  Fixed-rate codes
Modified fountain codes for network coding [PFS05, CHKS09, GS08, TF11]
  Network coding changes the degree distribution
  Cannot reduce coefficient vector overhead

## Slide 9: BATS Code in a Nutshell
A BATS code includes an outer code and an inner code
The outer code is a matrix fountain code at the source node
The inner code consists of random linear network coding at the intermediate network nodes
Outer Code
Inner Code

## Slide 10: Outer Code
Obtain a degree d by sampling a degree distribution Ψ
Pick d distinct input packets randomly
Generate a batch of M coded packets using the d packets
b1
b2
b7
b3
b4
b5
b6
X1
X2
X3
Encoding of batches: Xi = BiGi

## Slide 11: Inner Code
The batches traverse the network.
Encoding at the intermediate nodes forms the inner code.
Linear network coding is applied in a causal manner within a batch.
S
T
Network with linear network coding
Transmission of batches: Yi = XiHi
…, X3, X2, X1
…, Y3, Y2, Y1

## Slide 12: Belief Propagation Decoding
Find a check node i with degreei = rank(GiHi)
Decode the ith batch
Update the decoding graph. Repeat 1.
b1
b2
b7
b3
b4
b5
b6
G1H1
G2H2
Associated with a batch is a system of linear equations:
Yi = XiHi = BiGiHi = BiGiHi
G3H3

## Slide 13: Multi-Hop Transmission
10 Mbps
9 Mbps
8.1Mbps
7.3 Mbps
6.6 Mbps
Fountain Code
10% loss
10% loss
10% loss
10% loss
10% loss
10 Mbps
10 Mbps
10 Mbps
10 Mbps
10 Mbps
BATS Code
10% loss
10% loss
10% loss
10% loss
10% loss
Traditional approaches accumulate packet loss in multi-hop transmission, while BATS code compensates packet loss hop-by-hop.

## Slide 14: Comparison of BATS and Fountain
Chart: No. of Hops
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
BATS (10% loss) | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9
Fountain (10% loss) | 0.9 | 0.81 | 0.729 | 0.6561 | 0.5905 | 0.5314 | 0.4783 | 0.4305 | 0.3874 | 0.3487
BATS (20% loss) | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8
Fountain (20% loss) | 0.8 | 0.64 | 0.512 | 0.4096 | 0.3277 | 0.2621 | 0.2097 | 0.1678 | 0.1342 | 0.1074
  For a network of L hops each with loss rate e, throughput of BATS =1-e , vs throughput of Fountain =(1-e)L.

## Slide 15: BATS vs RLNC
  Much lower computation complexity (99.9% lower)
  Much smaller coding overhead (98% smaller)
 | Coding overhead | Encoding complexity | Decoding complexity | Intermediate node caching
BATS | O(1) | O(1) | O(1) | O(1)
RLNC | O(K) | O(K) | O(K2) | O(K)
*RLNC stands for Random Linear Network Coding
**For transmitting 1000 packets of size 1K bytes

## Slide 16: Achievable Rates of BATS Codes

## Slide 17: Analysis of BATS Codes
Asymptotic analysis provides
  An approach to characterize the achievable rates of BATS codes
  An approach to optimize the degree distribution
Finite-length analysis enables
  Exact characterization of BP/inactivation decoding performance
  Fine-tuning of the degree distributions

## Slide 18: Inactivation Decoding
Inactivation decoding can significantly reduce the coding overhead for BATS code with short block lengths
No. of Packets | Coding overhead |  |  | No. of Inactivation |  | 
 | Ave. | Max | Min | Ave. | Max | Min
1600 | 2.04 | 16 | 0 | 94 | 119 | 72
8000 | 6.30 | 77 | 0 | 215.5 | 268 | 179
16000 | 26.58 | 1089 | 0 | 352.2 | 379 | 302
Simulation results of inactivation decoding
(M=32, q=256)

## Slide 19: Inner Code Design
Systematic adaptive recoding
  Reduce computation cost
  Increase the achievable rate with the same batch size
Interleaved transmission
  Improve the performance with burst loss
  No delay accumulation at intermediate nodes

## Slide 20: 2. Protocol Design

## Slide 21: BATS Protocol
PHY
BATS enabled MAC
BATS enabled IP
BATS enabled TCP
BATS encoding
BATS decoding
Batch forwarding
Batch forwarding
Input file
output file
BATS enabled APP
Existing MAC
Existing IP
Existing TCP

## Slide 22: 3. Implementation

## Slide 23: BATS Code Implementations
BATS recoding has been implemented using low-end wireless routers.
  10 Mbps can be achieve using a single core
Using a particular CPU, >500Mbps decoding throughput can be achieved.
Gbps throughput can be achieved using CPU, GPU or hardware accelerator.

## Slide 25: 4. Applications in Wireless Relay Networks

## Slide 26: Application: Multi-hop Networks
Satellite
Video/signal relays for automobiles
Video relays for traffic surveillance
Wireless access point extender
HDMI repeater

## Slide 27: Application: Multicast Delivery
Shared video in conference rooms
Shared video in concerts/sport games/classrooms
TV broadcasting with relays

## Slide 28: Application: Internet of Things
Device-to-device networks
Sensor networks
Mobile networks
Wireless relays for drones

## Slide 29: References
[YY11] S. Yang and R. W. Yeung, “Coding for a network coded fountain,” ISIT 2011.
[YY14] S. Yang and R. W. Yeung, “Batched sparse codes,” IEEE Trans. Inform. Theory, vol. 60, no. 9, Sep. 2014.
[Tang12] B. Tang, S. Yang, Y. Yin, B. Ye and S. Lu, “Expander graph based overlapped chunked codes,” ISIT 2012.
[YT14] S. Yang and B. Tang, “From LDPC to chunked network codes,” ITW 2014.
[YZ15] S. Yang and Q. Zhou, “Tree Analysis of BATS Codes," IEEE Comm. Letters 2016.
[NY13] T-C Ng and S. Yang, “Finite-Length Analysis of BATS Codes,” NetCod 2013.
[YNY15] S. Yang, T-C Ng and R.W. Yeung, “Finite-Length Analysis of BATS Codes,” ArXiv 2016.
[Huang14] Q. Huang, K. Sun, X. Li, and D. O. Wu, “Just fun: A joint fountain coding and network coding approach to loss-tolerant information spreading,” Mobile Ad Hoc 2014.
[YYCY14] S. Yang, R. W. Yeung, H. F. Cheung, and H. H. Yin, “BATS: Network coding in action,” Allerton 2014.
[XGGC14] X. Xu, P. K. M. Gandhi, Y. L. Guan, and P. H. J. Chong, “Two-phase cooperative broadcasting based on batched network code,” arXiv 2015.