## Slide 1: Relay Improvement: Regarding CID 9058 & 9075
Date: 2016-03-11
Authors:

## Slide 2
Abstract
This contribution highlights a problem for 11ah relay that was associated with CID 9058 & 9075 and discusses potential solutions.

## Slide 3: CID 9058 & 9075
9058 | 0 | 0 | 0 | T | Resolution to i-459 is incorrect. The comment identifies a specific technical problem and a specific technical solution. The assertion in the resolution is thus false. No valid technical reason for rejecting the commenter's proposed change is given. | Include the specification requested, an alternate technical change to satisfy the comment, or record a valid technical reason why no change is required to the draft.
9075 | 10.51.2 | 333 | 41 | T | CID 8459 was rejected based on "non specific technical details have been provided". The original comment was "An S1G relay AP may control the number of relays using No More Relay Flag, however, there does not seem to be any control on how many STAs each relay is allowed to associate. When it comes to controlling relayed traffic flow, it matters how many relays there are and how many STAs are associated with each relay. A limit on the number of STAs that each relay is allowed to associate should be considered." If needed, a presentation to the group can be submitted to explain the technical problem. | Will provide a submission if desired.
Both CIDs relate to CID 8459.

## Slide 4: CID 8459
8459 | 329 | 44 | 9.51.2 | 11-16/0159r1 | An S1G relay AP may control the number of relays using No More Relay Flag, however, there does not seem to be any control on how many STAs each relay is allowed to associate. When it comes to controlling relayed traffic flow, it matters how many relays there are and how many STAs are associated with each relay. A limit on the number of STAs that each relay is allowed to associate should be considered. | Suggest to add a limit on the number of STAs that each relay is allowed to associate, for example in the Relay Activation Response frames | REJECTED (EDITOR: 2016-01-21 17:07:43Z) The comment fails to identify a technical issue in sufficient detail.
Should a S1G STA have some (optional) control on the numbers of STAs its relays can associate?

## Slide 5
11ah supports multi-hop relays
A S1G STA can refuse more relays by setting the “No More Relay Flag”
A S1G relay may use flow control if it is overwhelmed by traffic
A S1G STA can turn on/off a Relay STA
A Few S1G Relay Characteristics

## Slide 6
Currently, there is no restrictions on how many STAs are allowed to associate with a Relay AP
  Theoretically up to 6000 STAs per Relay AP
  Aside from traffic generated by end STAs, there will also be a lot of Reachable Address reporting
Aggregated traffic over a few hops of relays may overwhelm Relays and RootAPs
  Particularly when some S1G STAs may be operating on battery power
  A S1G STA has no control of how many next-hop Relay STAs that its relays STAs have (through the associated Relay APs)
  A S1G STA has no control of how many hops are attached to its Relay STAs (through the associated Relay APs)
  There is no possible way to predict how much traffic is routed through each Relay: it may be overwhelming!
Traffic Congestion Problem

## Slide 7
Such a problem may be hard to solve using existing mechanisms
  Flow control is designed to solve temporary problems, not for long-term issue such as there is too much traffic
  A STA that has visibility of the congested traffic cannot turn off its Relay STAs that are causing the problems easily after coverage has been established
    It is not aware of how many hops are beyond each Relay STAs
    It is not aware of how many Relays are associated with each Relay STAs
    It may cause severe coverage issues
Potential solutions:
  Relay tree add/trim algorithms
  Restrict Relay STA behavior at time of activation
Traffic Congestion Problem

## Slide 8
Relay tree add/trim algorithm
  Complicated
  May be less desirable at the stage of 11ah
Restrict Relay STA behavior at time of activation
  Simple
  Can be easily added
  E.g., by adding (optional) information to Relay Activation Element on how many STAs a Relay STA is allowed to associate through its Relay AP
  Two options:
    Reuse existing reserved bits
    Add optional field
Potential Solutions (1/2)

## Slide 9
Option 1:
  Reuse one or more bits from B3 – B7
  Use a small set of numbers to indicate possible restrictions on the number of STA a Relay STA is allowed to associate: e.g., no restriction, 128, 256, 1024, etc.
Option 2:
  Use one bit in B3 – B7 to indicate the presence of an optional Number of STA field
  Number of STA field may be one or two bytes long
  Indicated number may be precise or quantized as for Option 1
Other changes required to the draft:
  Section 10.51: add some descriptions on limit of number of STAs each Relay STA is allowed to associate through its Relay AP
Potential Solutions (2/2)

## Slide 10: Conclusion
A traffic congestion problem is presented that are associated with CID 9058 & 9075
The problem is shown to be not easily solved using existing mechanisms
Potential solutions have been discussed and presented

## Slide 11: Straw Poll 1
Do you agree that a Relay STA may optionally be restricted to associate with a limited number of STAs through its Relay AP?
Y/N/A:

## Slide 12: Straw Poll 2
Which option do you prefer to limit the number of STAs that a Relay STA is allowed to associate through its Relay AP?
Option 1 as presented on Slide 9
Y/N/A
Option 2 as presented on Slide 9
Y/N/A
Other options
Y/N/A