## Slide 1: Relays for 11ay
Date: 2016-03-11
Authors:

## Slide 2: Abstract
This contribution highlights the importance of relays for 11ay and suggests inclusion of some additional features in the 11ay relaying procedures based on a number of deficiencies identified for the 11ad relaying procedures.

## Slide 3: Introduction
Relays are important for mmW communications, especially for coverage extension and robust connections.
Two 11ay usage models assume relay support: Data Center and Wireless Backhauling [1].
While 11ad supports directional relays, it has some deficiencies.
11ah supports relaying with some advanced features, but it is limited to sub-1Ghz band.
11ay should retain support for directional relays, and update the procedures to enable enhanced functionality.

## Slide 4: Importance of Relays in the mmW Band
Relays can potentially increase the range of BSS/PBSS.
Relays can provide resilience against link outages due to blockage.
Relays can provide alternative connections with lower interference compared to the direct ones.
Relays may increase overall network throughput by breaking a long link into shorter links
  Shorter links may enable higher data rate transmissions
  Due to spatial containment of mmW transmissions using narrow beams multiple relay transmissions may occur simultaneously.

## Slide 5: Brief Overview of 11ad Relay Procedures
11ad supports
  Relay operation types: Link Switching and Link Cooperating.
  Relay operation modes:
    Full-Duplex/Amplify and Forward (FD/AF);
    Half-Duplex/Decode and Forward (HD/DF).
Relay is largely seen as a backup when the direct link between the Source and Destination fails.
HD/DF relays use alternating First and Second Periods to complete transmissions over two hops.
In link switching, FD/AF mode uses Link Change Interval and Data Sensing Time to switch between direct and relay links.
11ad relays have a number of deficiencies

## Slide 6: Problems with 11ad Relaying (1/4)
Lack of support for relay setup between STAs that are outside mutual transmission range.
  Both Source (S-REDS) and Destination (D-REDS) nodes must be part of the BSS/PBSS, and have a direct link setup between them before initiating relay link setup.

## Slide 7: Problems with 11ad Relaying (2/4)
Lack of coverage extension procedures.
  Both Source (S-REDS) and Destination (R-DEDS) nodes must be part of the BSS/PBSS before initiating relay link setup.

## Slide 8: Problems with 11ad Relaying (3/4)
Retransmission inefficiency due to lack of scheduling flexibility of fixed First and Second Periods.

## Slide 9: Problems with 11ad Relaying (4/4)
Lack of support for multi-hop relaying.
  Two 11ay usage models assume multi-hop relays [1]:
    Usage Model 4: Data Center
    Usage Model 8: Wireless Backhauling
  Another usage model could potentially benefit from (multi-hop) relays:
    Usage Model 7: Mobile Fronthauling

## Slide 10: Brief Overview of Relaying in 11ah
11ah allows multi-hop relaying.
Relays are used to extend coverage and reduce energy consumption (higher rate, lower power and shorter transmission time).
Sub-1 GHz (S1G) relay consists of an S1G relay AP, S1G relay STA and a relay function.
STAs can connect to an AP or an S1G relay.
Supports implicit and explicit ACK
The four-addresses scheme is utilized to correctly forward relay frames from source to destination.

## Slide 11: Relay features worth considering for 11ay
Several deficiencies in 11ad relaying procedures have been identified
Some of the deficiencies may be addressed by features similar to the relaying capabilities defined in 11ah
Given these, 11ay may want to consider the following relay features:
  Support for establishing relay links between STAs that do not have direct links
  Support for BSS/PBSS coverage extension using relays
  Support for multi-hop relays
  Support for improved efficiency when using relay links

## Slide 12: Conclusions
While 802.11ad relaying procedure adds important capabilities and imparts robustness to directional transmissions, it has some deficiencies.
Usage models for 11ay require relaying capabilities and 11ay should consider to enhance 11ad relaying features.

## Slide 13: Reference
[1] IEEE 802.11ay Usage Scenarios: 11-15-625r3, Sept 2015

## Slide 14: Straw Poll 1
Do you agree that 11ay shall provide additional relay capabilities and efficient relay procedures relevant to 11ay usage models?
Y/N/A:

## Slide 15: Straw Polls 2
Do you agree that one or more of the following features should be considered by 11ay?
11ay should consider supporting relay links between STAs that are outside communication range of each other.
Y/N/A:
11ay should consider BSS/PBSS coverage extension using relays.
Y/N/A:
11ay should consider supporting flexible channel utilization on successive relay hops.
Y/N/A:
11ay should consider multi-hop relays.
Y/N/A: