## Slide 1: Random Access UL MU Resource Allocation and Indication
Date: 2015-03-13
Authors:

## Slide 2: Summary
  Random access mechanism for UL OFDMA enables the following devices to reach the AP via UL OFDMA.[1]
    Unassociated STAs
    Associated STAs waking up from sleep state
While associated STAs which has an established AID can inform the AP of its buffer status in the TF-R initiated UL MU and later on be allocated a regular RU, unassociated STAs presently cannot.
In this contribution, we consider to support regular UL MU transmission for unassociated STAs by defining a user identifier and appropriate signaling in the TF.

## Slide 3: Resource allocation for unassociated STAs
After successfully obtaining a random access RU, unassociated STAs may need more resources to complete its transmission. The reasons can be one of the following.
200 byte RUs
250 byte frame
300 byte frame
RA RU AID 0
RU 2 AID X
RA RU AID 0
RA Trigger Frame (TF-R)
RU 4 AID Y
RU 5 AID Z
STA 2 selects RU 1
STA 1 selects RU 3
UL MU PPDU (STA 2, NULL+BSR)
UL MU PPDU (STA3)
UL MU PPDU (STA1, 200 byte+BSR)
UL MU PPDU (STA 4)
UL MU PPDU (STA 5)
1. By the nature of random access UL MU, the obtained RU by the STA may not be enough for data transmission.
-In addition, due to high collision rate of random access UL MU, there is a great benefit for the AP to shorten the duration of the UL MU making this more prevalent.
RU 1 AID 2
RU 2 AID X
RU 3 AID 1
RU 4 AID Y
RU 5 AID Z
250 byte RUs
Trigger Frame (TF)
Using AID 1, and AID 2, the AP allocates RU 1 and 3 to unassociated STAs 1 and 2.

## Slide 4: Resource allocation for unassociated STAs
2. When the random access UL MU is intended solely for BSR acquisition. [2]
BSR only
RA RU AID 0
RA RU AID 0
RA RU AID 0
RA Trigger Frame (TF-R)
RA RU AID 0
RA RU AID 0
UL MU PPDU (STA2, NULL+BSR)
UL MU PPDU (STA3, NULL+BSR)
UL MU PPDU (STA1, NULL+BSR)
byte+BSR)
UL MU PPDU (STA5, NULL+BSR)
UL MU PPDU (STA4, NULL+BSR)
After successfully obtaining a random access RU, unassociated STAs may need more resources to complete its transmission. The reasons can be one of the following.
RU 1 AID 1
RA 2 AID 2
RU 3 AID 3
RU 4 AID 4
RU 5 AID 5
UL MU PPDU (STA2, QOS DATA)
UL MU PPDU (STA3, QOS DATA)
UL MU PPDU (STA1, QOS DATA)
UL MU PPDU (STA5, QOS DATA)
UL MU PPDU (STA4, QOS DATA)
All STAs sends BSR and hope for an RU on next TF
STAs 1-5 are all unassociated STAs

## Slide 5: User identifier for unassociated STAs, etc.
In order to support Triggered UL MU transmission, the AP and STA must agree on an identifier for unassociated STAs
  For simplicity, we suggest to use a function of the STA MAC address
  e.g. (Last 12 bits of the MAC address)
However because this ID can be random in nature and can collide with TBD AIDs used by TF-R and AIDs of associated stations.
  We suggest to explicitly signal the type of user ID,
  e.g. (0, associated, 1 - unassociated, 2 - random access, etc.)
The Per User Info field includes the following subfields:
MCS [4 bits]
Coding type [# bits TBD]
RU allocation information [# bits TBD]
SS allocation [# bits TBD]
DCM [1 bit]
User identifier field [12 bits]
User ID type [#bits TBD]
- 0- associated, 1-unassociated, 2 –random access, etc

## Slide 6: Merits of user ID type signaling
Can support regular UL MU for unassociated STAs.
A user ID type field in the per User info in the TF is a much faster way of checking whether random access RUs are present.
User ID field can be used for different purposes independently.
(e.g. Associated STA, Unassociated STA, Random Access STA)

## Slide 7: Conclusion
In this presentation, we propose that unassociated STAs be able to receive allocated RUs in a regular UL MU transmission.
We presented a simple signaling scheme to prevent collisions between other defined user IDs.

## Slide 8: References
[1] 11-15-0875-01-00ax-random-access-with-trigger-frames-using-ofdma.pptx
[2] 11-15-1369-01-00ax-random-access-based-buffer-status-report.pptx

## Slide 9: Strawpoll 1
Do you agree to add the following in the SFD
The spec shall support regular UL MU transmission for unassociated STAs.

## Slide 10: Strawpoll 2
Do you agree to add the following in the SFD.
For unassociated STAs, a TBD function of the STA’s MAC address shall be used as a user ID in the trigger frame.

## Slide 11: Strawpoll 3
Do you agree to add a user ID type in the per User info field of the Trigger frame to distinguish between associated STAs, unassociated STAs, and random access user IDs.