## Slide 1
Simultaneous NAK for MU GCR-BA
Date: 2016-03-15
Authors:

## Slide 2: Introduction
GCR BA is a feature of 11aa and its performance in OBSS was presented in TGax[1][2]
In order to enhance its performance of GCR BA, TG specified MU-BAR frame to be utilized in GCR BAR and BA frame exchange[3]
Only the STAs indicated in MU-BAR frame could report its transmission success via indicated RU by MU-BAR frame[4]

## Slide 3: Recap : GCR BA
Trigger variant MU-BAR solicits Multiplexed Block ack for GCR BA
  Selecting bad channel (low SINR) STAs might enhance performance of GCR BA[1][2]
  AP STA selects destinations of BAR or MU-BAR to minimize Packet Loss Rate
802.11aa GCR BA
802.11ax GCR BA

## Slide 4: Recap : GCR BA
GCR BA mechanism with large number of destination STAs would provide effective retransmission opportunities for Multicast transmission
MU-BAR could reduce degradation caused by exchange of BAR and BA frame
  BA multiplexing reduces repeated BAR-BA air time
GCR BA overhead vs Retransmission profit
  To guarantee QoS Packet Loss Rate, Multicast PPDU could be retransmitted based on GCR BA feedback information
  Selecting appropriate destinations of BAR(or MU-BAR) could maximize retransmission profit

## Slide 5: Limitation of 11ax GCR BA
11ax GCR BA could reduce overhead but it still operates based on limited BA information of selected STAs
  Requesting BA for STAs which failed to receive multicast PPDU is not a easy problem
  Some STAs having packet error on multicast PPDU cannot report its failure information unless AP requests a BA frame of the STAs

## Slide 6: Proposed Solution : NAK for Multicast Transmission
Simultaneous NAK frame for failure STAs
  MU-BAR sets an RU for simultaneous NAK frame(s)
  The STAs which cannot decode its multicast PPDU(s) but is not requested by MU-BAR shall transmit simultaneous NAK if there are available RU(s) for simultaneous NAK

## Slide 7: Proposed Solution : NAK for Multicast Transmission
AP could allocate a single common RU for failure STAs
  Different to OFDMA Random Access, all failure STAs transmit simultaneous NAK for announcing multicast failure via the common RU

## Slide 8: Proposed Solution : NAK for Multicast Transmission
Similar to simultaneous CTS, simultaneous NAK could be transmitted by multiple failure STAs
MU-BAR shall provide enough information for simultaneous NAK
  MCS or Rate (Base rate is preferred)
  RU
  AID for Common RU or Group AID
  Common RU indicator for Simultaneous NAK (if Group AID is used)

## Slide 9: Proposed Solution : NAK for Multicast Transmission
Receiving NAK means that there are at least one group cast STA which couldn’t receive some data frames
  If AP need to enhance packet delivery ratio, perform retransmission procedure
  AP might determine whether to retransmit or not based on GCR BA and simultaneous NAK
Simultaneous NAK feedback could be utilized for controlling its multicast MCS and rate not only for retransmission
If there are valid simultaneous NAK in common RU(s), AP could transmit cascade MU-BAR to collect precise BA information

## Slide 10: Solution Analysis
Assumptions for analysis
  Single GCR BA procedure for single Multicast PPDU transmission
  PLR for a single Data PPDU : 0 to 0.5 (0.5 to 1 delivery ratio)
  MU-BAR transmission and NAK/BA transmission are always success
  N = [30 100] Number of group cast STAs
  Single Retransmission for Simultaneous NAK or NAK BA
  k = [1 3 5 9] RU for MU GCR BA

## Slide 11: Solution Analysis
N=30 k=1 (SU GCR BA(11aa) case for GCR BA PLR)

## Slide 12: Solution Analysis
N=30 k=3 (3RU MU-BAR case for GCR BA)

## Slide 13: Solution Analysis
N=30 k=5 (5RU MU-BAR case for GCR BA)

## Slide 14: Solution Analysis
N=30 k=9 (9RU MU-BAR case for GCR BA)

## Slide 15: Solution Analysis
N=100 k=9 (9RU MU-BAR case for GCR BA)

## Slide 16: Solution Analysis
Analysis Results
  S-NAK shows better PLR performance than MU GCR-BA only case
  Especially S-NAK shows overwhelming PLR performance when the PLR requirement of Multicast PPDU is very low and its channel is not too lossy
  S-NAK is more effective if there are many destinations of multicast STAs
  For 95% delivery ratio of single PPDU
(N,k) | (30,1) | (30,3) | (30,5) | (30,9) | (100,9)
S-NAK | 0.0025 | 0.0025 | 0.0025 | 0.0025 | 0.0025
GCR-BA | 0.0461 | 0.0392 | 0.0331 | 0.0235 | 0.0297
Ratio | 18.44 | 15.68 | 13.24 | 9.4 | 11.88

## Slide 17: Conclusion
11ax GCR BA could be enhanced by allocating common RU for simultaneous NAK
Especially simultaneous NAK is more effective on high QoS system
Cascade MU GCR BA with common RU could be used to collect more precise packet delivery information of multicast PPDU

## Slide 18: StrawPoll 1
Do you agree to add to the TG Specification Frame work document?
  4.7.X The spec might define a mechanism to utilize a simultaneous NAK (TBD) for multicast operation
    When AP allocates common RU for a simultaneous NAK, multicast destination STAs, which cannot successfully decode its multicast PPDU, transmit a simultaneous NAK frame (TBD) via the allocated common RU
    Y
    N
    A

## Slide 19: References
[1] 15/0046r0 “11aa GCR-BA Performance in OBSS”
[2] 15/0320r1 “GCR-BA Performance with Measurement Report in OBSS”
[3] 15/0132r15 “Spec Framework”
[4] 15/1043r1 “Overall Protocol of UL MU BA for Multicast Transmission”