## Slide 1: TG ax Enterprise Scenario, TPC and DSC
Date: 2016-03
Authors:

## Slide 2: Background
15/1609 “Adaptive CCA and TPC “ proposed a TPC scheme where the STA, if close to its AP, reduced its TX power, accompanied with a change in the CCA threshold.
16/0212 “Enterprise Scenario with DSC and Color”, evaluated the spatial re-use of the Enterprise Scenario.
This presentation investigates if TPC improves Spatial Reuse for the Enterprise Scenario.

## Slide 3
An Example of Adaptive CCA/PC Scheme
STA’s OBSS_PD threshold and transmit power are based on received RSSI (e.g, received RCPI of the beacon or path loss) and constants determined by AP
  Adjusted_TX_Pwr = TX_Pwrnominal –RSSIAP +constant 1
  Adjusted_OBSS_PD = OBSS_PDnominal + RSSIAP + constant 2
Limits the OBSS_PD threshold to be
  -82dBm<Adj_CCA<-62 dBm
(Note: OBSS_PD for AP can be set to the value based on the farthest STA.)
Less adjustment
More adjustment
Higher SR,
Lower TX PWR
Lower SR,
Higher TX PWR
From 15/1609r0

## Slide 4: TPC and CCA from 15/1609
Adjusted TX_PWR = 15 – RSSI + A -5<TX_PWR<15 dBm
Adjusted CCA = -82 + RSSI + B -82<CCA<-62 dBm
Assume the STA is close to the AP then RSSImax
TX_PWR = 15 – (RSSImax – A) = -5
Hence, (RSSImax – A) = 20…………………………………………….1)
CCA = -82 + RSSImax + B = -62
Hence, (RSSImax + B) = 20…………………………………………….2)
Therefore A = -B so we need only define a single factor, A IF we maintain the 20dB TX_PWR reduction.
How do we fix a value for A? Say RSSI = -35dBm (~2m)
Then A = -55dB This seems reasonable
A = -45dB would set the TX _PWR reduction to 10dB rather than 20.

## Slide 5: CCA
Adjusted CCA = -82 + RSSI + B -82<CCA<-62 dBm
This is, in fact, DSC
Using DSC, CCA= RSSI – DSC Margin RSSI < DSC Upper Limit
Therefore
-82 + RSSI + B = RSSI – DSC Margin
DSC Margin = 82 –B
For B = 62dB and -82<CCA<-62 dBm
DSC Margin = 20 dB, and DSC Upper Limit = -42dBm

## Slide 6
Enterprise scenario
Refer to 16/212r4

## Slide 7: Topography
STAs

## Slide 8: 4 Channel re-use and TPC
Set A = -55dB
DL AP to furthest STA -45dBm TX-PWR = 15 + 45 -55 = 5dBm (10dB reduction)
UL from furthest STA to AP = -48 -10 = -58dBm
DL AP to closest STA -37dBm TX-PWR = 15 + 37 -55 = -3dBm (18dB reduction)
UL from closest STA to AP = -40 -18 = -58dBm
TPC causes the UL RSSI at the AP to be the same for ALL STA, i.e. -58dBm
BUT AP to AP interference is -64dBm, ALL UL IS BLOCKED, only 6dB SNIR

## Slide 9: Interference
With TPC the TX_PWR is less for the closer STAs
But outer STAs still at full power.
Wanted UL RSSI is constant but now reduced for most STAs

## Slide 10: TPC 10dB
We see that TPC causes all UL RSSI to be the same for all STAs.
Using a 20 dB TX_PWR reduction, all UL are Blocked by the other AP DL packets.
Let’s try to use 10dB TX_PWR reduction, i.e. A = -45dB
DL AP to furthest STA -45dBm TX-PWR = 15 + 45 -45 = 15dBm (0dB reduction)
UL from furthest STA to AP = -48 = -48dBm
DL AP to closest STA -37dBm TX-PWR = 15 + 37 -45 = 7dBm (8dB reduction)
UL from closest STA to AP = -40 -8 = -48dBm
(TPC causes all UL to be same RSSI)
AP to AP interference is -64dBm, SNIR = 16dB, still “blocked”
All UL traffic is blocked by DL traffic in the OBSS.

## Slide 11: Summary for 4 CH - DSC
Using TPC does not add any significant advantage
for Spatial Reuse for the enterprise scenario.
Similar results for 20 and 10 dB TX_PWR reduction.
(Note: STA columns represent 4096 possibilities, AP 64 possibilities)
TPC | Shadowing | STA DL blocked by other STA UL and other AP DL |  | STA UL blocked by other STA UL and other AP DL | 
 | dB | STA | AP | STA | AP
NO | 0 | 6 | 2 | 88 | 36
 | 5 | 10-60 | 2-7 | 200-400 | 27-35
A= -55dB | 0 | 0 | 2 | 256 | 64
 | 5 | 0 | 1-9 | 400-652 | 64
A = -45dB | 0 | 6 | 2 | 256 | 64
 | 5 | 8-70 | 4-8 | 360-676 | 61-64

## Slide 12: TPC if Other BSS not TPC
TPC | Shadowing | STA DL blocked by other STA UL and other AP DL |  | STA UL blocked by other STA UL and other AP DL | 
 | dB | STA | AP | STA | AP
NO | 0 | 6 | 2 | 88 | 36
 | 5 | 10-60 | 2-8 | 200-400 | 27-35
A= -55dB | 0 | 0 | 2 | 4016 | 64
 | 5 | 0 | 2-8 | 4016 | 64
A = -45dB | 0 | 6 | 2 | 256 | 64
 | 5 | 8-60 | 4-8 | 2000-4000 | 64
If other BSS not using TPC, then UL results are bad.
Note: “Blocked” means <20dB SNIR

## Slide 13: Conclusions
With the Enterprise Scenario example, TPC can show some very small improvement for STA DL traffic but worse results for the UL traffic
Unless ALL STAs use TPC, total blocking UL occurs.
No real incentive for a STA to use TPC.