## Slide 1: Considerations on MU initial link setup
Date: 2016-03-15
Authors:

## Slide 2: Abstract
Addressing the impact of flooding on Initial Link Setup(ILS) in dense network environments
  Scanning-Authentication-Association
Considerations on MU ILS using UL OFDMA random access
Introducing conditions and expected form of MU ILS

## Slide 3: Problem definition
Initial Link Setup (ILS) flooding might degrades overall network throughput severely in dense network
  A large number of STAs move simultaneously
    Subway/train platform
    Break time of stadium or e-education
  The increase of the number of contending STAs raises the mean medium access delay
  Even worse for ILS delay of individual STAs
In order to support dense network environments, ILS flooding must be resolved

## Slide 4: Flooding in ILS
Probe flooding can be prevented by adaptive scanning
  Passive scanning/802.11ai FILS[1]
    Beacon frames includes all the necessary elements for scanning
    Overheard Probe responses can be used for scanning
    Not every STA transmits probe request
It is much harder to prevent flooding in auth., and assoc.
  Auth., Assoc. responses must be transmitted by unicast
    Including individual contents for each STA
      Security keys, status code, AID
  AP does not know which STAs are expected to transmit the requests

## Slide 5: ILS using MU feature
11ax has a perfect feature to resolve the problem
  UL OFDMA random access
UL OFDMA combines multiple contentions for UL transmission
With random access, STAs could voluntarily participate in UL MU transmission with trigger frame

## Slide 6: MU ILS indication
In order to prevent STAs from beginning contentions for ILS, AP should notice the presence of MU ILS operation during scanning
  Indication for MU ILS operation is necessary
    i.e., HE operation elements in beacon, probe resp. or discovery frames
    1-bit on/off indication
    More information using more bits
      i.e., Number of MU ILS in the current beacon period
  STAs may decide whether it participates MU ILS
    Depending on STAs’ status and requirements

## Slide 7: Conditions for triggering MU ILS
TF must define trigger type for MU ILS
  DL MU response of ILS is different from general data transmission
  type dependent common info. may be used for various purposes
    i.e., transaction sequence number, differentiated ILS, delayed response
    Common info. of Auth./Assoc. resp. may be included
  Temporary AID is necessary
  Unassociated STAs don’t have their AID
  AID is required for Per user info. in trigger frame, SIG-B in DL MU response
    For each allowed RA RU, a different temporary AID can be assigned
      Included in Per user info.
      Any unassigned AIDs (may include reserved AIDs ( 2008~)) can be used
    Requesting STA transmits its auth./assoc. req. through a randomly chosen RU
      Keep the temporary AID of the chosen RU
    Temporary AID could be maintained until MU assoc.
      Actual AID will be delivered with DL MU assoc. resp.

## Slide 8: DL response of MU ILS
In order to maximize the efficiency of MU ILS, auth./assoc. resp. should be transmitted with DL MU PPDU format
  auth./assoc. req. solicit unique type of responses
  Current M-BA format is not suitable for DL response of MU ILS
    User specific info. must be included in the DL response
      i.e., Status code, Security key info., AID
  DL MU auth./assoc. resp. replace DL acknowledgement of UL requests
    The format of DL MU auth. resp. is TBD
  Requesting STAs check the temporary AID in SIG-B and MAC address in the corresponding RU, to see if their requests accepted successfully without collision
    If the temp. AID and MAC address don’t match, discards the temp. AID

## Slide 9: Expected form of MU ILS
With MU ILS operation activated, AP triggers MU auth. req.
  State 1 STAs transmit auth. req. with random access
    Requesting STA will keep the temporary AID
  AP transmits DL MU auth. resp. to the STAs without collision
    AP may add DL ctrl./mgmt. frames with DL MU auth. resp.
For state 2 STAs, AP triggers MU assoc. req.
  MU assoc. req. may not be random access
    Temporary AID from MU auth. can be reused
  AP assigns actual AID with DL MU assoc. resp.
  MU assoc. trigger may not follow right after MU auth.

## Slide 10: Applications of MU ILS with other 11ax features
TF cascading
MU cascading structure

## Slide 11: Conclusion
In order to prevent throughput degradation in dense network environments, ILS flooding problem must be resolved
UL OFDMA can be adopted for MU ILS
  Further applications are possible with other 11ax features in order to enhance the efficiency
  Several elements must be defined for enabling MU ILS
    i.e., MU ILS indication, trigger types

## Slide 12: Strawpoll 1
Do you agree to add to the TG Specification Frame work document?
x.y.z the spec shall define a procedure for multiuser initial link setup (MU authentication, MU association)

## Slide 13: Reference
[1] Draft P802.11ai_D6.4