## Slide 1
MU-RTS/CTS for TWT Protection
Date: 2016-03-16
Authors:

## Slide 2: Introduction
TWT function is agreed in the 11ax SFD[1]:
  The spec shall include a mechanism that allows a target transmission time for a Trigger frame to be indicated. The mechanism is based on implicit TWT operation and additionally enables:
    Broadcast triggered TWT by including a TWT element in the Beacon
    Solicited triggered TWT by using implicit TWT negotiation procedure
  When the broadcast triggered TWT is enabled, STA and AP may exchange TWT request/response to indicate the target Beacon frame to be monitored by the PS STA.
  Multiple TWTs can be indicated in the TWT IE in the Beacon frame by allowing multiple TWT parameter sets in the same TWT IE.
In this presentation, TWT protection rule is discussed based on that of 11ah(S1G)

## Slide 3: Recap: Target Wake Time(TWT)
Solicited TWT: negotiates for TWT parameter
  Inclusion of Trigger frame in TWT SP is indicated in TWT element
Broadcast TWT: negotiates for First TBTT
  Each TWT SP information is indicated in TWT element in Beacon frame

## Slide 4: Recap : TWT element
Broadcast: indicates the use of broadcast TWT[3]
  TWT Flow Identifier: For Broadcast TWT, indicates flow type in TWT SP
Triggered:
  According to [2], [3] set if trigger frame is sent at the start of TWT SP
  According to [4], set if trigger frame is sent at least once during the TWT SP
Implicit
  In SFD: The mechanism is based on implicit TWT operation
TWT Protection: not defined in 11ax
 | NDP Paging Indicator | Responder PM Mode | Broadcast | Reserved
Bits: | 1 | 1 | 1 | 5
 | Element ID | Length | Control | Request Type | Target Wake Time | TWT Group Assignment | Nominal Minimum Wake Duration | TWT Wake Interval Mantissa | TWT Channel | NDP Paging (optional)
Octets: | 1 | 1 | 1 | 2 | 8 or 0 | 9 or 3 or 0 | 1 | 2 | 1 | 0 or 4
 | TWT Request | TWT Setup Command | Triggered | Implicit | Flow Type | TWT Flow Identifier | Wake Interval Exponent | TWT Protection
Bits: | 1 | 3 | 1 | 1 | 1 | 3 | 5 | 1

## Slide 5: TWT protection field in 11ah-RAW
TWT protection field in 11ah: indicates the protection of TWT SP using Restricted Access Window(RAW)
  “A TWT requesting STA sets the TWT Protection subfield to 1 to request the TWT responding STA to provide protection of the set of TWT SPs corresponding to the requested TWT flow identifier by allocating RAW(s) that restrict access to the medium during the TWT SP(s) for that(those) TWTs.”
  “When transmitted by a TWT responding STA that is an AP, the TWT Protection subfield indicates whether the TWT SP(s) identified in the TWT element will be protected.”

## Slide 6: Restricted Access Window(RAW)
RAW allows AP to restrict access for specified duration by group of STAs or types of traffic to improve medium utilization, by reducing collision
STAs which awake to receive Beacon frame are indicated RAW information and restrict their contention in RAW duration

## Slide 7: Limitation to use RAW in TWT Protection
Legacy STAs which cannot decode RAW Parameter Set (RPS) element in beacon may transmit packets in RAW duration
  Differ from 11ah (operates under 1GHz), there are legacy STAs in 11ax scenario
  TWT SP is not protected

## Slide 8: MU-RTS/CTS procedure in TWT SP
In SFD, MU-RTS/CTS frame exchange may be used for protection of MU transmissions during that TXOP
This MU-RTS/CTS procedure can be used to protect DL Data and Block Ack from hidden node in TWT SP

## Slide 9: TWT Protection using MU-RTS/CTS
As in 11ah, the indication of TWT protection in TWT element is needed
  In case of many OBSS STAs near intra BSS STA, TWT requesting STA can indicate to request the protection of TWT SPs
  TWT responding STA which is AP can indicate that MU-RTS will be sent at the start of TWT SP

## Slide 10: TWT Protection using MU-RTS/CTS
  TWT requesting STA which is indicated the use of MU-RTS/CTS by TWT element may wait for MU-RTS at the start of TWT SP
In broadcast TWT, the use of TWT protection in each TWT SP is indicated in TWT element in Beacon frame

## Slide 11: Conclusion
Protection of TWT SP is needed as in 11ah
  RAW operation is not enough because of legacy STAs which cannot decode RAW information
TWT SP can be protected by MU-RTS/CTS procedure
  In 11ax, MU-RTS is agreed for protection
Indication of TWT protection in TWT element is needed
  Using TWT element, TWT requesting STA can indicate to request the protection of TWT SPs
  TWT responding STA can indicate that MU-RTS will be sent at the start of TWT SP

## Slide 12: Straw Poll 1
Do you agree to add to the TG Specification Framework document?
  Spec shall define a mechanism to protect TWT SP.
    A TWT requesting STA sets the TWT Protection subfield to 1 in TWT Request frame to request the AP to provide protection of the set of TWT SPs using a NAV protection mechanism defined in 802.11ax (e.g., (MU-)RTS/CTS or CTS-to-self, etc.).
  Y
  N
  A

## Slide 13: References
[1] 11-15-0132-15-00ax-spec-framework
[2] 11-15-0880-02-00ax-scheduled-trigger-frames
[3] 11-15-1319-00-00ax-scheduled-trigger-frames-follow-up
[4] 11-16-0024-00-00ax-proposed-draft-specification