## Slide 1: LRLP: Discussion of Requirements and Potential STA Categories
Date: 2016-03-14
Authors:

## Slide 2: Abstract
The name Long Range Low Power (LRLP) suggests that this amendment will increase coverage still allow for low power operation
We discuss in absolute terms what we believe is required for LRLP to meet up to these expectations regarding LR and LP. We also discuss how it may differ from 802.11ax
To allow for both LR and LP, we suggest defining more than one non-AP STA category, rather than going for a “one size fits nobody” solution

## Slide 3: Outline
Background
What is achieved by 802.11ax
Requirements on long range
Requirements on low power
Allowing different “STA categories”
Conclusions

## Slide 4: Background
Work on LRLP was initiated to address the IoT market
  Allowing for additional “zero cost” to 802.11ax for dual mode AP
  Coin cell operation at the non-AP STA
  Operation in 2.4 GHz
In the last meeting, various presentations revealed that some may prioritize LR whereas others prioritize LP
From the comments during the presentations, it seems some believe already 802.11ax may be sufficient. To us this does not really seem to be the case without major additions

## Slide 5: What is achieved by 802.11ax?
The introduction of OFDMA naturally allows for relatively narrowband transmission ~ 2 MHz with a 26 sub-carrier RU. Say 10 dB gain in sensitivity. We expect this is not sufficient
802.11ax addresses average power consumption (through MAC enhancements), but not really peak power, which rather relies on PHY changes
Also, 802.11ax do not really exploit the asymmetric nature, when one node is a simple sensor whereas the other is an AP
We expect 802.11ax will neither qualify as long range nor low power

## Slide 6: Requirements on Long Range
We believe a reasonable target for link budget is 20 dB, not just as “stretch”
  We believe this may opens up for new use cases, although it is premature at this stage to speculate
  20 dB was obtained for 802.11ah (10 dB from BW scaling and another 10dB from lower carrier frequency)
  Is also significantly better than 802.11ax, which also may be needed to justify the work

## Slide 7: Requirements on (Average) Low Power
Average power consumption, i.e., what determines battery life time, depends on how often the device needs to leave the low power states and for how long
Especially, scanning for signals that are only present a small fraction of the time may consume more total energy that the actual data transfer
This is primarily something that needs to be addressed by the MAC, and potentially exploiting the asymmetry of the link

## Slide 8: Requirements on Low Power – Peak Power
Peak current consumption determines whether coin cell operation is feasible
In [1] on the order of 60mA is mentioned for LRLP. We believe this figure needs to come down to 10-15 mA. See e.g. [5]
This is primarily something that needs to be addressed by the PHY, and potentially exploiting the asymmetry of the link. Some ideas on next slide

## Slide 9: Requirements on Low Power – Peak Power
Modulation: For the UL, power efficient modulation, e.g. Single Carrier should be considered. For the DL is may still be preferable to use OFDM
FEC coding: For the UL, decoding complexity may not be an issue allowing for powerful FEC coding, whereas for the DL only simples coding may be feasible

## Slide 10: Requirements on Low Power
LRLP has the great advantage of free infrastructure compared to some competing technologies
However, LRLP needs to allow for operation that is on par with BLE, BLE Long Range and 802.15.4 concerning range, and in particular, power, otherwise this may ruin the above advantage and for many use cases not even be seen as an alternative

## Slide 11: Introducing “STA categories”
In e.g. 3GPP, different UE categories are defined, allowing a suitable sub-set of features to be supported for a certain type of device
Taking a similar approach for LRLP, one could e.g. define
  AP STA - Capable of all categories
  LR STA - Strict requirements on sensitivity
  LP STA - Relaxed requirements on sensitivity (allowing for LP). Potentially also naturally allow for WUR
A STA may support more than one category
A LR STA and a LP STA may use different PHYs and may not be able to communicate directly.

## Slide 12: Conclusions
LRLP STAs may be used for very different purposes, somewhere LR is critical, somewhere peak or average power is the main concern
To design one STA category that meets both requirements on LR and LP may lead to a compromise where neither is achieved
We believe 20 dB better link budget for LR and 10-15 mA peak current for LP are reasonable requirements for LRLP

## Slide 13: Straw Poll
Do you believe it makes sense to introduce more than one non-AP STA category for LRLP in order to better address specific requirements and make LRLP a more competitive standard
Y/N/A:

## Slide 14: References
11-15/1108r0, “Technical Feasibility for LRLP”, C. Ghosh et al.
11-15/1112r0,“Use Case of LRLP Operation for IoT ”, C. Ghosh
11-14/1064r0, “Long range, low power design criteria”, J. Kneckt et al.
11-16/0058r0, “Usage scenarios and applications for long range WiFi”, J. Liu et al.
11-16/0022r1, “Long range versus low power and coexistence”, S. Azizi et al.
11-15/1308r0, “Link budget analysis”, M. Park et al.
15-12/0383r0, “A Limitation of Coin Cell Batteries”, S. Emami