## Slide 1: Sounding Design
Date: 2016-03-13
Authors:
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Mingyue Ji |  |  |  | 

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tao Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | ttian@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 4: Authors (continued)
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 6: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
David X. Yang | Huawei | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Jian Yu |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan | +81 46 859 3135 | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  | +81 46 859 5097 | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  | +81 46 859 5107 | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  | +81 46 859 3494 | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  | +81 46 859 4233 | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  | +81 46 859 4222 | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan | +81 46 840 3759 | yamadaakira@nttdocomo.com

## Slide 10: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Tomoko Adachi | Toshiba |  |  | tomo.adachi@toshiba.co.jp
Narendar Madhavan |  |  |  | narendar.madhavan@toshiba.co.jp
Kentaro Taniguchi |  |  |  | kentaro.taniguchi@toshiba.co.jp
Toshihisa Nabetani |  |  |  | toshihisa.nabetani@toshiba.co.jp
Tsuguhide Aoki |  |  |  | tsuguhide.aoki@toshiba.co.jp
Koji Horisaki |  |  |  | kouji.horisaki@toshiba.co.jp
David Halls |  |  |  | david.halls@toshiba-trel.com
Filippo Tosato |  |  |  | filippo.tosato@toshiba-trel.com
Zubeir Bocus |  |  |  | zubeir.bocus@toshiba-trel.com
Fengming Cao |  |  |  | fengming.cao@toshiba-trel.com
Parag Kulkarni |  |  |  | parag.kulkarni@toshiba-trel.com

## Slide 11: Authors (continued)
Minho Cheong | Newracom, Inc. | 9008 Research Dr, Irvine, CA 92618 | +1-949-390-7146 | minho.cheong@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com
Sigurd Schelstraete | Quantenna | 3450 W. Warren Ave, Fremont, CA 94538 |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quanetnna.com

## Slide 12: Outline
We have agreed on the following:
  Sounding sequence shall be NDPA + NDP + Trigger + Feedback
  Tone grouping factors Ng = 4 and Ng = 16 shall be used
This contribution: address many aspects of sounding design
Topic 1: Feedback tone plan + NDP design
  Propose a feedback tone plan that is the same for all bandwidths (20/40/80 MHz)
  Investigate 2X and 4X NDPs and propose to use 2X NDP: shorter duration and nearly optimal in throughput
  Propose packet extension duration and CPs for NDP
Topic 2: Minimum unit of feedback
  In 11ac, minimum feedback unit is 20 MHz
  To efficiently handle OFDMA in 11ax, propose feedback scheme on RUs < 20 MHz
  Granularity: 26 tone RU, AP signals start and end RUs for feedback

## Slide 13: Outline (continued)
Topic 3: Add support for channel quality indicator feedback
  With OFDMA and MU-MIMO, AP needs to assign RUs to STAs that are “good” for them
  Full channel feedback from all STAs over entire bandwidth leads to excessive overhead
  Propose to support a channel quality indicator (CQI-only) feedback mode
  Coarser channel feedback is given to AP to help allot RUs to users with lesser overhead
Topic 4: Feedback parameters – who controls and where to put them?
  Quantities: Ng, Nc (#columns in compressed beamforming feedback), quantization, feedback bandwidth, CQI Indicator (full feedback or CQI-only)
  Propose to put them in NDPA
  AP controls these quantities
    Except for the case of NDPA addressed to a single STA requesting SU feedback. Here, STA controls Ng, Nc, quantization

## Slide 14: Topic 1 – Feedback tone plan + NDP design

## Slide 15: Feedback tone plan
Design Idea
  Align feedback tones for different PPDU BW
  Use multiples of 4 for both Ng = 4 and Ng = 16
  Start from tone index -4 and 4
20 MHz
  Ng = 4 → [-120:4:-4 4:4:120] + edge(± 122, ± 2 )
  Ng = 16 → [-116:16:-4 4:16:116] + edge(± 122, ± 2)
40 MHz
  Ng = 4/16 → [-244:Ng:-4, 4:Ng:244]
80 MHz
  Ng = 4/16 → [-500:Ng:-4, 4:Ng:500]

## Slide 16: NDP 2X vs 4X LTF
How does the goodput change with NDP size? Is 2X LTF as good as 4X LTF?
Simulation setup
  NDP: 2X and 4X LTFs
  STA interpolates (linearly) at pilot tones that fall on feedback tone plan
  Beamformed packet: 2X LTF, ZF beamforming
  Configurations:
    1 user, 4 Tx antennas at AP, 1 Rx antenna at each STA
    3 users, 4 Tx antennas at AP, 1 Rx antenna at each STA
    6 users, 8 Tx antennas at AP, 1 Rx antenna at each STA
  PHY Abstraction

## Slide 17: Typical cases
In 11nE for SU and 11nD for MU
hardly any difference between the options
SU, Ng = 16
MU, Ng = 4

## Slide 18: A more challenging case
Propose to use 2X NDP: shorter duration & no difference in goodput
8x1, 6 users, 11nE, Ng = 4
For more results, see Appendix A

## Slide 19: CP and packet extension
Current 2X HE-LTF can be used with 2 CP values: 0.8 us and 1.6 us
Propose to use the same CP choices for NDP
Propose packet extension of 4 us for NDP
  Computational effort is similar to 11ac where we also have 4uS packet extension

## Slide 20: Topic 2 – Minimum unit of feedback
start
end
80 MHz RU plan
In 11ac, minimum feedback unit is 20 MHz
With OFDMA in 11ax, minimum feedback unit must be smaller
    If scheduling algorithm determines that STA gets a 52 tone RU, wasteful to feed back entire 20 MHz
Proposal: AP signals (start 26 RU, end 26 RU) to indicate subband on which it would like feedback
Benefits
  Extremely flexible: any set of contiguous RUs can be fed back
  No need for special rules: If we restrict minimum feedback unit to 106 tones (for eg), need separate rules for 26 tone RUs between 106 tone RUs
  Cleanly handles the center 26 RU in 20 & 80 MHz

## Slide 21: Topic 3 – CQI-only feedback
For efficient network usage with OFDMA and MU-MIMO, AP needs to assign RUs to STAs that are “good” for them
Full channel feedback (S+V) as in 11ac from all STAs over whole bandwidth leads to very large overhead
Propose to add channel quality indicator (CQI-only) feedback mode
Coarser channel feedback is given to AP to help it allot users to RU with lesser overhead
Exact metric for CQI-only feedback is TBD

## Slide 22: Topic 4 Feedback parameters: who controls and where to put them?
Feedback parameters
  Ng – tone grouping factor
  Nc – number of columns in compressed beamforming feedback
  Quantization
  Feedback bandwidth
  Feedback type (full feedback or CQI-only)
Include all parameters in NDPA
  Feedback computations begin right after NDP
  STA is ready for computations as early as possible
AP controls choice of these quantities (mostly)
  Two qualifiers
    Max Nc that beamformee can support will be negotiated through capability exchange at association
    For NDPA addressed to a single STA requesting SU type feedback, STA controls Ng, Nc, quantization as in 11ac

## Slide 23: Summary
Topic 1: Feedback tone plan, NDP design
  Aligned FB tone plan for all bandwidths: [4:Ng:end, 4:Ng:end] (edge(±2, ± 122) added for 20 MHz)
  NDP: 2X LTF
  NDP supports 0.8 us and 1.6 us CP and shall use 4 us packet extension
Topic 2: Minimum unit of feedback
  Granularity: 26 tone RU
  AP signals start and end 26 tone RUs
  Extremely flexible, clean & doesn’t require special rules
Topic 3: CQI-only feedback
  Propose to support a CQI-only feedback mode
  Coarser channel feedback helps allot “good” RUs to STAs with lesser overhead
Topic 4: Feedback parameters ‒ who controls and where to put them?
  Ng, Nc, quantization, feedback bandwidth, feedback type (CQI-only or full feedback)
  Put them all in NDPA, AP controls their choice
    Two qualifiers for Nc
      Nc is limited by max value beamformee can support – negotiated through capability exchange
      For NDPA addressed to a single STA requesting SU type feedback, STA controls Ng, Nc, quantization

## Slide 24: SP #1
Move to add to the SFD
The tones used for channel feedback shall be a subset of the sets given below:
NDP bandwidth 20 MHz:
Ng = 4 → [-120:4:-4, 4:4:120] + edge(±2,±122)
Ng = 16 → [-116:16:-4, 4:16:116] + edge(±2,±122)
NDP bandwidth 40 MHz:
Ng = 4/16 → [-244:Ng:-4, 4:Ng:244]
NDP bandwidth 80 MHz:
Ng = 4/16 → [-500:Ng:-4, 4:Ng:500]

## Slide 25: SP #2
Move to add to the SFD
2X HE-LTF sequence shall be the only mandatory mode for NDP. 4X HE-LTF shall not be supported in NDP.

## Slide 26: SP #3
Move to add to the SFD
The NDP
always has extension of 4uS
shall support the CP values 0.8 us and 1.6 us

## Slide 27: SP #4
Move to add to the SFD
AP can request beamforming feedback over partial BW which is less than the NDP BW. The indication of the feedback BW goes in NDPA.

## Slide 28: SP #5
Move to add to the SFD
The granularity of channel feedback requested by the AP is a 26 tone RU. The AP signals start and end 26 tone RUs requested for feedback.

## Slide 29: SP #6
Move to add to the SFD
The max Nc for sounding feedback that a BFee can support shall be negotiated through a capability exchange at association.

## Slide 30: SP #7
Move to add to the SFD
AP shall control the Ng, quantization, and Nc of the sounding FB in NDPA except in the special case of a NDPA addressed to a single STA which requests SU type feedback. In the aforementioned special case, the STA controls these quantities.

## Slide 31: SP #8
Move to add to the SFD
A channel quality indicator only (CQI-only) feedback (exact metric TBD) will be supported by the sounding protocol in 11ax. The request for CQI-only feedback goes in NDPA.

## Slide 32: Appendix A

## Slide 33
UMi-LoS

## Slide 34
11nE, 8 antenna AP