## Slide 1: A Multi-Zone Q-D Propagation Model for IEEE 802.11ay Large Scale Environments
Date: 2016-03-15
Authors:

## Slide 2: Motivation
802.11ay introduces new large scale scenarios [1], such as open area, street canyon, etc..
Due to the fact that 802.11ay operates in the 60 GHz band, if the propagation distance is up to several hundred meters, signal propagation may experience multiple significantly different physical effects during its journey.
In order to accurately reflect these effects, this presentation shows a multi-zone propagation model* for 802.11ay new large-scale scenarios.
* The model could be complementary with the Q-D channel model in 11ay.

## Slide 3: An Illustration of Physical Propagation Effects
    Zone 1 (close range free space)
    direct path with few reflections
    Zone 2 (LOS/scattered/waveguide)
    direct path with significant close reflections
    Zone 3 (NLOS scattered)
    strong reflections with some weak direct path energy
    Zone 4 (distant NLOS)
    both direct and reflected signals are weak
** The thicknesses of lines stand for the strengths of signal.

## Slide 4: Preliminary Results of Propagation Effects in Different Transmission Zones
    73GHz measurement campaign;
    Open office scenario;
    RX position A is 6.03m away from TX;
    RX position B is 12.79m away from TX;
TX
RX
position A
RX
position B

## Slide 5: Preliminary Results of Propagation Effects in Different Transmission Zones (2)
Main lobe LOS
A
B
Glass reflections
TX
RX
position A
RX
position B
A
B
    Position A (near-end): narrow delay spread & angular spread;
Joint domain spectrum @ position A

## Slide 6: Preliminary Results of Propagation Effects in Different Transmission Zones (3)
2 order reflections
Glass reflections
TX
RX
position A
RX
position B
A
B
    Position B (far-end): wide delay spread & narrow angular spread;
Joint domain spectrum @ position B

## Slide 7: It looks like that we need more than one set of parameters to reflect the characteristics of channel…

## Slide 8: CIR Structure of Different Zones based on Q-D Channel Modeling Approach
    RX locates in the zone that the propagation is dominated by the direct path and significant close reflections
Copy from [1]

## Slide 9: CIR Structure of Different Zones based on Q-D Channel Modeling Approach (2)
TX
RX
    RX locates in the zone that the propagation is mainly by the reflections with some direct path energy but these are attenuated by distance.
Power, angular spread (AS), or delay spread (DS) may change

## Slide 10: Zones for 11ay New Large-Scale Environments
The typical deployment “scenario” may overlap multiple propagation zones depending on the details of the environments.
Therefore, for example for 11ay new large-scale scenarios,
  Open area – Zones 1 and 2;
  Street canyon – Zone 2 and 3;
  Hotel lobby – Zone 1, 2 and 3;

## Slide 11: Zone Determination Criteria
Option 1 -- Distance Criterion
  According to prior information, a distance within d1 could be classified into Zone 1, and a distance with d2 to d3 could be considered as Zone 2, etc..
Option 2 – Power Criterion based on D-rays ray tracing
    According to the strength of D-rays, e.g., if the LOS ray is significantly larger than the 1st order reflection ray, then Zone 1 is determined;
    After that, R-rays are modeled in each zone.
Option 3 – Clustering Criterion based on R-rays statistical measurements
  Clustering of the joint domain spectrum, and then zones are determined based on the characteristics of the clusters, e.g., narrow delay spread and angular spread corresponds to Zone 2.
  After that, D-rays are calculated in each zone.

## Slide 12: References
[1] IEEE 802.11-15/1150r2, “Channel Models for IEEE 802.11ay”