## Slide 1: Achieving High Efficiency in Medium Access via Roster Mode
Date: 2016-03-14

## Slide 2: Abstract
Rosters (i.e., ordered lists) greatly reduce EDCA medium access overhead, by providing 11ax devices with predictable and unique backoff slots, and without requiring scheduling or duration information [1-3].
This presentation extends the previous ones, via:
A—an intuitive development showing how this mode naturally fits with ordinary EDCA;
B—results showing throughput gains (where the challenge is to make these gains be low); and
C—a motion

## Slide 3: Abstract
Rosters (i.e., ordered lists) greatly reduce EDCA medium access overhead, by providing 11ax devices with predictable and unique backoff slots, and without requiring scheduling or duration information [1-3].
This presentation extends the previous ones, via:
A—an intuitive development showing how this mode naturally fits with ordinary EDCA;
B—results showing throughput gains (where the challenge is to make these gains be low); and
C—a motion

## Slide 4: Intuitive development
(A-1)
Time and system state in EDCA as perceived by an example STA:
Medium busy
…
…
AIFS
Medium usage
(RTS or A-MPDU, maybe collision)
Backoff slots

## Slide 5: Development—II
(A-2)
Time and system state in EDCA as perceived by an example STA:
Medium busy
…
…
AIFS
Medium usage
(RTS or A-MPDU, maybe collision)
Backoff slots
43
9
9
9
43
9
9
s

## Slide 6: Development—III
(A-3)
Time and system state in EDCA as perceived by two example STAs:
Medium busy
…
…
43
9
9
9
43
9
9
s
Medium busy
…
…
34
9
9
9
34
9
9
s
*
*

## Slide 7: Development—IV
(A-4)
In EDCA, if two or more STAs (1) each hear same transmissions;
(2) have same AC; and (3) experience no collisions …
Medium busy
…
…
Medium busy
…
…
… then they remain (unknowingly) synchronized as long as (1)-(3) last

## Slide 8: Development—V
(A-5)
With enough contention, transmitters should usually use RTS-CTS [1];
then, in EDCA, all these devices see the medium usage like this:
… i.e.,  200 s of medium usage or more before every data start
Medium busy
…
…
Medium busy
…
…
43
9
9
9
52
16
44
16
s

## Slide 9: Development—VI
Initiation
(A-6)
If each device knows which backoff slot it may use, and that slot is
assigned only to it, we can eliminate almost all of the  200 s
Initiation informs devices which backoff slots they are assigned within
this short time period (looks like a single TXOP to other devices)
…
9
9
9
s
A-MPDU
A-MPDU
A-MPDU
…
…
…
 4 ms

## Slide 10: Development—VII
Initiation
(A-7)
Roster mode creates the required conditions, so that we can eliminate
almost all of the  200 s
… informs these STAs which backoff slots they may use …
…
…
…
…
 4 ms
AP restricts to a subset of STAs …
… and reverts to
ordinary EDCA at
the end
Internal roster state vanishes

## Slide 11: Implications
Initiation
(A-8)
Processing at each STA follows same form as in ordinary EDCA:
  only some IFS times change ( feasible to implement)
Relation to ordinary EDCA gives roadmap for full protocol,
including exceptions (e.g., defer to end of roster + EIFS, etc.)
…
A-MPDU
A-MPDU
A-MPDU
…
…
…
 4 ms
EIFS

## Slide 12: Summary—A
A—Intuitive development, relation to ordinary EDCA:
Ordinary EDCA already possesses a significant degree of automatic synchronization, simply from devices each following the same protocol
Roster mode systematizes this synchronization for very short time period
Processing at individual STA follows all the rules of ordinary EDCA: only some aspects of timing change
Recovery rules also inherit the structure of ordinary EDCA
(A-9)

## Slide 13: Abstract
Rosters (i.e., ordered lists) greatly reduce EDCA medium access overhead, by providing 11ax devices with predictable and unique backoff slots, and without requiring scheduling or duration information [1-3].
This presentation extends the previous ones, via:
A—an intuitive development showing how this mode naturally fits with ordinary EDCA;
B—results showing throughput gains (where the challenge is to make these gains be low); and
C—a motion

## Slide 14: Frames
Frame formats to enable roster mode: see Appendix A
(B-1)
Initiation
…
…
…
…
44
16
60
16
44
16
s
…
RI
CTS
to
Self
CTS
CF-End
60
If necessary
Variable


## Slide 15: Scenarios
Let’s look at the less promising cases
  It’s natural to discount high gain numbers if there are any assumptions that are at all optimistic
  It’s useful to see how well a mode does in less-than-ideal conditions
(B-2)
1 ms
N = 3
Internal hidden nodes
4 ms
N = 20
No hidden nodes
WORSE
BETTER

## Slide 16: Scenario 1
Roster duration 1 ms, with data packets 150-250 s where present
1/2 of participating devices have data; no internal hidden nodes
EDCA, with 20 competing devices, has  56% efficiency
(B-3)
Initiation
Data
CF-End
IFS + Backoff
196
9
150
9
250
27
200
18
60
Roster mode throughput change: +17%
 65%
Appendix B

## Slide 17: Scenario 2
Roster duration 3.25 ms, with data packets 150-250 s where present
1/2 of participating devices have data; 1/4 have internal hidden nodes
EDCA, with 20 competing devices, has  56% efficiency
(B-4)
Initiation
Data
CF-End
196
9
200
18
120
200
18
60
Roster mode throughput change: +33%
…
CTSs
 74%
Appendix B

## Slide 18: Scenario 3
Roster duration 4 ms, with data packets 150-250 s where present
1/3 of participating devices have data; no hidden nodes (BSS or OBSS)
EDCA, with 20 competing devices, has  56% efficiency
(B-4)
Initiation
Data
CF-End
136
18
200
27
200
27
60
Roster mode throughput change: +48%
…
 83%
Appendix B

## Slide 19: Scenario 4
Roster duration 3.2 ms, with data packets 50-100 s where present
1/2 of participating devices have data; no hidden nodes (BSS or OBSS)
EDCA, with 50 competing devices, packets 75s, has  36% efficiency
(B-4)
Initiation
Data
CF-End
136
9
75
18
75
18
60
Roster mode throughput change: +108%
…
 75%
Appendix B

## Slide 20: Summary—B
B—Roster mode provides consistent gains across scenarios
Even where roster mode has relatively unfavorable conditions while ordinary EDCA does well
It’s not straightforward to find natural conditions where it does not provide a gain
Relative gains of roster mode increase with decreasing packet size and increasing number of competing devices
  I.e., in conditions where channel access overhead is a more significant factor, and in which contention overhead is greater
(B-5)

## Slide 21: Abstract
Rosters (i.e., ordered lists) greatly reduce EDCA medium access overhead, by providing 11ax devices with predictable and unique backoff slots, and without requiring scheduling or duration information [1-3].
This presentation extends the previous ones, via:
A—an intuitive development showing how this mode naturally fits with ordinary EDCA;
B—results showing throughput gains (where the challenge is to make these gains be low); and
C—a motion

## Slide 22: Straw poll 1 (pre-motion)
Do you support adding to the SFD:
The 11ax specification shall include at least one mode of operation in which:
an AP may specify the order (within some specified time period) in which (a specified set of) STAs are permitted to transmit,
no two STAs are permitted to transmit simultaneously,
the durations of the STA transmissions are not signalled in advance of their commencement, and
a STA’s starting transmission time is determined by the actual (rather than scheduled) end of the previous STA’s transmission
(C-1)

## Slide 23: Motion 1
Do you support adding to the SFD:
The 11ax specification shall include at least one mode of operation in which:
an AP may specify the order (within some specified time period) in which (a specified set of) STAs are permitted to transmit,
no two STAs are permitted to transmit simultaneously,
the durations of the STA transmissions are not signalled in advance of their commencement, and
a STA’s starting transmission time is determined by the actual (rather than scheduled) end of the previous STA’s transmission
(C-1)

## Slide 24: References
[1] IEEE doc. 11/15-1114r1, “Airtime Analysis of EDCA”, S. Coffey, D.Z. Liu (Realtek), September 2015
[2] IEEE doc. 11/15-1115r1, “High Efficiency in Accessing the Medium”, S. Coffey, D.Z. Liu (Realtek), September 2015
[3] IEEE doc. 11/16/0102r1, “High Efficiency in Accessing the Medium via Rosters,” S. Coffey, D.Z. Liu (Realtek), January 2016

## Slide 25: APPENDIX

## Slide 26: Appendix A—Frame formats
Example format for Roster Initiation frame:
Octets: 2
1
1
0 or 1
Offset
Roster ID
Control
Number
Variable
Variable
Variable
Variable
Imm Ack
Usage
Protection
Exter Prot
0 to (e.g.) 16
Control indicates which variable bitmaps are present
Number indicates number of bytes per following field
Usage, Immediate Ack, Protection, External Protection are bitmaps

## Slide 27: Appendix B—Throughput gains
For performance of ordinary EDCA, see [1, slide 19]
Roster mode:
Scenario 1: total duration = 196 + 3 x (18 + 200) – 9 + 18 + 60 = 919 s, of which 600 s carry data: efficiency = 600 / 919  65%
Scenario 2: total duration = 196 + 3 x (18 + 120 + 200) + 9 x (18 + 200) – 9 + 18 + 60 = 3.241 ms, of which 12 x 200 s carry data: efficiency = 2.4 / 3.241  74%
Scenario 3: total duration = 136 + 16 x (27 + 200) – 9 + 27 + 60 = 3.846 ms, of which 16 x 200 s carry data: efficiency = 3.2 / 3.846  83%
Scenario 4: total duration = 136 + 32 x (18 + 75) – 9 + 18 + 60 = 3.181 ms, of which 32 x 75 s carry data: efficiency = 2.4 / 3.181 = 75%
Note: both ordinary EDCA and roster mode efficiencies are calculated without Acks or Block Acks

## Slide 28: Appendix C—Notes
In [3], the interframe spacing within roster mode was reduced to a “VIFS” (Vestigial Inter-Frame Space), which could be as small as 4 s or so. The current presentation alters this to 9 s, i.e., a single slot time. The gains over ordinary EDCA are large enough anyway.
Roster mode requires setup and periodic maintenance, which imposes extra overhead. This is not shown explicitly in slides 16-19, but the examples were chosen to account for this effect. With total setup from scratch 500 s-5 ms, 100 uses of a roster before it is discarded, and 6 successful transmissions per roster use, the amortized cost is < 1 s to < 9 s per successful transmission, i.e., at worst less than one backoff slot time. This is why the probability of slot use in the examples was chosen to be quite low: it’s equivalent to a higher probability of slot use with an extra slot to account for setup and maintenance overhead.
For protection of legacy modes: this is an issue that affects all new 11ax modes, and roster mode can use whatever general solution is adopted. For a specific solution, see [3, slides 21-23] (roster mode forms single EDCA state, with sufficient silent time afterwards to permit equalizing channel access opportunities).

## Slide 29: Notes—II
“Internal” hidden nodes are those that are internal to the roster [3]. It is only necessary to protect those STAs that are hidden to one or more STAs that follow it in the roster, given the offset used.
The roster initiation sequence (CTS-To-Self followed by a new RI packet) could be replaced by a single packet, increasing the efficiency. For example, this single packet could be an HE trigger frame. Alternatively, with CTS-To-Self followed by RI, the RI packet may be sent at any rate that can be decoded by the devices in the roster, i.e., not necessarily at the lowest basic rate.
Roster mode is primarily directed at uplink traffic, but there is no reason that downlink traffic cannot be included. The AP may reserve any subset of slots for its own use.. Apart from permitting DL traffic with less overhead, this aids roster management (AP reserves some slots and transfers them to selected STAs via direct exchange of messages). Similarly traffic can in principle be MU / OFDMA.