## Slide 1: Issues on BSS Color Bits Collision
Date: 2016-03-14
Authors:

## Slide 2: Introduction
11ax defines operations depending whether the detected frame is Intra-BSS frame or not [1].
To determine the origin of a frame, BSS color can be used [1].
  HE PPDU includes 6 bits of BSS color subfield in HE-SIG-A field [1].
    Total 64 BSS color values are available.
  Due to the lack of BSS color values, there may be the case* that neighboring BSSs use the same BSS color value.
    * This case is referred as “BSS color collision” hereinafter.
  BSS color collision problem may result in inappropriate operations.
We propose to refine power save and NAV-related operations when BSS color collision is detected.

## Slide 3: Possibility of BSS Color Collision
Distributed assignment
  Taking into account the characteristic of “distributed” system, neighboring APs may select the same value for BSS color.
  Although APs scan surroundings before selecting BSS color value, there is a case that APs are hidden each other.
Especially, in the real-world measurement [2], there are locations at which more than 64 APs are audible.
After the dense deployment of 11ax APs, BSS color collision can be highly probable.
Therefore, it is necessary to discuss 11ax power save and NAV-related operations with BSS color collision.

## Slide 4: Recap: Power Save During Intra-BSS PPDU
HE STA may enter the doze state until the end of a received PPDU including the same BSS color, if the PPDU is [1]
  1. HE SU PPDU and UL/DL flag indicates UL
  2. HE MU PPDU and any of STA identifiers in HE-SIG-B does not match its own STAID or that of a broadcast/multicast identifier
  3. HE Trigger-based PPDU
Intra-BSS
AP
Intra-BSS
STA
STA (Doze)
UL SU PPDU
1. HE SU PPDU
2. HE MU PPDU
3. HE Trigger-based PPDU
Intra-BSS
AP
Intra-BSS
STA
STA
(Doze)
MU PPDU
Intra-BSS
STA
Intra-BSS
STA
Intra-BSS
AP
Intra-BSS
STA
STA
(Doze)
Trigger-based PPDU
Intra-BSS
STA

## Slide 5: Problem 1: Power Save During Inter-BSS PPDU
If Inter-BSS uses the same BSS color value,
STA can enter doze state for particular Inter-BSS PPDUs because of the same BSS color value.
During doze state, STA cannot receive the frame for the STA.
Awake
Doze
Inter-BSS STA
with same BSS color
Inter-BSS Frame*
STA
Intra-BSS AP
DL Data to STA
STA detects Inter-BSS frame and may enter doze state for the same BSS color.
STA cannot receive the frame for the STA during doze state.
Intra-BSS
* The frame includes HE-SIG-A and the frame is SU UL PPDU, MU PPDU which does not carry STAID that should be decoded by STA, or Trigger-based PPDU.

## Slide 6: Recap: Two NAVs
A STA maintains two NAVs (Mandatory or optional TBD) [1].
  One for Intra-BSS frames
  Another for other frames (Inter-BSS frames or Frames that cannot be determined to be Intra- or Inter-BSS)
To determine which BSS is the origin of a frame, the HE STA may use BSS color [1].
By using two NAVs,
  In case that STA sets NAV by Intra-BSS frame and Inter-BSS frame sequentially,
    NAV set by Intra-BSS is not updated by Inter-BSS.
    STA can consider NAV set by Inter-BSS to determine whether to respond to Trigger frame from Intra-BSS.
  CF-End from Intra-(Inter-)BSS can reset only NAV set by Intra-(Inter-)BSS.

## Slide 7: Problem 2a: Incorrect Intra-BSS NAV Setting
If Inter-BSS uses the same BSS color value,
Intra-BSS NAV may be set by Inter-BSS frame after decoding HE-SIG-A of the frame.
STA can response to Trigger frame sent by Intra-BSS AP.
This causes interference to packet reception of Inter-BSS STA.
Inter-BSS Frame*
Inter-BSS STA1
with same BSS color
Intra-NAV
STA
Trigger Frame
Intra-BSS AP
Trigger-based UL Frame
Inter-BSS Frame
Inter-BSS STA2
with same BSS color
TXOP (Inter-BSS)
Inter-BSS
Intra-BSS
Inter-BSS frame sets Intra-BSS NAV.
Interference!
* The frame includes HE-SIG-A and the frame is SU UL PPDU, MU PPDU which does not carry STAID that should be decoded by STA, or Trigger-based PPDU.

## Slide 8: Problem 2b: Not Setting Regular NAV
If Inter-BSS uses the same BSS color value,
Desirable regular NAV is not set.
If CF-End frame resets Intra-BSS NAV, STA can result in packet collision.
Intra-BSS NAV
STA
Intra-BSS DL Frame
Intra-BSS AP
CF-End
TXOP (Intra-BSS)
Inter-BSS Frame*
Inter-BSS STA
with same BSS color
Desirable regular NAV, but not be set (Intra-BSS NAV may be updated)
TXOP (Inter-BSS)
Sets Intra-BSS NAV
 Proper operation
Does not set regular NAV
 Undesirable operation
STA may transmit PPDU
Interference to Inter-BSS!
Resets Intra-BSS NAV
Inter-BSS Frame
Intra-BSS
* The frame includes HE-SIG-A and the frame is SU UL PPDU, MU PPDU which does not carry STAID that should be decoded by STA, or Trigger-based PPDU.
Cancelled

## Slide 9: Proposed Operations (1)
After STA detects BSS color collision, STA cannot identify the frame with the same BSS color value as Intra-BSS or Inter-BSS using BSS color.
In case that STA has detected BSS color collision,
  The STA should not perform operations (e.g., intra-PPDU power save or Intra-BSS NAV setting) based on the same BSS color
  Operation to different BSS color, such as applying OBSS PD level for channel access, can be permitted.
  Report/Resolution procedure may be required.
For Problem 1, after STA detects BSS color collision,
  The STA shall not enter the doze state during the frame using the same BSS color

## Slide 10: Proposed Operations (2)
For Problem 2a and 2b, after STA detects BSS color collision,
  The STA shall not update its Intra-BSS NAV based on TXOP Duration in HE-SIG-A. Also the STA can update its regular NAV based on TXOP Duration in HE-SIG-A.
    Case 1) The STA receives a PPDU with the different BSS color.
      Proper regular NAV is updated using TXOP Duration in HE-SIG-A
    Case 2) The STA receives a PPDU with the same BSS color.
      Case 2a) Decoding MAC is possible.
        E.g., SU PPDU / MU PPDU carrying STA’s AID or broadcast AID in HE-SIG-B
        Proper Intra-BSS NAV or regular NAV is updated using Duration in MAC header.
      Case 2b) Decoding MAC is not possible.
        E.g., MU PPDU not carrying STA’s AID and broadcast AID in HE-SIG-B / Trigger-based PPDU
        Only regular NAV is updated using TXOP Duration in HE-SIG-A.
   Regular NAV protects Inter-BSS transmissions.

## Slide 11: Proposed Operations (3)
Applying the solution in Slide 10, after STA detects BSS color collision,
  For Problem 2a,
Inter-BSS Frame*
Inter-BSS STA1
with same BSS color
Regular NAV
STA
Trigger Frame
Intra-BSS AP
Inter-BSS Frame
Inter-BSS STA2
with same BSS color
TXOP (Inter-BSS)
Inter-BSS
Intra-BSS
Inter-BSS frame sets regular NAV.
- STA does not determine that NAV was set by a frame originating from the AP sending the Trigger frame.
- STA can consider NAV in determining whether to respond.
* The frame includes HE-SIG-A and the frame is SU UL PPDU, MU PPDU which does not carry STAID that should be decoded by STA, or Trigger-based PPDU.

## Slide 12: Proposed Operations (4)
Applying the solution in Slide 10, after STA detects BSS color collision,
  For Problem 2b,
We also need that CF-End from Inter-BSS should not reset NAV if STA cannot determine whether NAV is set by Intra-BSS or Inter-BSS.
  For the case that STA sets regular NAV by Intra-BSS frame and receives CF-End from OBSS
  “When a STA receives a CF-End from an OBSS STA, if the last NAV update was caused by an Intra-BSS frame, the STA should not reset its NAV” [1].
Intra-BSS or regular NAV
STA
Intra-BSS DL Frame
Intra-BSS AP
CF-End
TXOP (Intra-BSS)
Inter-BSS Frame*
Inter-BSS STA
with same BSS color
Regular NAV
TXOP (Inter-BSS)
Sets Intra-BSS or regular NAV
(Regular NAV when MAC cannot be decoded)
Sets regular NAV
Resets only Intra-BSS NAV
Inter-BSS Frame
Intra-BSS
* The frame includes HE-SIG-A and the frame is SU UL PPDU, MU PPDU which does not carry STAID that should be decoded by STA, or Trigger-based PPDU.
- Although STA receives CF-End from Intra-BSS, regular NAV remains.

## Slide 13: Conclusions
BSS color collision is unavoidable with limited BSS color bit space and distributed BSS color assignment.
We propose that after BSS color collision is detected,
  STA shall not enter the doze state during the frame using the same BSS color.
  STA shall not update its Intra-BSS NAV based on TXOP Duration in HE-SIG-A.
  STA that receives a CF-End frame from Inter-BSS should not reset NAV set by a PPDU which cannot be identified as Intra- or Inter-BSS.

## Slide 14: References
[1] 11-15/0132r15 Specification Framework for TGax
[2] 11-15/1336r1 BSS Color Size Measurements

## Slide 15: Straw Poll 1
  Do you agree to add the following text into 11ax SFD ?
  6.3.z An HE non-AP STA that is in intra-PPDU power save mode shall not enter the doze state, if the detected frame cannot be identified as Intra-BSS or Inter-BSS.
  Y
  N
  A

## Slide 16: Straw Poll 2
  Do you agree to add the following text into 11ax SFD ?
  6.y.z A STA that receives a valid HE-SIG-A in a HE PPDU and cannot identify the frame as Intra-BSS or Inter-BSS shall not update its Intra-BSS NAV with the information from the TXOP Duration field in the HE-SIG-A.
  Y
  N
  A

## Slide 17: Straw Poll 3
  Do you agree to add the following text into 11ax SFD ?
  6.y.z An HE STA that receives a CF-End frame should not reset its NAV if the most recent NAV update was due to a PPDU which cannot be identified as Intra-BSS or Inter-BSS.
  Y
  N
  A

## Slide 18: Appendix: Detection of BSS Color Collision
BSS color collision may be detected by a STA in some methods.
  E.g., during normal packet reception procedure
    HE SU DL PPDU
    HE MU PPDU of which HE-SIG-B includes STAID with the same STAID or STAID of a broadcast STAID
L Preamble | RL-SIG | HE-SIG-A | … | MAC
1. SU PPDU
(1. Extended range SU PPDU)
2. DL / Same BSS color
 PPDU may be intended to the STA
* Receive procedure
3. Continues decoding
Can detect BSS color collision using Address in MAC header
L Preamble | RL-SIG | HE-SIG-A | HE-SIG-B | … | MAC
1. MU PPDU
2. Same BSS color
* Receive procedure
4. Continues decoding
Can detect BSS color collision using Address in MAC header
3. STAID indicates that PPDU is intended to the STA.