## Slide 1: Considerations on Trigger Frame for Random Access Procedure
Date: 2016-03-14
Authors:
Name | Affiliation | Address | Phone | Email
Evgeny Khorov | IITP RAS |  |  | khorov@frtk.ru
Anton Kiryanov | IITP RAS |  |  | kiryanov@iitp.ru
Sigurd Schelstraete | Quantenna |  |  | sigurd@quantenna.com
Huizhao Wang | Quantenna |  |  | hwang@quantenna.com

## Slide 2: Background
In [1] it was first proposed to define a Trigger frame that allocates resources for random access (TF-R).
In [2] UL OFDMA-based Random Access Procedure was proposed with some analytics.
But the existed procedure is not absolutely clear and many issues are open both in the spec framework [3] and in the standard draft [4].
In this presentation, we identify several open issues in UL OFDMA-based Random Access Procedure and try to clarify them.

## Slide 3: Random Access Procedure [3,4]
When a STA has a frame to send, it initializes its OBO (OFDMA Back-off) to a random value in the range 0 to OCW (OFDMA Contention window).
A STA decrements its OBO by the number of RUs assigned to AID value TBD in a TF-R unless OBO=0.
A STA with OBO decremented to 0 randomly selects any one of the assigned RUs for random access and transmits its frame.
OBO for any STA can only be 0 once every TF-R.
How a STA shall select the OCW value?

## Slide 4: OCWmax
An HE AP indicates the value of OCWmin for the random access operation. The method of indication of the OCWmin value is TBD. [4]
  It is naturally that at the very beginning an HE STA selects OCW=OCWmin.
  If the HE AP does not change OCWmin later, the protocol shall allow to resolve collisions, if any.
  To reduce contention in case of unsuccessful transmission attempt triggered by a Trigger frame for random access, OCW is doubled similar to CW in DCF until it reaches OCWmax. OCW is reset to OCWmin similarly to the DCF rules.
  The OCWmax value may be indicated by an HE AP similarly to the OCWmin value.
How an HE STA shall modify OCW value in case of collisions?

## Slide 5: Restarting Backoff
The method of indication of the OCWmin value is TBD.
Anyway, this value can be changed with time, since contention conditions change.
Shall an HE STA restart backoff when an HE AP indicates new OCWmin and OCWmax values?
If both values are the same as the previous ones, backoff shall not be restarted.
If the current OCW is in the range of new OCWmin and OCWmax, backoff shall not be restarted (case 1 is a subcase of case 2).
Otherwise, backoff shall be restarted and OCW shall be set to OCWmin.

## Slide 6: Indication of OCW
The method of indication of the OCWmin value is TBD [4].
Since contention conditions change, an HE AP can adaptively advertise OCWmin and OCWmax in Trigger frames for random access and may be in other frames (e.g. beacons).

## Slide 7: Straw Poll #1
Do you agree to add the following text in SFD:
  x.y.z. In case of unsuccessful transmission attempt triggered by a Trigger frame for random access, OFDMA Contention Window (OCW) is doubled (similar to CW in DCF) until it reaches OCWmax.
  Y
  N
  A

## Slide 8: Straw Poll #2
Do you agree to add the following text in SFD:
x.y.z. An HE AP indicates the values of OCWmin and OCWmaх for the UL random access operation. The method of indication of the OCWmin and OCWmax values is TBD.
  Y
  N
  A

## Slide 9: Straw Poll #3
Do you agree to add the following text in SFD:
x.y.z. An HE AP can indicate the values of OCWmin and OCWmaх in a Trigger frame for random access.
  Y
  N
  A

## Slide 10: Straw Poll #4
Do you agree to add the following text in SFD:
x.y.z. When an HE AP changes contention window parameters (OCWmin and OCWmax) for the UL random access operation, an HE STA
  shall not restart the OFDMA back-off and change OCW if the current OCW is in the range of new OCWmin and OCWmax,
  shall restart the OFDMA back-off and set OCW=OCWmin, otherwise.
  Y
  N
  A

## Slide 11: References
[1] IEEE 802.11-15/0604r1 “Random Access with Trigger Frames using OFDMA”
[2] IEEE 802.11-15/1105r0 “UL OFDMA-based Random Access Procedure”
[3] IEEE 802.11-15/132r15 “Specification Framework for TGax”
[4] IEEE 802.11-16/0024r1 “Proposed TGax draft specification”