## Slide 1: Short SSW Format for 11ay
Date: 2016-March-14
Authors:
Name | Company | Address | Phone | Email
Alecsander Eitan | Qualcomm |  |  | eitana@qti.qualcomm.com
Carlos Cordeiro | Intel |  |  | carlos.cordeiro@intel.com

## Slide 2: Preface
In mmWave path-loss is large and the main method to overcome it is by using high gain antennas. These are practical due to the very short wavelength.
Massive arrays provide excellent coverage while AP form factor has “infinite” footprint availability for these arrays.
Mobile form factor dictates small arrays.
In outdoor, massive arrays are expected.

## Slide 3: Motivation
The standard needs to support massive arrays.
Massive array achieves high gain with narrow beam which requires much more sectors to be used for training/access.
Example:
  Massive array with 256 antennas uses 256 sectors.
  Each sector is ~4 degrees wide.
  256 sectors require at least 4 ms for initial sector sweep.
SSW is a basic mandatory flow that is essential for reliable link.
We want to reduce the massive array SSW time by shortening the SSW duration.
We prefer changes which minimize impact to existing software and hardware.

## Slide 4: Existing Frames: Sector Sweep (SSW) Time Analysis
SSW frame is defined at 8.3.1.16 in 802.11ad.
Overall 26 bytes in each SSW frame.
Must be transmitted in CP in order to be received by the non-directed receiver.
 | Frame Control | Duration | RA | TA | SSW | SSW Feedback | FCS
Octets: | 2 | 2 | 6 | 6 | 3 | 3 | 4
SSW frame format(11ad) |  |  |  |  |  |  | 
 | B0 | B1 B9 | B10 B15 | B16 B17 | B18 B23
 | Direction | CDOWN | Sector ID | DMG Antenna ID | RXSS Length
Bits: | 1 | 9 | 6 | 2 | 6
SSW field format(11ad) |  |  |  |  | 

## Slide 5: Existing Frames: Sector Sweep (SSW) Time Analysis (cont.)
63% of the scan time is spent on transmissions of the 26 bytes SSW frames and the corresponding parity check bits.
31% of the scan time is spent on preambles + PHY headers.
6% of the scan time is spent on BIFSs.
  In case of multiple DMG antennas, the percentage is slightly higher due to LBIFS instead of SBIFS.
SSW duration is Nsectors*15.8us.
 |  | Samples | Time [us]
Preambles | 57 x G_128 | 7296 | 4.15
Header | 5 Bytes | 1280 | 0.73
Payload | 26 Bytes | 6656 | 3.78
Parity | 2 codewords | 10752 | 6.11
BIFS | 1 |  | 1.00
Total |  |  | 15.76
Nsectors | 32 | 64 | 128 | 256 | 512
SSW time [ms] | 0.5 | 1.0 | 2.0 | 4.0 | 8.1

## Slide 6: Existing Frames: Sector Sweep (SSW) Time Analysis (cont.)
When the AP is the initiator and an associated STA is the responder
  Several fields can be either compressed or removed
This is the most common scenario for the SSW.
Use of shorten SSW frame is optional (only when the two sides are supporting it).
Long time for massive array AP

## Slide 7: Requirements for Short SSW
An EDMG STA can transmit Short SSW packets to a peer STA only after, at a minimum, it discovers that the peer STA is also an EDMG STA
  Knowledge of MAC addresses and possibly STA capability required beforehand
  A MAC rule is required to this effect
The total number of bytes for the MAC payload of the Short SSW packet needs to stay <= 6 bytes
A legacy DMG STA shall be able to set CCA busy for the duration of the Short SSW packet by PLCP header detection
Initiator needs to be able to indicate to any recipient EDMG STA that the packet is a Short SSW packet
To keep it short, SLS using Short SSW packet uses DMG Control PHY and not EDMG Control PHY

## Slide 8: Short SSW format proposal
Field | Definition
Packet Type | Indicates the type of the packet. Possible values: 0: Short SSW, 1-3: Reserved
Addressing | The format is TBD.
CDOWN | A down-counter indicating the number of remaining Short SSW packet transmissions and LBIFSs to the end of the TXSS/RXSS across all antennas. This field is set to 0 in the last Short SSW packet transmission.
RF Chain ID | Identifies the RF chain the transmitter is currently using for this transmission.
Short SSW Feedback | In a RSS, contains the value of the CDOWN field of the Short SSW packet that was received with best quality in the immediately preceding sector sweep. The determination of which packet was received with best quality is implementation dependent. This field is reserved when transmitted as part of an ISS.
Direction | Indicates the direction of the transmission. The Direction field is set to 0 to indicate that the frame is transmitted by the beamforming initiator and set to 1 to indicate that the frame is transmitted by the beamforming responder.
FCS | The four MSBs of the FCS
 | Frame Control | Duration | RA | TA | SSW | SSW Feedback | FCS
Bits: | 16 | 16 | 48 | 48 | 24 | 24 | 32
 | Packet Type | Addressing | CDOWN | RF Chain ID | Short SSW Feedback | Direction | Reserved | FCS
Bits: | 2 | 16 | 11 | 2 | 11 | 1 | 1 | 4
26 octets
6 octets
11ad SSW frame
Proposed Short SSW packet

## Slide 9: Details of proposed format
Short SSW is a PHY packet (similar to 11n/ac NDP), not a MAC frame
For this format, the Length field in the PLCP Header is set to 6. Therefore:
  A legacy DMG STA drops the packet since this is an invalid length, and keeps CCA busy until the end of packet
  A third party EDMG STA computes the ISS/RSS duration through the CDOWN field and sets the NAV for this duration
Packet Type field allows for future packets to be defined and that use the same approach
Short SSW Feedback field allows using the Short SSW for ISS and RSS
Support of up to 2048 sectors
Hash function for Addressing field is TBD.
Short SSW duration is 9.6usec (including the BIFS) (saves 37.8%)
For EDMG STAs, define LBIFS as equal to: 2*TXTIME(Short SSW)+2*SBIFS

## Slide 10: Summary
The standard needs to support massive arrays with many sectors. The SLS overall duration scales with the number of sectors.
We suggest to reduce the SLS duration by shortening the SSW duration.
We suggest to add a Short SSW Format to 11ay to be used EDMG STAs reducing the transmission duration to 9.8usec (37.8% saving)
Suggested format supports ISS and RSS up to 2048 sectors
We also suggest to set the LBIFS to be same as duration of two Short-SSW and keep the counting CDOWN during this period.

## Slide 11: Motion
Insert the following in section 7 of the SFD: “
7.6 EDMG Beamforming
The format of the Short SSW packet is defined in <slide 8>. ”
SP: 28/0/8
Insert the following in section 4.2 of the SFD: “
An EDMG STA shall not transmit a Short SSW packet to another STA that is not also an EDMG STA.
For SLS using Short SSW frames, LBIFS is equal to 2*TXTIME(Short SSW) + 3*SBIFS. An EDMG STA performing an SLS using Short SSW frames shall increase the value of the CDOWN field within the Short SSW frame by two for each LBIFS contained as part of a sector sweep.”
SP: 25/0/7