## Slide 1: BF Training for SU MIMO
Date: 2016-03-14
Authors:

## Slide 2: Background
Many BF features were agreed in 11ay SFD:
  The 11ay SLS beamforming protocol shall enable feedback of one or more sectors per TX and RX antenna.
  The 11ay beamforming protocol shall enable TX and RX training using the same BRP frame.
  The 11ay beamforming protocol shall enable simultaneous BF training of transmit DMG antennas.
  The 11ay beamforming protocol shall support simultaneous RX antenna training.
  The 11ay beamforming protocol shall provide means to enable TX sector down selection as part of beamforming training.
  etc.
  Based on these BF features, this contribution intends to address the flow of BF for SU MIMO.

## Slide 3: BF Flow for SU-MIMO
  Assumption: Control PHY connection established between Initiator and Responder.
  BF for SU MIMO can be performed in the following phases:
  SLS: Coarse BF training to allow TX sector down selection for Initiator and Responder
    Can be skipped if the previous I-TXSS and R-TXSS are still valid.
  Setup (TBD): Message exchange between Initiator and Responder for specifying how the TX-RX sector/antenna mapping phase is performed.
  TX-RX sector/antenna mapping (name: TBD): BF training of RX sectors/antennas/RF chains for each of the candidate TX sectors to determine best TX-RX configuration for SU MIMO.

## Slide 4: SLS
I-TXSS to allow TX sector down selection for Initiator by collecting feedback of multiple TX sectors from Responder.
    Each TX antenna should have the same number of selected sectors. The intention is to avoid the case that the candidate sectors bias a TX antenna.
R-TXSS to allow TX sector down selection for Responder by collecting multiple TX sector feedback from Initiator.
  If Responder has antenna pattern reciprocity, RX sector down selection for Initiator can be performed in the same manner as TX sector down selection for Responder.
  Should be used only when the number of TX sector/RX sector pairing is large.
Feedback candidate sectors per TX antenna for Responder,
Setup for TX-RX mapping phase
Allow TX sector sweep using a single BRP frame;
Feedback candidate sectors per TX antenna for initiator
Allow TX sector sweep using a single BRP frame

## Slide 5: Setup
  What possibly can be done during Setup:
  Perform TX sector down selection based on the previous I-TXSS and R-TXSS if necessary. For example,
    SLS phase is skipped and the previous I-TXSS and R-TXSS do not include feedback of multiple candidate sectors.
    may be included into the TX-RX sector/antenna mapping phase
  Determine whether TX-RX sector/antenna mapping is performed for Responder link besides for Initiator link.
    may be performed during SLS phase
  Determine whether TX or RX makes TX/RX sector/antenna mapping decision based on the TX/RX capability
    may be performed via capability exchange during association
  etc.
Our preference is to eliminate or reduce the amount of negotiation between Initiator and Responder per BF Training to simplify the BF training flow.

## Slide 6: TX-RX Sector/Antenna Mapping
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms
Selected TX sectors/antennas for Initiator
Example 1: Initiator link only where RX makes mapping decision

## Slide 7: TX-RX Sector/Antenna Mapping
CSI Feedback for Initiator link
Selected RX sectors/antennas for Initiator
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms
Example 2: Initiator link only where TX makes mapping decision

## Slide 8: TX-RX Sector/Antenna Mapping
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms
Selected TX sectors/antennas for Initiator
Selected TX sectors/antennas for Responder
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms
Example 3: Both links where RX makes mapping decision for both links

## Slide 9: TX-RX Sector/Antenna Mapping
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms
CSI feedback for Initiator link
Selected RX sectors/antennas for Responder
CSI feedback for Responder link
Selected RX sectors/antennas for Initiator
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms
Example 4: Both links where TX makes mapping decision for both links

## Slide 10: TX-RX Sector/Antenna Mapping
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms
Selected TX sectors/antennas for Initiator
Selected RX sectors/antennas for Initiator
CSI feedback for Responder link
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms
Example 5: Both links where RX makes mapping decision for Initiator link and TX makes mapping decision for Responder link

## Slide 11: TX-RX Sector/Antenna Mapping
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms
Allow TX sector sweep and RX sector sweep using a single BRP frame
Multiple TX antennas can transmit simultaneously using orthogonal waveforms
CSI feedback for Initiator link
Selected RX sectors/antennas for Responder
Selected TX sectors/antennas for Responder
Example 6: both links where TX makes mapping decision for Initiator link and RX makes mapping decision for Responder link

## Slide 12
Straw Poll
Do you agree to insert the following text into 11ay SFD?
  BF for SU MIMO comprises the following phases:
    SLS: Coarse BF training to allow TX sector down selection for Initiator and Responder including feedback with candidate sectors.
    TX-RX Sector/Antenna Mapping (name: TBD): BF training of RX sectors/antennas/RF chains for each of the candidate TX sectors to determine best TX-RX configuration for SU MIMO.
    others: TBD
  Yes:
  No:
  Abstain: