## Slide 1: Discussion on LTE-WLAN Aggregation (LWA) and LTE WLAN Radio Level Integration with IPsec tunnel (LWIP)
Date: 2016-01-19
Authors:

## Slide 2: Agenda
This contribution highlights some important points of comparison between the two 3GPP technologies LAA and LWIP introduced in [1]
  Including the possibility for LAA and LWIP to reuse IEEE 802.11 technologies such as authentication and metrics for selection and traffic steering
An updated comparison summary is proposed, together with a proposal for LS response to 3GPP

## Slide 3: LWA vs LWIP per [1]
 | eNB control | WLAN measurements | Offload granularity | WLAN traffic direction | Feedback/flow control | Fast WLAN authentication | WLAN infrastructure impact | New network nodes
LWA | Yes | Yes | Split bearer | DL only | Yes | Yes2 | Yes4 | WT
LWIP | Yes | Yes | Bearer1 | DL + UL | No | No3 | No | LWIP-SeGW
When a bearer is configured to use IPsec, LTE DRB configuration remains, however eNB is not expected to send packets on LTE and IPsec simultaneously, as LWIP does not support re-ordering
After connecting to WLAN, LWA UE only performs 4-way handshake (if network uses the eNB based authentication)
After connecting to WLAN, LWIP UE performs WLAN native 802.1x EAP/AKA authentication, IP address acquisition and IPsec tunnel establishment
Impact due to eNB based authentication mechanism, if used by network. Optional UE feedback mechanisms (as opposed to network feedback) allow to limit WLAN infrastructure impact of LWA
The following table was presented in [1] as a comparison between LWA and LWIP:

## Slide 4: Comments and analysis
Bearer split performance and implementation issues
  LWA’s PDCP processing of every packet on WLAN access introduces unnecessary complexities – power consumption, I/O and memory bandwidth, and CPU cycles
    Will continue to become more serious as data rates increase
  LWIP addresses the same bearer split use cases with simpler implementation
    Aggregation of a DRB over LTE and WLAN radios can be implemented without “per packet” granularity, and therefore without the need for a reorder buffer, using similar techniques used in LTE-WLAN interworking (e.g. make traffic steering decision for each short-term IP flow)
WLAN authentication
  The LWA authentication mechanism introduces new complexities in the security key distribution and management over WLAN, as well as limitations (inability to prioritize QoS based on user profile, no authentication to other WLAN services)
  LWIP supports the ability to use IEEE 802.11 technologies for fast authentication
WLAN selection and traffic steering metrics
  Metrics for WLAN selection and traffic steering in both LWA and LWIP have limitations as documented in previous liaison from IEEE 802.11 to 3GPP
  IEEE 802.11 REVmc now incorporates enhanced metrics (D4.3, 10.46 Estimated Throughput) which would enable improved performance of both technologies

## Slide 5: Proposed LWA vs LWIP summary
 | eNB control | WLAN measurements | Offload granularity | WLAN access | Feedback/flow control | Fast WLAN authentication | WLAN infrastructure impact | New network nodes
LWA | Yes | Yes | Split bearer | DL only | Yes | Yes2 | Yes4 | WT
LWIP | Yes | Yes | Split bearer1 | DL + UL, full user profile based access5 | No | Yes3 | No | LWIP-SeGW
When a bearer is configured to use IPsec, LTE DRB configuration remains. LWIP split bearer can be implemented in both DL and UL without the need for a reorder buffer.
After connecting to WLAN, LWA UE only performs 4-way handshake (if network uses the eNB based authentication). Note this mechanism requires support for:
  - New WLAN security key distribution and management mechanism
  - New Ethernet frame transport
  - Network based flow control to be implemented in the WLAN Gateway. Optional UE feedback mechanisms (as opposed to network feedback) allow to limit impact of LWA on WT
After connecting to WLAN, LWIP UE performs 802.1x EAP/AKA authentication, IP address acquisition and IPsec tunnel establishment. LWIP can therefore make use of 802.11-based fast authentication (e.g. 11ai FILS) and fast roaming (e.g. 11r Fast Transition) mechanisms.
Impact due to eNB based authentication mechanism, if used by network. Optional UE feedback mechanisms (as opposed to network feedback) allow to limit WLAN infrastructure impact of LWA
LWIP authentication provides full DL + UL access on WLAN, including ability to support user profile based QoS

## Slide 6: Proposed next steps
We propose IEEE 802 send an LS response to 3GPP requesting 3GPP consider the following items for Rel. 14:
  Simplified transport over WLAN, similar to that used for other LTE-WLAN interworking scenarios e.g. “trusted access”
  LWA authentication based on AAA server, already well supported in WLAN deployments (e.g. HS2.0)
  IEEE 802.11 Estimated Throughput as a WLAN metric reported by the terminal to the eNB.

## Slide 7: References
[1] 11-16/351r1 “Liaison from 3GPP on LWA and LWIP”, Richard Burbidge
[2] 11-14/936r3 “Followup liaison response to 3GPP R2-141855”, Youhan Kim et al