## Slide 1: ESP Element ID Request
Date: 2016-03-14
Authors:

## Slide 2: Abstract
Need ANA assignment for new IE created for Estimated Service Parameters Information element

## Slide 3: Background of the IE
ESP IE and ESP behavior approved as part of REVmc process
  I.e. currently part of baseline draft REVmc D5.0
ESP IE contains per AC information:
  Estimated available airtime fraction for next STA to join
  Expected aggregation use by transmitting STA
  BA Window size of transmitting STA
  Target PPDU duration of transmitting STA

## Slide 4: Where is the ESP IE?
Element usage by ESP STAs:
  Sent by ESP AP in all Beacons to allow passive throughput estimation
  Sent by ESP AP in Probe Responses when requested in Probe Request
  Optionally sent by ESP AP in Probe Responses when not requested in Probe Request
  Optionally sent by non-AP ESP STA in Probe Request

## Slide 5: Use of ESP Information by non-AP STA
  non-AP ESP STA either associated with responding ESP AP or not yet associated with the responding ESP AP
  non-AP ESP STA uses information to estimate throughput if association is established with responding ESP AP
    Beacon-based ESP IE always present from ESP AP
    Beacon-based ESP IE indicates estimated airtime fraction of next non-AP STA to join the BSS
      Potential BSS member STA can estimate DL throughput based on AP indicated aggregation, BA window and PPDU duration parameters plus airtime and an MCS estimate based on link SINR
      Potential BSS member STA can estimate UL throughput based on AP indicated aggregation airtime fraction and self-determined aggregation, BA window and PPDU duration and an MCS estimate based on link SINR

## Slide 6: Traditional vs Extended ID
Element ID values
  About 48 remaining
Extended Element ID values
  ~240 remaining
Presence of ESP IE in all Beacons sent by ESP AP suggests shorter duration of IE
  To minimize Beacon overhead
  Hence, traditional IE ID preferred

## Slide 7: Motion
Move to instruct ANA to assign an element ID for use by the Estimated Service Parameter Information element