## Slide 1: Functional requirements for 802.11az
Date: 2016-05-11
Authors:

## Slide 2: Measurement Requirements (2.1.1)
Append the following text as an additional requirement to the end of section 2.1.1:
The 802.11az protocol shall support at least one mode of operation that enables AoA/AoD measurements in the 2.4GHz and 5GHz bands, alone or in conjunction with range measurements.

## Slide 3: Requirements for Scalability (2.1.3)
Replace section 2.1.3 R18 as follows:
Current text: Support at least 200 unassociated and associated STAs, per AP performing locationing operation concurrently.
Proposed text: Support locating and tracking all associated and at least 200 unassociated STAs per AP concurrently
Replace section 2.1.3 R20 as follows:
Current text: Utilize less than 10% of the channel capacity of an AP
Proposed text: Support configuration of the network to modify performance parameters such as the frequency and number of STAs tracked to achieve network resource usage over a range from less than 5% or to greater than 50% in cases were a dedicated AP is present.

## Slide 4: Requirements for Scalability (2.1.3) cont.
Replace section 2.1.3 R21 as follows:
Current text: Operate with a maximum refresh rate of .5Hz.
Proposed text: Operate with tracking refresh rates ranging from 0.1 to 0.5Hz with higher refresh rates available in APs dedicated to providing location.
Append the following text as additional requirements to the end of section 2.1.3:
Determining initial STA location within (TBD, but not greater than 10s) in APs dedicated to providing location
Support continuous tracking of STAs with a latency of <= 500ms

## Slide 5: Motion
Motion
To adopt the functional requirements listed in slides 2 through 4 of submission 11-16/0579r2 and include them in the TGaz Functional Requirements Document 11-16/0424
  Moved: Kare Agardh
  Seconded: Ganesh
  Result: 5-0-4

## Slide 6: References
[1] https://mentor.ieee.org/802.11/dcn/16/11-16-0137-04-00az-ngp-use-case-document.pptx
[2] Functional requirements for scalability operation 11-16-0134-03-00az-accuracy-and-coverage-functional-requirements
[3] https://mentor.ieee.org/802.11/dcn/16/11-16-0424-01-00az-proposed-802-11az-functional-requirements.docx
[4] https://mentor.ieee.org/802.11/dcn/16/11-16-0315-02-00az-smart-buildings-use-cases.ppt
[5] https://mentor,ieee.org/802.1+/dcn/16/11-16-595-00-00az-proposed-functional-requirements-for-network-based-positioning.pptx