## Slide 1
Channel State Estimation based Bidirectional Initialized Random Access
Date: 2016-05-12
Authors:
Name | Affiliation | Address | Phone | Email
Bo Li | Northwestern Polytechnical University | 127 West Youyi Road, Xi’an Shaanxi,710072, P.R.China | +86-18192187626 | libo.npu@nwpu.edu.cn
Mao Yang |  |  |  | yangmao@nwpu.edu.cn
Zhongjiang Yan |  |  |  | zhjyan@nwpu.edu.cn
Xiaoya Zuo |  |  |  | zuoxy@nwpu.edu.cn
Run Zhou |  |  |  | zhourun_xsy@163.com

## Slide 2: Background
In the current 802.11 WLAN, it is always the sender node that initializes the transmission through CSMA/CA.
BUT, the channel state, e.g. idle or busy, detected by the sender can hardly precisely reflects the real-time channel state of the receiver. This results in low transmission reliability.
  e.g. the sender believes that the channel is idle and transmits data after backoff but, actually, the receiver is now experiencing severe interference.

## Slide 3: Motivation
To improve the transmission reliability, two possible methods:
  the sender is able to estimate the receiver’s channel state
  the receiver can initialize the transmission rather than just the sender does it.

## Slide 4: Channel State Estimation based Random Access
The sender maintains the average interference difference △Isd between the sender and the receiver through the historic transmission.
  The sender and the receiver can exchange their average interference information during RTS/CTS.
During the sender’s backoff period, the sender detects the RSSI, and estimates the interference at the receiver Ide = RSSI - △Isd.
  If Ide > CCA, backoff suspend
  If Ide < CCA, backoff counter decreases by 1 and backoff continues
The sender sends Data or RTS when the backkoff period completes.

## Slide 5: Bidirectional Initialized Random Access
Step 1: At the end of the TXOP initialized by the sender, if the sender still has large enough data to send, it fills one bit Rq in the last data frame to ask the receiver to directly initialize the following TXOP from the sender to the receiver.
Step 2: If the receiver receives the last data frame with Rq, it responds with ACK with one bit named Rs filling in.

## Slide 6: Bidirectional Initialized Random Access
Step 3: the receiver runs backoff period according to itself’s channel state.
Step 4: if the receive finishes its backoff period, it directly sends CTS to the sender to initialize the transmission.

## Slide 7: Conclusion
In this presentation, in order to improve the transmission reliability, we introduce channel state estimation and bidirectional initialized, i.e. both the sender and the receiver, based random access.