## Slide 1
Fractional-Backoff Procedure and Dynamic CCA
Date: 2016-05-12
Authors:
Name | Affiliation | Address | Phone | Email
Bo Li | Northwestern Polytechnical University | 127 West Youyi Road, Xi’an Shaanxi,710072, P.R.China | +86-18192187626 | libo.npu@nwpu.edu.cn
Mao Yang |  |  |  | yangmao@nwpu.edu.cn
Zhongjiang Yan |  |  |  | zhjyan@nwpu.edu.cn
Xiaoya Zuo |  |  |  | zuoxy@nwpu.edu.cn
Bo Yang |  |  |  | yangboo@mail.nwpu.edu.cn

## Slide 2: Rethink the Current Backoff Procedure
In the current backoff procedure, the per-slot decreased value of backoff counter is bivariate, either 1 or 0.
The throughput of bivariate backoff is deeply affected by the CCA level.
  Higher CCA level: collision increase
  Lower CCA level: spatial reuse suppressed
Therefore, to improve area throughput, the backoff procedure and the CCA method needs to be jointly considered.
Per-slot Decreased Value | Channel Status | Action
1 | idle | backoff continue
0 | busy | backoff suspend

## Slide 3: Motivation
The station who offers more contributions to the area throughput should adopt faster backoff.
The station who offers less contributions to the area throughput should adopt slower backoff.
The fractional-backoff procedure needs to be introduced.
To be consistent with the precise fractional-backoff procedure, CCA level needs to extend from one fixed point to a range [-∞, CCAth].

## Slide 4: Fractional-Backoff Procedure
Step 1: During every time slot, the sender S detects the RSSI (dB).
  If RSSI > CCAth, the backoff procedure suspends.
  If RSSI < CCAth, execute the fractional-backoff procedure, goto Step 2.
Step 2: S estimates the SINR (dB) at the receiver D.
  where Pr0 (dB) indicates the receive power of the CTS or ACK during the last transmission of SD.

## Slide 5: Fractional-Backoff Procedure
Step 3: S determines transmitting rate R based on the RATE-SINR mapping. Then, S calculates the its area throughput.
  where Ss,d is the area covered by S or D.

## Slide 6: Fractional-Backoff Procedure
Step 4: S determines the decreased value of the current time slot.
  where Rarea is the area throughput contributed by S. R0 is the equivalent maximum area throughput where S overlaps D. BOMAX is the maximum decreased value, e.g. 2.0.

## Slide 7: Fractional-Backoff Procedure
Step 5: When the backoff counter is deceased to be or less than 0, S finishes the backoff period and accesses the network.

## Slide 8: Simulation Results
Parameter | Value
BSS size | 50m*50m
STA Num | 5 up 5 down
Traffic | Full buffer video
Simulation | 5s
CCAth | -62dbm
BOMAX | 1.0
Chart: 
| 1 | 2 | 4 | 8 | 10
小数退避 | 95.93 | 109.382 | 177.204 | 296.351 | 427.791
基线版本 | 108.8 | 107.54 | 111.505 | 181.961 | 247.645
BSS number
Network Throughput
Fractional-Backoff Procedure
Legacy Backoff Procedure

## Slide 9: Conclusion
In this contribution, we rethink the backoff procedure of legacy IEEE 802.11, and analyze its performance limitation.
In order to increase the area throughput, we jointly propose a fractional-backoff procedure and dynamic CCA method. Based on this procedure, the per-slot decreased value of backoff counter is determined by the contributions for the area throughput.