## Slide 1
Multi-BSS Association for Edge Users’ Throughput Improvements
Date: 2016-05-12
Authors:
Name | Affiliation | Address | Phone | Email
Mao Yang | Northwestern Polytechnical University | 127 West Youyi Road, Xi’an Shaanxi,710072, P.R.China | +86-18629531351 | yangmao@nwpu.edu.cn
Bo Li |  |  |  | libo.npu@nwpu.edu.cn
Zhongjiang Yan |  |  |  | zhjyan@nwpu.edu.cn
Xiaoya Zuo |  |  |  | zuoxy@nwpu.edu.cn
Li Ji |  |  |  | 471641625@qq.com

## Slide 2: Background & Motivation
To improve the edge users’ throughput is an important objective of IEEE WLAN, which directly affects quality of services and area throughput.
The next generation WLAN has to face high dense deployment scenario. Therefore, edge users may probably hear signals from multiple BSSs.
  Edge users experience severe interference
  Why not allow them to transmit data through multiple BSSs?

## Slide 3: Multi-BSS Association
Step 1: edge STA sends Multi-BSS Association Initiation frame (MA-INIT) to neighbor BSSs (secondary APs).
  Multiple BSSs may work in different channels.
Step 2: secondary APs respond edge STA with ACK or NAK.

## Slide 4: Multi-BSS Association
Step 3: edge STA sends Multi-BSS report frame (MA-Rpt) to the primary AP to feedback the multi-BSS results.
Step 4: primary AP responds edge STA with ACK.

## Slide 5: Parallel Backoff
Step 5: edge STA runs backoff procedures in multiple BSSs simultaneously, and accesses the BSS (channel) in which the backoff counter is first decreased to 0.
Step 6: edge STA transmits data through the selected BSS.

## Slide 6: Conclusion
In this contribution, we propose a multi-BSS association scheme for edge users’ throughput improvements. The edge user initializes the multi-BSS handshakes and then runs backoff procedures in multiple BSSs simultaneously.
Multi-BSS association benefit the edge users’ throughput and QoS.