## Slide 1: Simulation-based evaluation of DSC in enterprise scenario 11-16-0604-00-00ax
Date: 2016-May
Authors:

## Slide 2: Outline
Context
DSC: The big picture
Scenarios and assumptions
Metrics used for evaluation
Four 80 MHz Channels
Nine 40 MHz Channels
Conclusions/next steps
References
Appendix

## Slide 3: 1. Context
Spatial reuse in the SFD
  The amendment shall include one or more mechanisms to improve spatial reuse by allowing adjustments to one or more of the CCA-ED, 802.11 Signal Detect CCA, OBSS_PD or TXPWR threshold values. The constraints on selecting threshold values are TBD”
  DSC could be used to select these threshold values
DSC: Dynamic Sensitivity Control
  DSC widely studied in TGax WG: DSC increases per-user throughput in dense scenarios [1-12] but what about fairness? More than 20 contributions about DSC since July 2013 and only [12] studies fairness
  DSC text for SFD has been proposed in [13] but DSC has still not been studied for some of the simulation scenario proposed in [14]
In this submission we,
  investigate the performance of DSC in enterprise scenario and recommend DSC parameters to use
  Highlight the importance of fairness study while analyzing mechanisms supposed to increase spatial reuse
May 2016

## Slide 4: 2. DSC: The big picture
DSC varies CST levels for each station
  Based on beacons RSSI: R
  Stations close to the AP have a higher CST
  Use of a margin M: CST = R – M
    Help to take into account sudden
    change in beacon signals
  DSC decreases number of exposed nodes but increases hidden nodes
May 2016
CST STA1 = R
CST STA2 = R
STA2
STA1
CST STA1 = R
CST STA2 = R
STA2
STA1
CST STA1 = R-M
CST STA2 = R-M
AP
AP

## Slide 5: 3. Scenarios and assumptions (1/3)
Topology
  Single floor office building,
    8 offices
    64 cubicles per office
    Each cubicle has 4 STAs so 8*64*4 = 2048 STAs
8 offices
1 Office = 64 cubicles
1 Cubicle = 4 STAs
May 2016

## Slide 6: 3. Scenarios and assumptions (2/3)
Channel allocation: 5GHz (based on [15])
  Four 80MHz channels (Ch1 to Ch4)
  Nine 40Mhz channels (Ch1 to Ch9)
Four 80MHz channels
Nine 40MHz channels
May 2016
AP
Channel
1
2
3
4
5
6
7
8
9

## Slide 7: 3. Scenarios and assumptions (3/3)
May 2016
Parameters | Values
Traffic type | UDP CBR uplink transmissions in saturation conditions
MPDU size | 1538 Bytes (from SSD) (1544 Bytes in total incl. all overhead)
Aggregation | Aggregation: 32 MPDUs with 4-byte MPDU delimiter per A-MPDU No A-MSDU Implicit immediate BA
PPDU of Data frame | VHT PPDU (MCS 5, fixed)
Guard Interval | Short
CCA Threshold | -76 for 80MHz -79 for 40MHz
Simulator | ns-3

## Slide 8: 4. Metrics used for evaluation
Aggregated throughput i.e. sum of UDP throughputs observed at AP level
Fairness (Jain’s index [16])
  Measure per STA throughput fairness i.e. a Jain’s fairness index of 1 means an equal portioning of throughput among STA
  Jain’s fairness has to be studied conjointly with the aggregated throughput
Goodput Ratio
  An illustration of fairness: Goodput Ratio GR
  STA Goodput Ratio: GRi = #APUDPReceivedi / #STAUDPSenti
May 2016
Chart: Aggregated Throughput
| Legacy CCA | DSC
 | 150 | 300
Aggregated Throughput is a good indicator but should not be the only one: what if the throughput gain is obtained only for few nodes at the expense of numberous others? Fairness is needed
Is case 1 really better than case 2?
Case 1: Jain’s index = 0.75
Case 2: Jain’s index = 0.70
75
0
75
75
20
10
50
75

## Slide 9: 5. Four 80MHz channels (1/4)
Observations:
  Margin highly affects DSC behavior
  DSC may allow to increase aggregated throughput compared to Legacy CCA threshold (up to 80%)
  A DSC margin of 25dBm is giving the best results of all the CST tested for aggregated throughput
Conclusions:
  Margin is a crucial parameter for the DSC as an incorrect margin parametrization could result in negative gain (the smaller is the margin, the higher is the CST and thus number of exposed STA)
May 2016
Aggregated Throughput
*
* 80MHz: Legacy CCA threshold = -76dBm
Chart: Aggregated Throughput
| Legacy CCA | DSC (m=5) | DSC(m=10) | DSC (m=15) | DSC (m=20) | DSC (m=25) | DSC (m=30) | DSC (m=35) | DSC (m=40)
 | 2120 | 1313.012 | 2321.04 | 3467.56 | 3644.04 | 3813.68 | 2837.44 | 2322.6 | 2072.132
Chart: % of throughput increase regarding to Legacy CCA threshold
| DSC (m=5) | DSC(m=10) | DSC (m=15) | DSC (m=20) | DSC (m=25) | DSC (m=30) | DSC (m=35) | DSC (m=40)
 | -0.38065 | 0.09483 | 0.63564 | 0.71889 | 0.79891 | 0.33842 | 0.095566 | -0.022579

## Slide 10: 5. Four 80MHz channels (2/4)
Observations:
  DSC is not always increasing the fairness compared to Legacy CCA threshold ([12] observed the opposite for the residential scenario case whatever the tested margin)
  A DSC margin of 25 seems the best compromise (same fairness than Legacy and 80% of aggregated throughput increase)
Conclusions:
  DSC can increase fairness and aggregated throughput at the same time
  Is Jain’s fairness representing everything?
May 2016
Fairness: Jain’s Fairness Index
Chart: Jain's fairness index
| Legacy CCA | DSC (m=5) | DSC(m=10) | DSC (m=15) | DSC (m=20) | DSC (m=25) | DSC (m=30) | DSC (m=35) | DSC (m=40)
 | 0.75 | 0.42 | 0.6 | 0.88 | 0.91 | 0.75 | 0.6 | 0.64 | 0.75
Chart: % of Jain's fairness index increase and associated % of throughput increase
| DSC (m=5) | DSC(m=10) | DSC (m=15) | DSC (m=20) | DSC (m=25) | DSC (m=30) | DSC (m=35) | DSC (m=40)
% of throughput increase | -0.38065 | 0.09483 | 0.63564 | 0.71889 | 0.79891 | 0.33842 | 0.095566 | -0.022579
% of Jain's fairness increase | -0.44 | -0.2 | 0.17333 | 0.21333 | 0 | -0.2 | -0.14667 | 0

## Slide 11: 5. Four 80MHz channels (3/4)
Observations:
  Legacy CCA threshold: at least a ratio of 0.10 for each STA
  DSC: a non-insignificant percentage of STAs has a ratio close to 0
  For Legacy STA, the closest STA has a low goodput ratio while it’s the opposite for DSC with a margin of 25
Conclusions:
  Some STAs are almost unable to transmit when using DSC in enterprise scenario with a margin of 25
  DSC could worsen the situation even if aggregated throughput is increased
  Jain’s fairness does not represent completely the fairness as CCA Legacy fairness is the same than DSC m=25
Goodput ratio GR: STA Goodput Ratio: GRi = #APUDPReceivedi / #STAUDPSenti
-76dBm (One channel)
DSC with m=25 (One channel)
May 2016

## Slide 12: 5. Four 80MHz channels (4/4)
Observations:
  Legacy CCA: No STA has a goodput ratio less than 0.10
  DSC m=20 (best Jain Fairness): 45% of STA has a goodput ratio of 0.7
  DSC m=25: 12% of STAs has a goodput ratio less than 0.1
Conclusions:
  DSC must be studied regarding both to fairness and goodput, not only for aggregated throughput
  A DSC margin of 20dB is recommended for the four 80MHz scenario
Probability Density Function of goodput Ratio
May 2016
Chart: PDF of goodput ratio
| 0.1 | 0.2 | 0.30000000000000004 | 0.4 | 0.5 | 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989
Legacy | 0.0019493 | 0.24172 | 0.30409 | 0.20273 | 0.1306 | 0.046784 | 0.048733 | 0.019493 | 0.0038986 | 0
m=20 | 0.031189 | 0.02924 | 0.015595 | 0.05653 | 0.10916 | 0.27096 | 0.47173 | 0.015595 | 0 | 0
m=25 | 0.13255 | 0.05848 | 0.052632 | 0.068226 | 0.089669 | 0.076023 | 0.08577 | 0.10136 | 0.11501 | 0.22027
DSC with m=20 (One channel)

## Slide 13: 6. Nine 40MHz channel (1/3)
May 2016
Observations:
  Same behavior than for four 80Mhz Channel: Margin highly influences throughput
  A DSC margin of -35dBm is giving the best results of all the tested margins for aggregated throughput
Aggregated throughput
Chart: Aggregated Throughput
| Legacy CCA | DSC (m=5) | DSC(m=10) | DSC (m=15) | DSC (m=20) | DSC (m=25) | DSC (m=30) | DSC (m=35) | DSC (m=40)
 | 1461.3333 | 576.2133 | 1143.7333 | 1740.9067 | 1820.9067 | 1816.96 | 1896 | 2134.56 | 1715.52
Chart: % of throughput increase regarding to Legacy CCA threshold
| DSC (m=5) | DSC(m=10) | DSC (m=15) | DSC (m=20) | DSC (m=25) | DSC (m=30) | DSC (m=35) | DSC (m=40)
 | -0.60569 | -0.21734 | 0.19131 | 0.24606 | 0.24336 | 0.29745 | 0.46069 | 0.17394
* 40MHz: Legacy CCA threshold = -79dBm
*

## Slide 14: 6. Nine 40MHz channel (2/3)
May 2016
Observations:
  DSC could increase fairness compared to CCA Legacy Threshold
  Even if DSC with 35 margin is giving the best aggregated throughput, it does not seem to be the best candidate regarding to Jain’s fairness (m=25 seems to be as it increase both fairness and throughput)
Fairness: Jain’s Fairness Index
Chart: Jain Fairness
| Legacy CCA | DSC (m=5) | DSC(m=10) | DSC (m=15) | DSC (m=20) | DSC (m=25) | DSC (m=30) | DSC (m=35) | DSC (m=40)
 | 0.55 | 0.43 | 0.54 | 0.82 | 0.79 | 0.85 | 0.79 | 0.48 | 0.5
Chart: % of Jain's fairness index increase and associated % of throughput increase
| DSC (m=5) | DSC(m=10) | DSC (m=15) | DSC (m=20) | DSC (m=25) | DSC (m=30) | DSC (m=35) | DSC (m=40)
% of throughput increase | -0.60569 | -0.21734 | 0.19131 | 0.24606 | 0.24336 | 0.29745 | 0.46069 | 0.17394
% of Jain's index increase | -0.21818 | -0.018182 | 0.49091 | 0.43636 | 0.54545 | 0.43636 | -0.12727 | -0.090909

## Slide 15: 6. Nine 40MHz channels (3/3)
Observations:
  Legacy CCA: 23% of STAs has a goodput ratio less than 0.10
  DSC m=25 (best Jain Fairness): 65% of STA has a goodput ratio of 0.3. No STA has a ratio less than 0.1
  DSC m=35: 40% of STAs has a goodput ratio less than 0.1
Conclusions:
  DSC must be studied regarding to fairness and goodput, not only for aggregated throughput
  A DSC margin of 25dB is recommended for the nine 40MHz scenario
Probability Density Function of goodput Ratio
May 2016
Chart: PDF of goodput ratio
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Legacy CCA | 0.23797 | 0.37143 | 0.16104 | 0.075325 | 0.051948 | 0.038961 | 0.031169 | 0.0077922 | 0.01039 | 0.0077922
DSC m=25 | 0 | 0.051948 | 0.65455 | 0.28831 | 0.0051948 | 0 | 0 | 0 | 0 | 0
DSC m=35 | 0.40759 | 0.067532 | 0.075325 | 0.11688 | 0.05974 | 0.051948 | 0.046753 | 0.015584 | 0.031169 | 0.11688

## Slide 16: 7. Conclusions/next steps
  As stated in the SFD, “include one or more mechanisms to improve spatial reuse by allowing adjustments to one or more of the CCA-ED, 802.11 Signal Detect CCA, OBSS_PD or TXPWR threshold values. The constraints on selecting threshold values are TBD”
    DSC is a good candidate mechanism, however, we must study spatial reuse mechanism not only regarding to aggregated throughput but also for STA fairness and goodput
    DSC scheme provides improvements in throughput but not always regarding to fairness and goodput. However, there is still a DSC margin value that allows increase in fairness, goodput and aggregated throughput
    DSC parametrization is of crucial importance
  DSC draft proposal:
    “A variety of methods could be used for the AP to determine these values, either by pre-setting them based upon the location and environment of the network, or by a learning process”
    The learning process should be investigated

## Slide 17: 8. References
Graham Smith, DSP Group, 11-13-1290-01 Dynamic Sensitivity Control for HEW
Graham Smith, DSP Group, 11-13-1487-02 Dense Apartment Complex Capacity Improvements with Channel selection and Dynamic Sensitivity Control
Graham Smith, DSP Group, 11-13-1489-05 Airport Capacity Analysis
Graham Smith, DSP Group, 11-14-0045-02 E-Education Analysis
Graham Smith, DSP Group, 11-14-0058-01 Pico Cell Use Case Analysis
Graham Smith, DSP Group, 11-14-0294-02 Dynamic Sensitivity Control Channel Selection and Legacy Sharing
Graham Smith, DSP Group, 11-14-0365-01 Dynamic Sensitivity Control Implementation
Graham Smith, DSP Group, 11-14-0328-02 Dense Apartment Complex Throughput Calculations
Graham Smith, DSP Group, 11-14-0779-00 Dynamic Sensitivity Control Practical Usage
Imad Jamil, Orange, 11-14-0523-00 Mac Simulation Results for DSC and TPC
William Carney, Sony, 11-14-0854-00 DSC and Legacy Coexistence
Shahwaiz Afaqui, 11-15-0027-1 Simulation-based evaluation of DSC in residential scenario
Graham Smith, DSP Group, 11-16-0310-1-00 CCA Proposal DSC Text
11-14-0980-16 TGax Simulation scenarios
Graham Smith, 11-15-0548-1 Enterprise scenario and DSC
J. R., “Fairness: How to measure quantitatively?”