## Slide 1: Remaining Issues in Trigger Frame Design
Date: 2016-05-16
Authors:
Name | Affiliation | Address | Phone | Email
Lochan Verma | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | lverma@qti.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
Raja Banerjea |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rajab@qca.qualcomm.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alice Chen |  | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com

## Slide 3
Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Thomas Derham |  |  |  | 
Mingyue Ji |  |  |  | 

## Slide 4: Authors (continued)
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Feng Jiang |  |  |  | feng1.jiang@intel.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 6: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Jarkko Kneckt |  |  |  | jkneckt@apple.com
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
David X. Yang | Huawei | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Jian Yu |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
Yuchen Guo |  | F1-17, Huawei Base, Bantian, Shenzhen |  | guoyuchen@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan | +81 46 859 3135 | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  | +81 46 859 5097 | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  | +81 46 859 5107 | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  | +81 46 859 3494 | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  | +81 46 859 4233 | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  | +81 46 859 4222 | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan | +81 46 840 3759 | yamadaakira@nttdocomo.com

## Slide 10: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Sigurd Schelstraete | Quantenna |  |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quantenna.com
Minho Cheong | Newracom | 9008 Research Dr. Irvine, CA 92618 |  | minho.cheong@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com

## Slide 12: Introduction
In these slides we touch upon some remaining open items in the trigger frame design for 802.11ax
Outline
  Current trigger frame structure
  TBDs in Common Info field and Per User Info field of Trigger frame
    Propose resolutions for the TBDs
  Issue with UL MU-MIMO LTF mode signaling and its solution
  Minor change to the ordering of the fields

## Slide 13: Current Trigger Frame Format
 | Frame Control | Duration | RA | TA | Common Info | Per User Info | … | Per User Info | Padding | FCS
Octets: | 2 | 2 | 6 | 6 | TBD | TBD |  | TBD |  | 4
 | Length | Cascade Indication | CS Required | Spatial Reuse | BW | CP and LTF Type | MU MIMO LTF Mode | # of LTFs
Bits: | 12 | 1 | 1 | >=2 | TBD | TBD | 1 | 3
STBC | LDPC Extra Symbol | AP TX Power | Packet Extension | Trigger Type | Type-dependent Common Info
1 | 1 | TBD | >=3 | 4 | variable
 | User Indentifier | RU Allocation | Coding Type | MCS | DCM | SS Allocation | Target RSSI | Type dependent Per User Info
Bits: | 12 | 8 | 1 | 4 | 1 | 6 | TBD | variable
Trigger Frame Format
Common Info field
Per User Info field
Slide-set focused on subfields shown in red

## Slide 14: TBD in Common Info Field (1/2)
BW 2 bits
  Set to 0 for 20 MHz, 1 for 40 MHz, 2 for 80 MHz, 3 for 160 & 80+80 MHz
  No need to indicate channel bonding
    3 bits not sufficient to indicate all channel bonding cases anyways
CP and LTF Type
  Proposal: 2 bits
    Combinations: 2x LTF+1.6 μs, 4x LTF+3.2 μs, 1x LTF+1.6 μs
    1x LTF + 1.6 ms gives a 1x LTF mode for full BW operation in UL trigger based PPDUs
      Longer CP helps with arrival time spreads in UL MU-MIMO

## Slide 15: TBD in Common Info Field (2/2)
AP Tx Power  Please refer to discussion in [1]
  6 bits
Packet Extension (PE)  3 bits
  PE definition for HE_TRIG PPDU consistent with other PPDU types
  First two bits indicate “a-factor” and third bit indicates PE-Disambiguity

## Slide 16: HE-SIG-A fields of HE_TRIG PPDU
HE-SIG-A of HE_TRIG PPDU
  19 bits are already decided, 33 bits left
Fields of the HE-SIG-A should be same across all STAs in HE_TRIG_PPDU
  Implies that even reserved bits should be set by the AP  Gives some future proofing advantages
Proposal: AP sets in trigger, the ‘33 – TXOP’ bits that constitute SR + Reserved
  STAs come up the TXOP field that is identical across all transmitters using Duration/ID of trigger
Field | Length (Bits) | Description
Format, BSS Color, Bandwidth, CRC, Tail | 19 | Cumulative length of format, BSS color, BW, CRC, and Tail fields
Spatial Reuse | TBD | Move to add to the spec framework in trigger based UL > 1 SR fields are signaled for > 1 different sub-bands [Motion 5, March 2016]
TXOP Duration | TBD | Indicates the remaining time in the current TXOP; can be derived from the Duration/ID of the Trigger frame itself
Reserved | TBD | 
Table: HE-SIG-A for HE_TRIG PPDU

## Slide 17: TBD in Per User Info Field
Target RSSI  Please refer to discussion in [1]
  7 bits

## Slide 18: Implication of MU MIMO LTF Mode subfield Signaling
Common Info field signals MU MIMO LTF Mode
  Indicates single-stream pilots or a masked LTF for UL MU MIMO RUs [1]
  STA always uses single-stream pilots for SU RU allocation
Per User Info field doesn't indicate if RU allocation is SU/MU
  STA needs to parse all Per User Info fields to determine it  Not a good design
We propose a way for the recipient STA to determine what UL MU-MIMO LTF Mode to use

## Slide 19: MU MIMO LTF Mode Setting Policy
Enforce a policy at the HE AP such that it sets the MU MIMO LTF Mode to:
  Single-stream pilots for any OFDMA transmission (including the case where MU-MIMO happens on part of the BW)
  The appropriate LTF mode for full BW MU-MIMO
Implication of the above
  Masked LTF mode can only be used in case of full BW UL MU-MIMO
  STAs do not get an explicit indication about the RU being SU vs MU

## Slide 20: Minor ordering issues
Move the Trigger Type to the first element of the Common Info Field
Move the field ‘Spatial Reuse + Reserved’ to the end of Common Info Field

## Slide 21: Summary
We presented Trigger frame related TBDs
  Proposed bit width of TBD subfields in Common Info field and Per User Info field
MU MIMO LTF Mode signaling issue
  Define MU MIMO LTF Mode setting policy at the HE AP
Slight modification to the ordering of the fields

## Slide 22: References
[1] Doc 11-16/0617r0, “Remaining topics in power control”, Bin Tian, Qualcomm

## Slide 23: SP #1
Do you agree to add the following to the SFD?
  “BW subfield length in the Common Info Field of the Trigger frame is 2 bits”

## Slide 24: SP #2
Do you agree to add the following to the SFD?
  “PE subfield length in the Common Info Field of the Trigger frame is 3 bits”

## Slide 25: SP #3
Do you agree to add the following to the SFD?
  ‘CP and LTF Type’ subfield length in the Common Info Field of the Trigger frame is 2 bits

## Slide 26: SP #4
Do you agree to add the following to the SFD?
  The AP specifies in the Trigger frame, the value of SR and Reserved bits which is used by the STA in HE-SIG-A of a trigger-based PPDU.

## Slide 27: SP #5
Do you agree to add the following to the SFD ?
  The HE AP shall set the MU MIMO LTF Mode bit in the trigger to indicate:
    Single-stream pilots for any OFDMA transmission (including the case where MU-MIMO happens on part of the BW)
    The appropriate LTF mode (single stream pilots or masked LTFs) for full BW MU-MIMO

## Slide 28: SP#6
Do you agree to add the following ordering of the common info fields of the trigger frame to the SFD?

## Slide 29: SP#7
Do you agree to add the following ordering of the common info fields of the trigger frame to the SFD?