## Slide 1: Block Ack generation and selection rules
Name | Affiliation | Address | Phone | Email
Alfred Asterjadhi | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alice Chen |  | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Date: 2016-05-14

## Slide 2
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tao Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | ttian@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Authors (continued)

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 4: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Zhou Lan |  |  |  | Zhou.lan@mediaTek.com
Russell Huang |  |  |  | russell.huang@mediatek.com

## Slide 5
Name | Affiliation | Address | Phone | Email
Peter Loc | Huawei |  |  | peterloc@iwirelesstech.com
Le Liu |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18601656691 | liule@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com
Authors (continued)

## Slide 6
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Authors (continued)

## Slide 7
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  |  | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  |  | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com
Authors (continued)
Sigurd Schelstraete | Quantenna |  |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quantenna.com

## Slide 8: Authors (continued)
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | mfischer@broadcom.com
Matthew Fischer |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Minho Cheong | Newracom | 9008 Research Dr. Irvine, CA 92618 |  | minho.cheong@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com

## Slide 9: Introduction
11ax uses two frame formats for BlockAck frames
  Compressed BlockAck (C-BA) and Multi-STA BlockAck (M-BA)
Each of which has signaling details for Bitmap lengths yet to be specified
  Both use the Fragment Number fields, though with undefined mapping[1, 2]
Same consideration for BlockAck frame/length selection rules [3]
  Both need signaling on which frame/length needs to be used
We propose to finalize the following design details:
  Mapping of Fragment Number subfield of BA frames and their BA Bitmap lengths
  Negotiation and selection of BlockAck frames during a block ack session
    Including BAR solicitation of these BA frames
While being compliant to baseline and passed motions on these topics

## Slide 10: Compressed BlockAck frame
According to REVmc D5.0 and 11ax D0.1:
  Fragment Number is 0 in C-BlockAck frame
    Fragment Number equal to 1 indicates re-mapping of BA Bitmap for fragmentation level 3 [3]
[1] proposed a variant of C-BA frame with 256-bits BA Bitmap field
  Reserved bit(s) in Fragment Number field of the frame indicates length of the BA Bitmap
We propose this mapping of the Fragment Number subfield
  B0 of Fragment Number is 1 to indicate that re-mapping of BA Bitmap for Fragmentation level 3 is ON [3]
  B2 and B1 of Fragment Number indicate the length of the BA Bitmap field for C-BA frame
    Only two values are defined in this case: 8 or 32 Bytes, as defined in [1]
  B3 is reserved
Same signaling applies to M-BA frames as well, with more options for Bitmap length [2]
  See next slide for more details
2 | 8 or 32
BA Starting Sequence Control | Block Ack Bitmap
 | B0 B3 | B4 B15
 | Fragment Number | Starting Sequence Number
Bits: | 4 | 12

## Slide 11: Multi-STA BlockAck frame
[2] proposed a variant of M-BA frame with variable length BA Bitmap field
  Length of the BA Bitmap field is indicated in Fragment Number field of the M-BA
We propose this mapping of the Fragment Number subfield
  B0 of Fragment Number is 1 to indicate that re-mapping of BA Bitmap for Frag. L3 is ON [3]
  B2 and B1 of Fragment Number indicate the length of the BA Bitmap field for M-BA frame
    Possible values are 4, 8, 32 and TBD, as defined in [2]
      We also propose to define the TBD as 16
  B3 is reserved
2 | 0 or 2 | 0, 4, 8, 16, or 32
Per AID TID Info | BA Starting Sequence Control | Block Ack Bitmap
 | B0 B3 | B4 B15
 | Fragment Number | Starting Sequence Number
Bits: | 4 | 12
Repeat for each AID and TID

## Slide 12: Mapping for FN subfield of BA frames
 |  | 4, 8, 16, or 32
Fragment Number | Starting Sequence Number | Block Ack Bitmap
4 | 12 | variable
Fragment Number subfield |  |  | BA Bitmap Length field [Octets]-Fragmentation L3 [ON/OFF] |  | Maximum number of MSDUs/A-MSDUs that can be acknowledged
B3 | B2 B1 | B0 | Compressed Block Ack | Multi-STA Block Ack | 
0 | 0 | 0 | Bitmap [8 Octets] – Frag [OFF] | Bitmap [8 Octets] – Frag [OFF] | 64
0 | 1 | 0 | Reserved | Bitmap [16 Octets] – Frag [OFF] | 128
0 | 2 | 0 | Bitmap [32 Octets] – Frag [OFF] | Bitmap [32 Octets] – Frag [OFF] | 256
0 | 3 | 0 | Reserved | Bitmap [4 Octets] – Frag [OFF] | 32
0 | 0 | 1 | Bitmap [8 Octets] – Frag [ON] | Bitmap [8 Octets] – Frag [ON] | 16
0 | 1 | 1 | Reserved | Bitmap [16 Octets] – Frag [ON] | 32
0 | 2 | 1 | Bitmap [32 Octets] – Frag [ON] | Bitmap [32 Octets] – Frag [ON] | 64
0 | 3 | 1 | Reserved | Bitmap [4 Octets] – Frag [ON] | 8
1 | Any | Any | Reserved |  | 

## Slide 13: Block Ack negotiation/selection
Reminder - Baseline rules:
  Originator/recipient negotiate BA op. parameters during HT-Immediate BA setup
    During which, along other parameters for a TID, Buffer Size is also negotiated
      Note: each MPDU consumes one of these Buffers
Passed motions:
  Both C-BA and M-BA frames can be used, both with variable Bitmap lengths [1, 2]
  M-BA will be used as a response frame for UL MU PPDUs, multi-TID A-MPDUs:
    A value of 15 in TID subfield of Per STA TID Info field of M-BA frame indicates successful acknowledgement of a MGMT frame that requires an immediate response and is carried in the soliciting A-MPDU [5]
    The spec shall allow UL MU transmission of Multi-STA Block ACK frame in response to multi-TID A-MPDU of DL MU transmission. The value of AID field in M-BA is TBD [6]
    MPDUs from multiple TIDs that ask for Ack/BA acknowledgement and one MGMT frame that asks for Ack may be aggregated in one A-MPDU of MU transmission [6]
    RX indicates max. # of TIDs the originator can aggregate in multi-TID A-MPDU[4]
    Etc.

## Slide 14: Proposed rules: BA Bitmap/TID selection
BA Bitmap length is negotiated during BA setup (for each TID)
  Block Ack Bitmap length of the BA frame is tied to the negotiated buffer size, e.g.,
    If buffer size is within [1, 64] then Bitmap length of 64 will be used during the BA session
    If buffer size is within [65, 256] then Bitmap length of 256 will be used during the session
Max. number of TIDs that can be aggregated in an A-MPDU is indicated in the HE Capabilities IE sent by the recipient
  Zero value indicates no support for multi-TID A-MPDU
  >0 indicates support for multi-TID A-MPDU and # of TIDs allowed in A-MPDU
    Note 1: Currently D0.1 has 1 bit for multi-TID support in HE Capabilities IE
  This indication is valid for both AP and non-AP STAs
    Note 2: The AP can still dynamically govern the max # of TIDs of QoS Data frames that each STA is allowed to aggregate in their A-MPDUs within an UL MU PPDU*
      By signaling that number to each STA in the Trigger frame
*UL MU PPDU refers to trigger-based PPDU in this slide deck

## Slide 15: BlockAck frame selection
Support/selection of BA frames
  C-BlockAck shall be supported if HT-immediate BA is supported
    Same as baseline
  M-BA shall be supported if either UL MU or multi-TID A-MPDU is supported
    Used as default response by AP to UL MU PPDUs and by STA to multi-TID A-MPDUs*
      Which could contain an Action Ack frame as well.
    We need capability bit from the originator to indicate RX support of ALL ACK signaling
      This is because originator needs to keep track of the state of all TXed MPDUs in an A-MPDU for all TIDs, Action Ack frame, and compare this state with each of Rxed multi-TID blockack records
Control response frame generation for SU PPDUs follow baseline:
  Consistently use Ack/C-BA frames
    C-BA Bitmap length is negotiated during setup, and used consistently during BA session
      This ensures consistency in BW/MCS/NAV setting rules
Control response frame generation for MU PPDUs is described next
  See slides 16-20

## Slide 16: Reference exchange sequences
STA 1
STA 2
STA 3
STA 4
DL MU
STA 2
UL SU
SIFS
STA 1
STA 2
STA 3
STA 4
DL MU
UL MU
SIFS
STA 1
STA 2
STA 3
STA 4
1) DL MU PPDU | SIFS | UL SU response
2) DL MU PPDU | SIFS | UL MU response
STA 1
STA 2
STA 3
STA 4
UL MU
DL SU
SIFS
STA 1
STA 2
STA 3
STA 4
UL MU
DL MU
SIFS
STA 1
STA 2
STA 3
STA 4
3) UL MU PPDU | SIFS | DL SU response
4) UL MU PPDU | SIFS | DL MU response
Trigger
SIFS
Trigger
SIFS
STA 1
STA 2
STA 3
STA 4
originator
AP
STAs
originator
AP
recipient(s)
STAs
recipient(s)
originators(s)
recipient
AP
STAs
originators(s)
AP
STAs
recipient

## Slide 17: 1) DL MU PPDU | SIFS | UL SU response
Further considerations for the soliciting DL MU PPDU:
    Only one of the recipients can have the Ack Policy setting to Normal Ack* within the DL MU PPDU
  The A-MPDU under these conditions** cannot contain an Action Ack frame
    Action Ack frames do not have an Ack Policy field to differentiate between SU and MU
      As such we can enable one way (preferred UL MU since most common case for DL MU responses)
  DL MU PPDU contains neither Trigger frames nor UL MU Response scheduling
# of originators generating the DL MU PPDU | Content of the A-MPDU(s) carried in the DL MU PPDU | Ack Policy setting | Control response frame generated by the recipient | UL PPDU response format
ONE (AP) | (A-) MPDU | No Ack or BlockAck | No Response | N/A
ONE | VHT Single MPDU | Normal Ack* | Ack frame | SU
ONE | A-MPDU | Implicit BAR* | C-BA frame | SU
ONE | Multi-TID A-MPDU** | Implicit BAR* | M-BA frame | SU
*Normal Ack and Implicit BAR are represented by the same value of the Ack Policy. |  |  |  | 

## Slide 18: 2) DL MU PPDU | SIFS | UL MU response
Further considerations for the soliciting DL MU PPDU:
  An A-MPDU under these conditions*** may contain an Action Ack frame
    Action Ack frames do not have an Ack Policy field to differentiate between SU and MU (preferred)
      I.e., by default the response to DL Multi-TID A-MPDU frames containing this MPDU is in MU mode
  The # of TIDs carried in multi-TID A-MPDU cannot exceed the # of TIDs specified by RX [4]
Recipient can only respond to the DL MU PPDU if its allocated RU contained:
  Either one/more Trigger frames or one/more HE variant HT Control fields with UL MU Response Scheduling but not both
# of originators generating the DL MU PPDU | Content of an (A-) MPDU carried in the DL MU PPDU | Ack Policy setting [# recipients] | Control response frame generated by each recipient | UL PPDU response format
ONE (AP) | (A-) MPDU | No Ack or BlockAck [ALL] | No Response | N/A
ONE | VHT Single MPDU | MU Ack** [>0] | Ack frame | UL MU PPDU*
ONE | A-MPDU | MU Ack [>0] | C-BA frame | UL MU PPDU*
ONE | Multi-TID A-MPDU*** | MU Ack [>0] | M-BA frame | UL MU PPDU*
*STAs cannot solicit response from AP to an UL MU PPDU if Trigger info in DL MU PPDU was not Basic or was UL MU Response Sched. *STAs can solicit a response from the AP to the UL MU PPDU if the Trigger carried in the DL MU PPDU was a Basic Trigger. **MU Ack is signaled by a value of PSMP Ack value of the Ack Policy. |  |  |  | 

## Slide 19: 3) UL MU PPDU | SIFS | DL SU response
Further considerations for the soliciting UL MU PPDU:
  An A-MPDU under these conditions*** may contain an Action Ack frame
    By default the response to Multi-TID A-MPDU frames containing this MPDU is an M-BA
  The # of TIDs carried in multi-TID A-MPDU cannot exceed the number of TIDs specified by the recipient [4]
# of originators generating the UL MU PPDU | Content of the A-MPDU(s) carried in the UL MU PPDU | Ack Policy setting [# originators] | Control response frame generated by the recipient (AP) | DL PPDU response format
ONE/MORE (non-AP STAs) | (A-)MPDU | No Ack [ALL] | No Response | N/A*
ONE/MORE | VHT Single MPDU | Normal Ack [> 0] | Ack [if 1 orig.] or M-BA [if >1 orig.] | SU**
ONE/MORE | A-MPDU | Implicit BAR [>0] | C-BA [if 1 orig.] or M-BA [if >1 orig.] | SU**
ONE/MORE | Multi-TID A-MPDU*** | Implicit BAR [>0] | M-BA frame [if > 0 orig.] | SU**
*STAs cannot solicit response to UL MU PPDU if Trigger soliciting this UL MU PPDU was not Basic or was UL MU Response Sched. field. **STAs can solicit a response to the UL MU PPDU if the Trigger that solicited this UL MU PPDU was a Basic Trigger. |  |  |  | 

## Slide 20: 4) UL MU PPDU | SIFS | DL MU response
Further considerations for the soliciting UL MU PPDU:
  An A-MPDU under these conditions*** may contain an Action Ack frame
    By default the response to Multi-TID A-MPDU frames containing this MPDU is an M-BA
  The # of TIDs carried in multi-TID A-MPDU cannot exceed the number of TIDs specified by the recipient [4]
# of originators generating the UL MU PPDU | Content of the A-MPDU(s) carried in the UL MU PPDU | Ack Policy setting [# originators] | Control response frame generated by the recipient (AP) | DL PPDU response format
ONE/MORE (non-AP STAs) | (A-)MPDU | No Ack [ALL] | No Response | N/A*
ONE/MORE | VHT Single MPDU | Normal Ack [> 0] | Ack [if 1 orig.] M-BA [if >1 orig.] | MU**
ONE/MORE | A-MPDU | Implicit BAR [>0] | C-BA [if 1 orig.] M-BA [if >1 orig.] | MU**
ONE/MORE | Multi-TID A-MPDU*** | Implicit BAR [>0] | M-BA frame [if > 0 orig.] | MU**
*STAs cannot solicit response to UL MU PPDU if Trigger soliciting this UL MU PPDU was not Basic or was UL MU Response Sched. field. **STAs can solicit a response to UL MU PPDU if the Trigger that solicited this UL MU PPDU was a Basic Trigger. |  |  |  | 

## Slide 21: BAR-solicited BA frames
Originator may solicit BA frames with a BAR frame which shall be either:
  The only MPDU carried in the PPDU (same as baseline)
  The last MPDU of the A-MPDU (same as baseline)
  Included as part of the BAR variant of the Trigger frame
    If this Trigger is aggregated in an A-MPDU then no other BAR frames shall be present in the A-MPDU
BAR frame (or content of the MU BAR variant of Trigger) can be either:
  Compressed BAR if maximum number of TIDs supported by recipient is 1
  Multi-TID BAR if maximum number of TIDs supported by recipient is 1 or more

## Slide 22: Summary
We discuss the remaining design details for BA operation:
  Provide BA selection rules for variable bitmaps and multi-TID support
    And propose FN signaling for the variable lengths of BA frames
  Provide the respective per-PPDU acknowledgment rules
  Clarify presence of BAR frames
While ensuring that the new operations/additions do not affect:
  NAV duration setting, MCS selection rules, BA rules, scoreboard maintenance, its advancement, etc.

## Slide 23: Straw Poll 1
Do you support to add to the 11ax SFD the following mapping for the FN subfield of BA frames?
Fragment Number subfield |  |  | BA Bitmap Length field [Octets]-Fragmentation L3 [ON/OFF] |  | Maximum number of MSDUs/A-MSDUs that can be acknowledged
B3 | B2 B1 | B0 | Compressed Block Ack | Multi-STA Block Ack | 
0 | 0 | 0 | Bitmap [8 Octets] – Frag [OFF] | Bitmap [8 Octets] – Frag [OFF] | 64
0 | 1 | 0 | Reserved | Bitmap [16 Octets] – Frag [OFF] | 128
0 | 2 | 0 | Bitmap [32 Octets] – Frag [OFF] | Bitmap [32 Octets] – Frag [OFF] | 256
0 | 3 | 0 | Reserved | Bitmap [4 Octets] – Frag [OFF] | 32
0 | 0 | 1 | Bitmap [8 Octets] – Frag [ON] | Bitmap [8 Octets] – Frag [ON] | 16
0 | 1 | 1 | Reserved | Bitmap [16 Octets] – Frag [ON] | 32
0 | 2 | 1 | Bitmap [32 Octets] – Frag [ON] | Bitmap [32 Octets] – Frag [ON] | 64
0 | 3 | 1 | Reserved | Bitmap [4 Octets] – Frag [ON] | 8
1 | Any | Any | Reserved |  | 

## Slide 24: Straw Poll 2
Do you support to add to the 11ax SFD:
The BA Bitmap length of BA frames generated during a BA session is negotiated during the BA setup
  If the negotiated buffer size is within [1, X] then a BA Bitmap length of X bits will be used during the BA session for the negotiated TID
  If the negotiated buffer size is within [X+1, Y] then a BA Bitmap length of Y bits will be used during the BA session for the negotiated TID
    Note: X and Y correspond to the agreed BA Bitmap lengths of the respective BA frame (e.g., 32, 64, etc.)
  Per-PPDU BA selection rules within a BA session for the BA Bitmap length of the BA frames is TBD for <RA, TA, TID>

## Slide 25: Straw Poll 3
Do you support to add to the 11ax SFD:
The maximum number of TIDs of QoS Data frames that an originator can aggregate in a multi-TID A-MPDU is indicated in the HE Capabilities element sent by the recipient
  A nonzero value also indicates that the recipient supports reception of multi-TID A-MPDUs
    Note: A multi-TID A-MPDU allows the aggregation of an Action Ack frame as well
A STA that transmits a trigger-based PPDU as an immediate response to the Basic variant Trigger frame follows the indication of max number of TIDs contained in the Trigger Dependent Per User Info field of the Trigger frame addressed to the STA (i.e., AID of the Per User Info field is that of the STA) and can transmit an A-MPDU that contains a number of aggregated TIDs in the A-MPDU that is up to that value.

## Slide 26: Straw Poll 4
Do you support to add to the 11ax SFD:
Multi STA BA frames shall be supported if either UL MU or multi-TID A-MPDU operation is supported
Originator indicates support for reception of ALL ACK signaling (Ack Type subfield set to 0 when responding to the soliciting A-MPDU) in Multi STA Block Ack frame that is sent as a response to the A-MPDU via a capability bit

## Slide 27: Straw Poll 5
Do you support to add to the 11ax SFD:
HE STAs follow the solicitation/response rules listed in slides 17-20.

## Slide 28: Straw Poll 6
Do you support to add to the 11ax SFD:
A STA shall not send a Multi TID BAR to a STA that has not indicated support for multi-TID A-MPDU.
  Also applicable to each BAR information carried in the MU BAR variant Trigger frame

## Slide 29: References
[1] S. Merlin (Qualcomm Inc.) et.al., 11-16-0378-02-00ax-extended-ba-bitmap
[2] D. Qiao (Huawei) et. al., 11-16-0404-00-00ax-blockack-bitmap
[3] IEEE members, et. al Draft P802.11ax_D0.1
[4] C. Ghosh (Intel) et. al., 11-16/0362r1 Multi-TID Aggregation Limit
[5] L. Chu (Marvell) et. al., 11-16/0359r0 Management Ack
[6] L. Chu (Marvell) et. al., 11-16/0069r0 Multi-TID A-MPDU in MU transmission