## Slide 1: DCM PHY Parameters
Date: 2016-05-16
Authors:

## Slide 2: Authors (continued)

## Slide 3: Authors (continued)

## Slide 4: Authors (continued)

## Slide 5: Authors (continued)
Authors (continued)

## Slide 6: Authors (continued)

## Slide 7: Authors (continued)

## Slide 8: Authors (continued)

## Slide 9: Authors (continued)

## Slide 10: Authors (continued)

## Slide 11: Overviews
DCM has been introduced to 11ax as an optional mode.
Some PHY parameter exceptions for MCS0-DCM need to be addressed when DCM is used.
There are also some related issues in current D0.1 on the MCS tables.

## Slide 12: MCS0-DCM Non-Integer NDBPS Issue
For some RU sizes, with MCS0-DCM, NDBPS is non-zero.
  106-RU, MCS0-DCM, 1SS: NSD.DCM =102/2=51, NCBPS=51, NDBPS = 51/2.
  242-RU, MCS0-DCM, 1SS: NSD.DCM=234/2=117, NCBPS=117, NDBPS=117/2
Proposed parameters for these cases.

## Slide 13: 1. BCC Case: Post-FEC padding for MCS0-DCM
Conduct post-FEC padding of 1 bit per-symbol after BCC encoder to make up NCBPS coded bits, before interleaving.
BCC
BCC Interleaver
Constellation Mapper for 1st half band
Padding 1 bit
(for MCS0-DCM, 1SS, 106-RU or 242-RU)
IDFT
Constellation Mapper for 2nd half band
DCM Modulation Mapper
Consellation Mapper

## Slide 14: 2. LDPC Case
Solution: no post-FEC padding required, directly conduct LDPC encoding process as in 11ac assuming the NCBPS, NDBPS, parameters – just like any other non-integer NDBPS cases for LDPC.

## Slide 15: Notes on the MCS Table in D0.1
In Current MCS table of D0.1 we saw the following issues:
  In DCM=1 case, NSD and NCBPS are identical to DCM=0, with a coding rate 1/4. There is no such a coding scheme especially for LDPC, in which we reuse 11ac encoding procedure and this NCBPS value leads to a different LDPC code!
  DCM=1 is applied to all MCS tables, we need to mark DCM=1 only in the MCS tables that allows DCM.
Proposed Changes:
  Change the NSD, NCBPS and NDBPS parameters as proposed.
  Change the coding rate R to be identical to DCM=0.
  Limit DCM=1 only to the allowed Nss cases.

## Slide 16: SP1
Do you agree to add the following text to the SFD:
  When DCM = 1, the NSD, NCBPS, and NDBPS are set by the following expressions:
  In the case of MCS0, DCM=1, Nss=1, 106-RU or 242-RU, if the coding is BCC, then for each OFDM symbol 1 bit is padded after the NDBPS*2 BCC encoded bit before going into the BCC interleaver; if the coding is LDPC, LDPC encoding flow should be based on NDBPS and NCBPS as defined in the above equations

## Slide 17: SP2
Do you agree to make the following changes to D0.1 MCS Tables:
  When DCM=1, change the NSD parameter to be ½ of DCM=0 cases for the same RU size.
  When DCM=1, change the NCBPS parameter to be ½ of DCM=0 case.
  When DCM=1, change the NDBPS parameter to be ½ of DCM=0 case, or take the floor for the two cases: 106-RU, MCS0, DCM=1, Nss=1, and 242-RU, MCS0, DCM=1, Nss=1.
  When DCM=1, change the coding rate R parameter to be identical to the DCM=0 case.
  Limit DCM=1 only to the allowed Nss.