## Slide 1: Buffer Status Report in HE Control field
Date: 2016-05-16
Authors:
Name | Affiliation | Address | Phone | Email
Jayh hyunhee Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | hyunh.park@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2
Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Thomas Derham |  |  |  | 
Mingyue Ji |  |  |  | 

## Slide 3
Authors (continued)
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Feng Jiang |  |  |  | feng1.jiang@intel.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Jie Huang |  |  |  | jiehuang@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Edward Au |  |  |  | edwardau@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 5
Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Lochan Verma |  | 5775 Morehouse Dr. San Diego, CA USA |  | lverma@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 6
Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 7
Authors (continued)
Joonsuk Kim | Apple |  |  | joonuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Jarkko Kneckt |  |  |  | jkneckt@apple.com
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com

## Slide 8
Authors (continued)
Name | Affiliation | Address | Phone | Email
David X. Yang | Huawei | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | zhangjiayin@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen |  | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Jian Yu |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
Yuchen Guo |  | F1-17, Huawei Base, Bantian, Shenzhen |  | guoyuchen@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  |  | Iwatani.junichi@lab.ntt.co.jp
Shoko Shinohara |  |  |  | Shinohara.shoko@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com

## Slide 10: Authors (continued)
Name | Affiliation | Address | Phone | Email
Yuichi Morioka | Sony Corporation | 1-7-1 Konan Minato-ku, Tokyo 108-0075, Japan |  | yuichi.Morioka@jp.sony.com
Masahito Mori |  |  |  | masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | yusukeC.Tanaka@jp.sony.com
Kazuyuki Sakoda |  |  |  | kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | william.Carney@am.sony.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com

## Slide 11
Authors (continued)
Sigurd Schelstraete | Quantenna |  |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quantenna.com
Minho Cheong | Newracom | 9008 Research Dr. Irvine, CA 92618 |  | minho.cheong@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com

## Slide 12
Authors (continued)

## Slide 13: Current Spec text on BSR
In 11ax Draft Spec [1]:
  The buffer status report from HE STAs may be utilized to support the efficient UL MU operation. An AP may poll HE STAs for buffer status reports using the frame carrying the trigger information. The frame may be a broadcast Trigger frame, a unicast Trigger frame, a Trigger frame for random access, or a Data type of frame carrying the trigger information.
  An AP may request an HE STA to send its buffer status information by TBD indication in the Trigger frame or in the HE A-Control field in a Data type of frame.
  In this case, an AP may indicate TBD granularity of the Queue Size for an HE STA to report (signalling method TBD). Upon reception of the frame including the TBD indication in the Trigger frame or in the HE A-Control field, the HE STA may respond with the frame including the Queue Size subfield in a QoS Control field or TBD HE A-Control field.
  To report the buffer status for a given TID, an HE STA shall set the Queue Size subfield in a QoS Data or a QoS Null frame to the amount of queued traffic present in the output queue belonging to the TID

## Slide 14: Motivation
One of the main features introduced in 11ax is UL MU operation
  AP allocates UL resources used by multiple STAs to transmit their data
For an efficient UL allocation a buffer status (BS) report mechanism was defined [2]
  STAs use the Queue Size subfield of the QoS Control field in frames they transmit
    This per-TID buffer status information is present in every QoS Data/Null frames
  AP can additionally poll STAs for BS using the frame carrying trigger info
    The poll can request for specific BS information with TBD granularity
      BS could be per-TID and per-AC (which is TBD)
In this contribution, we propose that the buffer status information can be reported if the buffer status for multiple TIDs needs to be reported

## Slide 15: QoS Control field
QoS Control field
  The TID subfield in the QoS Control field indicates only one TID of the current data frame

## Slide 16: Problem Statement
One problem with buffer status report using QoS Control is that a STA can only report its Queue Size for the TID that current frame belongs to
When the STA has other TID traffic backlogged especially latency sensitive traffic, it cannot inform the AP in a timely manner
In such case, the STA has to either contend for the medium to transmit the new TID data or wait for AP’s allocation and transmit the new TID data if the allocation is sufficient
Allow Buffer Status Report (BSR) to include buffer status info of multiple AC or multiple TID

## Slide 17: Buffer Status Report
STAs implicitly report their buffer status information in BS report frames
  A BS report frame can contain the QoS Control field, i.e.,
    QoS Data, QoS Null frames for delivering per-TID BS reports
We propose to allow HE STA to send a buffer status information for multiple TIDs/ACs using an HE Control header (using available 26 bits)
HE Control field
Bits: | 2 | 4 | variable | : 4 bytes
 | rev | Control ID | Control Information | 

## Slide 18: Proposed BSR field
Proposed HE Control field: BS report for multiple TIDs/ACs
  A new Control ID value of the HE variant HT Control field identifies a BSR (e.g., Control ID: 3)
  Control Information: Buffer status information content
    One or more (number is TBD) Queue Size subfields report the queue size
    Identifier of AC/TID (and for which) is currently TBD

## Slide 19: Summary
We propose to allow STA to send a buffer status information for multiple TIDs/ACs using an HE Control header
  An HE STA may send the buffer status report (BSR) in the HE variant HT Control field for one or more queues (whether content of queue is per TID or per AC is TBD) when the AP supports its reception

## Slide 20: References
[1] https://mentor.ieee.org/802.11/dcn/15/11-15-0132-16-00ax-spec-framework.docx
[2] A. Asterjadhi, et.al., 11-15-1120-00-00ax-buffer-status-report

## Slide 21: Straw Poll
Do you agree to add the following text to the 11ax Specification Frame work document:
  An HE STA may send the buffer status report (BSR) in the HE variant HT Control field for one or more queues (whether content of queue is per TID or per AC is TBD) when the AP supports its reception
    A new Control ID value of the HE variant HT Control field identifies a BSR
    One or more (number is TBD) Queue Size subfields report the queue size
    Identifier of AC/TID (and for which) is currently TBD

## Slide 22: Appendix

## Slide 23: AC based BSR
An EDCA parameter is defined per-AC not TID
  A STA can access the channel to send a packet with a TID using the EDCA parameter related to the AC for the TID
  The packets belonging to the same AC but different TIDs are transmitted using the same access parameter such as AIFSN, CWmin, CWmax
DL MU-MIMO in 11ac uses the AC based TXOP sharing mechanism
The AC based buffer status information can be reported if the buffer status for multiple TIDs needs to be reported
  The AC based BS report requires less overhead than the TID based one when multiple TIDs/ACs needs to be reported