## Slide 1: Consideration on backoff procedure for UL MU transmission
Date: 2016-05-17
Authors:

## Slide 2: Background
A non-AP STA possibly commences UL transmission using UL SU MPDU or UL MU MPDU after performing Carrier Sensing (CS) in 11ax specification.
  The non-AP STA commences UL transmission using UL SU MPDU in case of the medium is determined to be idle for the duration of (DIFS/EIFS + backoff).
  The non-AP STA commences UL transmission using UL MU MPDU when the STA receives Trigger Frame (TF) while performing CS during the (DIFS/EIFS + backoff) period.

## Slide 3: Issue
Backoff procedure is defined in baseline 802.11 specification
  “ …. After the DIFS or EIFS medium idle time, the STA shall then generate a random backoff period for an additional deferred time before transmitting, unless the backoff timer already contains a non zero value, …”
In case of UL MU transmission (sub- bullet #2 in previous page)
  A STA potentially gets more chance accessing the channel and commences SU UL transmission since the STA will use the remaining backoff time according to the baseline behavior (which is nonzero due to the UL transmission is triggered) instead of generates new backoff period

## Slide 4: Proposal
We propose that a non-AP STA should set its backoff timer to 0 after transmitting an UL PPDU as the response to trigger frame

## Slide 5: SP
Do you agree to the following statement marked as blue to 11ax TG SFD:
  A STA shall set its backoff timer to 0 after transmitting an UL PPDU as the response to trigger frame
  then commence the transmission of an HE trigger-based PPDU at the SIFS time boundary after the end of a received PPDU, when all the following conditions are met (p. 58, line 5)

## Slide 6: References
11-16/0024r1, Draft Specifications, March 2016
11-15/0132r15, Specification Framework for TGax, Jan 2016