## Slide 1
Multi-User EDCA
Date: 2016-05-15
Authors:

## Slide 2: Introduction
MU DL is defined for MU-MIMO procedure in 11ac[1]
  Sharing a TXOP is a channel access scheme for MU-MIMO
  Channel Access follows the rules for the Access Category of Primary Access Category
  Transmission success is judged by Primary transmission only
802.11ax MU UL channel access has not been defined yet
Many comments are related to Access Category and channel access of UL MU transmission[2]
  CID 158, 799, 809, 814, 815, 816, 1646, 2173, 2271, 2638, 2644, 2656
In this contribution, virtual queue for UL MU transmission to remove the ambiguities regarding UL MU is discussed.

## Slide 3: Review – DL MU-MIMO transmission[1]
TXOP Initiator = TX Data
Multiple AC could exist on DL Data
Choose Primary AC by virtual contention
DL OFDMA may reuse this scheme[3]

## Slide 4: Channel Access for Trigger Frame
MU UL begins with Trigger Frame transmitted by AP
Need to define a procedure whether to transmit DL data or to transmit Trigger Frame
Hard to know which EDCA parameters are appropriate for UL transmission
STA
3
UL PPDU
STA
2
UL PPDU
STA
1
UL PPDU
M
-
BA
Trigger
Frame
AP
STAs
AIFS
Which EDCA parameters should Trigger Frame follow ?
When or How often Trigger Frames should be transmitted?
Ambiguity 1
Ambiguity 2

## Slide 5: Channel Access for Trigger Frame
Buffer Status Report (BSR) Procedure was adopted for 802.11ax MU UL and it should be used for AP to determine UL transmission scheduling
  DL transmission or UL transmission
  UL Trigger Frame transmission timing
Although Buffer Status Report Procedure is defined, Access Category or TID of UL data can not be regulated for MU UL transmission
  Trigger Frame can not restrict transmission of any AC or TID of STAs
Therefore, applying legacy access category scheme including ‘sharing a TXOP scheme’ for Trigger Frame Channel Access is not feasible

## Slide 6: UL MU access category for Trigger Frame
UL MU Access Category and UL MU virtual queue can clarify the two ambiguities of UL MU channel Access
  When or how often Trigger Frames should be transmitted ?
  Which EDCA parameters should Trigger Frame follow ?
Queue size of AC_MU is determined with cumulated Buffer Status Report information and STAs SU transmission status

## Slide 7: UL MU access category for Trigger Frame
For internal contention, UL MU virtual contention parameters controlled by virtual queue size
  Large virtual queue size should provide a high probability of channel access  small Backoff (BO) value
If AC_MU wins the internal contention, trigger frame follows the channel access parameters of AC_MU

## Slide 8: UL MU access category for Trigger Frame
Backoff (BO) values should be controlled depending on the AC_MU queue size
  BO values should be controlled with Contention Window (CW) size
  Unlike the conventional BO, minimum(Min) BO should be regulated to solicit large number of STAs.

## Slide 9: Example of UL MU Contention Control
AC_MU gets virtual back-off values in the range of [Min BO, CW] instead of [0,CW]
If the queue length of AC_MU(UL) is smaller than certain threshold value, trigger frame cannot get a transmission opportunity due to its large minimum back off number
Either fixed CW or variable CW can be used
  N>1 : variable CW
  N=1 : fixed CW with UL MU threshold
Category | Queue Length(Q) | Min BO | CW(Max BO)
1 (Hold BO) | Q<Th_1 | 1024 (Hold) | 1024 (Hold)
2 | Th_1≤Q<Th_2 | 8 | 31
3 | Th_2≤Q<Th_3 | 0 | 31
4 | ⁞ | ⁞ | ⁞
N+1 (N≥1) | Th_n≤Q | 0 | 0

## Slide 10: Channel Access for Trigger Frame
When AC_MU wins the virtual contention, Trigger frame is transmitted with Trigger frame access category (AC_MU) EDCA parameters
EDCA parameters for Trigger frame access category (AC_MU) needs to be defined
  Not only fixed value, but also variable value which is based on queue length could be considered (Legacy ACs could be reused for AC_MU, e.g., AC_VI)
STA
3
UL PPDU
STA
2
UL PPDU
STA
1
UL PPDU
M
-
BA
Trigger
Frame
AP
STAs
AIFS(AC_MU)
BO=[MinBO, CW]
TXOP(AC_MU)

## Slide 11: Revisit: DL MU channel access procedure
We could have two options of DL MU
  Opt.1 : Using sharing a TXOP method for both DL-MU MIMO and DL-MU-OFDMA
  Opt.2 : Using virtual DL_MU queue similar to virtual UL_MU queue
Opt.1 is simple but it has some regulations
  Since the failure of Primary transmission is regarded as the transmission failure, an inefficient procedure should be taken, i.e., CW should be doubled
  Multi-TID cannot be used for Primary transmission
Opt.2 requires new procedure but it could be more flexible
  Transmission success can be more properly defined (e.g. Only one response of DL MU transmission can be considered as a success)
  Multi-TID A-MPDU could be utilized for DL MU as well

## Slide 12: Further Discussion on MU Channel Access
We need more discussion whether “sharing a TXOP” is efficient and only option for DL MU channel access.
Specific parameters for contention need to be defined.
  Min BO, Max BO(=CW), TXOP, AIFSN
  Whether parameters are variable or fixed
If other Trigger variant frames need to be transmitted with contention based channel access, Trigger variant frames’ channel access methods need to be defined.
  MU-RTS may follow EDCA of the following channel access procedure of MU data transmission.
  UL MU for management frames including BSR procedure may use different mechanism and UL MU parameters.

## Slide 13: Conclusion
MU UL virtual queue based on BSR information could be a solution for 11ax EDCA
Variable virtual contention parameters for AC_MU could control when and how often Trigger frames are transmitted
Although BSR procedure is considered for UL MU transmission, actual UL PPDU could be a Multi-TID A-MPDU and its Access Category is hard to known to AP
  AP cannot determine which access category shall be adopted for channel access parameters
  Regardless of UL PPDU contents, Trigger frame always need to be transmitted following AC_MU

## Slide 14: StrawPoll 1
Do you agree to add to the TG Specification Frame work document?
  x.y.z. Spec shall define a virtual queue for UL MU contention based channel access procedure and its EDCA parameters (TBD) for trigger frame channel access
    Y
    N
    A

## Slide 15: References
[1] Draft P802.11REVmc_D5.0
[2] 11-16/0535r03 “Comments on TGax D0.1”
[3] 11-15/0132r16 “Spec Framework”