## Slide 1: Spatial Re-Use OA-CCA Mode and SR Field Discussion
Date: 2016-05-16
Authors:
Name | Affiliation | Address | Phone | Email
James Wang | Mediatek | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | james.wang@mediatek.com
Jianhan Liu |  |  |  | thomas.pare@mediatek.com
Thomas Pare |  |  |  | chaochun.wang@mediatek.com
ChaoChun Wang |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee |  | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
David X. Yang | Huawei | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Jian Yu |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
Yuchen Guo |  | F1-17, Huawei Base, Bantian, Shenzhen |  | guoyuchen@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Lochan Verma |  | 5775 Morehouse Dr. San Diego, CA USA |  | lverma@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Thomas Derham |  |  |  | 
Mingyue Ji |  |  |  | 
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Feng Jiang |  |  |  | feng1.jiang@intel.com

## Slide 6
Authors (continued):
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hyeyoung Choi | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | hy0117.choi@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Giwon Park |  |  |  | giwon.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Jarkko Kneckt |  |  |  | jkneckt@apple.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan |  | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  |  | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  |  | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  |  | ishihara.koichi@lab.ntt.co.jp
Akira Kishida |  |  |  | kishida.akira@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan |  | yamadaakira@nttdocomo.com
Fujio Watanabe |  | 3240 Hillview Ave, Palo Alto, CA 94304 |  | watanabe@docomoinnovations.com
Haralabos Papadopoulos |  |  |  | hpapadopoulos@docomoinnovations.com

## Slide 9: Authors (continued)
Minho Cheong | NeNewracomwracom | 9008 Research Dr. Irvine, CA 92618 |  | minho.cheong@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Sigurd Schelstraete | Quantenna |  |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quantenna.com

## Slide 10: Authors (continued)

## Slide 11: Outline
OA-CCA (Opportunistic Adaptive CCA)
SR Parameter discussion
Conclusion

## Slide 12: Background
Two modes of Spatial Reuse operation are proposed.
  OBSS_PD threshold: Based on adjustment of the transmit power and the OBSS_PD threshold (adopted in SFD) without using SRP (in SR field)
    allows simple “semi-static” implementation where a STA can set its OBSS_PD (e.g., A STA can determine its TX_PWR based on the path loss to the intended receiver and environment and raise OBSS_PD threshold)
  OA-CCA: Opportunistic Adaptive CCA: based on SR field in SIG A and per link detection
    Adjust transmit power based on specific information of path losses and acceptable receiver interference level to protect the receiver of the on-going transmission
    based on specific link detected, one PPDU at a time
    allow gathering of per-BSS color information to operate on a per color and per SRP basis - this is more accurate and specific to deployment

## Slide 13: Opportunistic Adaptive CCA (OA-CCA)
Opportunistic Adaptive CCA (OA-CCA) is
  SR STA detects a valid OBSS PPDU(s) and retrieves the SR field parameters
  SR STA adjust its transmit power to meet the SR condition before an SR attempt
  under the above situation, the 11ax STA may discard the OBSS PPDU if the SR condition is met,
The SR condition is to ensure the receiving STA of the on-going OBSS transmission is not affected by the SR transmission (i.e., protecting the receiver of the on-going frame exchange) under TBD conditions.
More aggressive SR transmission can be performed (e.g., SR STA only back off the TX power to the exact required level).

## Slide 14: OC-CCA for Trigger frame and UL MU
Trigger frame (from STA2) for UL MU carries SRP (see Slide 20), OBSS Color, and the uplink duration.
  Uplink STA (STA1) copies SRP from trigger frame into SR field
STA3 (SR initiator) can initiate a spatial re-use transmission during the uplink PPDU duration after receiving the SRP
Trigger
Trigger frame carries SRP (not in SIG A) for UL STAs
SR transmission duration
TX_PWR adjusted based on RSSI and SRP
UL MU
UL MU
UL _MU
SIG A: SRP
STA1 (UL STA)
STA2 (AP)
STA3 (SR initiator)
on-going frame
Transmission
STA4 (SR responder)
RSSItrigger frame
Space Loss
STA2 (AP)
STA1s

## Slide 15: Opportunistic Adaptive CCA (OA-CCA) for Trigger Frame and UL MU
STA1 and AP engages in frame exchange and STA3 (SR initiator) is attempting to initiate a SR transmit to STA4 (SR responder)
SR conditions are met when
  STA3 identifies STA1 and STA2(AP) are OBSS
  SR transmission from STA3 satisfies the condition: TX PWRSTA3 – Space LossSTA3->STA2(AP) < Acceptable Receiver Interference LevelSTA2(AP)
STA1
STA2(AP)
STA3 (SR initiator)
on-going frame
Transmission
STA4 (SR responder)
RSSItrigger frame
Space Loss
It can be shown (Slide 20) that SR condition can be simplified to
  TX PowerSTA3 < SRP – RSSItrigger frame@STA3
  where
  SRP = TX PWRSTA2(AP) + Acceptable Receiver Interference levelSTA2(AP)

## Slide 16: SIG A SR Field
Propose to adopt 4 bits for SR Field in SIG A HE-PPDU. For HE PPDU and MU PPDU, the definition of SR field is TBD
  SDF includes Spatial Reuse field in SIG A for HE PPDUs.
  For HE SU PPDU, Spatial Reuse field is TBD (e.g., indication of CCA Level, Interference Level accepted, TX Power)
  SFD contains “SR_allowed” signaling in HE-SIGA to indicate whether SR operation is allowed or not.
  More flag and SR parameter are being proposed.
For Triggered-based HE PPDU, SR field are defined as follows:
    TBD value for SR_Allow Flag, (under TBD restrictions)
    One value is reserved
    The remaining 14 values are used for SRP
      SRP = TX PWRAP + Acceptable Receiver Interference LevelAP
      SR STA shall back-off its TX power based on
        TX PWRSR STA < SRP –RSSItrigger frame
    Note TX PWRAP and TX PWRSR STA are normalized to 20MHz: Transmit power -10*log(BW/BW20M)

## Slide 17: SIG A SR Field (continued)
For HE trigger-based PPDU, 4 SR fields are signaled:
  For 20MHz one SR field corresponding to entire 20MHz (other 3 fields indicate identical values)
  For 40MHz two SR fields for each 20MHz (other 2 fields indicate identical values)
  For 80MHz four SR fields for each 20MHz
  For 160MHz four SR fields for each 40MHz
The exact location of each 20MHz for 80MHz BW is TBD

## Slide 18: Conclusions
OA_CCA is explained
SR parameters (SRP) are introduced
SR Field in SIG A is discussed and proposed numeric values provided.

## Slide 19: Backup Charts

## Slide 20: SR Parameter (SRP) for trigger frame and UL-MU
STA1 transmits to STA2 and STA1’s transmission is detected by STA3 (above the baseline CCA level), STA3 identifies OBSS transmission and tries to initiate a spatial re-use transmission to STA4
For STA3 not to interfere with STA2 reception
  TX PWRSTA3 – Space Loss < Acceptable Receiver Interference levelSTA2(AP)
  where Space loss = TX PWRSTA2(AP) –RSSItrigger frame@STA3
STA1
STA2 (AP)
STA3 (SR initiator)
on-going frame
Transmission
STA4 (SR responder)
Define Type 1 SR Parameter (SRP) as follows:
  SRP = TX PWRSTA2(AP) + Acceptable Receiver Interference levelSTA2(AP)
The required TX power backoff is simplified to
  TX PWRSTA3 < SRP –RSSItrigger frame@STA3
All Power levels normalized to 20MHz : power-10*log(BW/BW20M)
Note: if the STA2 has excess link margin (already at highest MCS), it should add the excess link margin to SRP. This allows STA3 to further raise its transmit power.
RSSItrigger frame
STA3 TX PWR is adjusted to
  SRP –RSSItrigger frame@STA3
Acceptable Receiver Interference levelSTA2 (AP)
Space Loss
Space Loss

## Slide 21: Reference
[1] DCN 14-1187r1 “The Effect of Preamble Error Model on MAC Simulator”, Po-Kai Huang, Intel
[2] DCN 15-367r0 “OBSS preamble detection”, Gwen Barriac , Qualcomm
[3] DCN 14-637 “Spatial Reuse and Coexistence with Legacy Devices” James Wang, Mediatek
[4] DensiFi “Spatial-Reuse Prioritized Channel Access Schemes “, Jianhan Liu, Mediatek
[5] IEEE 802.11ah D4.0 Clause 9.50.4 P317L43 (SR EDCAF procedure)
[6] DensiFi “Intel Spatial Reuse for close links with PHY signaling” Po-Kai Huang
[7] DCN 14-0082r1 “Improved Spatial Reuse Feasibility – Part I” Ron Porat, Broadcom
[8] DCN 14-1224 “Link Aware CCA” Brian Hart, Cisco
[9]DCN 14-637 “Spatial Reuse and Coexistence with Legacy Devices” James Wang, Mediatek
[10] DCN 14-1207r1 “OBSS reuse mechanism which preserves fairness” Imad Jamil, Orange
[11] DCN 14-1199r1 “CCA Study in Residential Scenario - Part 2” Gwen Barriac, Qualcomm
[12] DCN 14-846r0 “CCA Study in Residential Scenario”, Gwen Barriac, Qualcomm
[13] DCN 14-1448r2 “Considerations for Adaptive CCA” Reza Hedayat, Newracom
[14] DCN 15-588r0 “CCA Revisited” Amin Jafarian, Newracom
[15[ DCN 15/1045r0 Dynamic CCA control and TPC Simulation Results with SS1~SS3, Takeshi Itagaki, Sony
[16] DCN

## Slide 22: Straw Poll 1
Propose to include in SFD:
Adopt the following 4 bit SR field (in SIG A) for HE Trigger-Based PPDU
  One TBD value for SR Disallow Flag, (under TBD restrictions)
  One TBD value is reserved
  Remaining 14 values for SRP
    SRP = TX PWRAP + Acceptable Receiver Interference LevelAP
    SR STA shall back-off its TX power based on
      TX PWRSR STA < SRP –RSSItrigger frame@SR STA
Note TX PWRAP and TX PWRSR STA are normalized to 20MHz: Transmit power -10*log(BW/BW20M)
  Yes
  No
  Abstain

## Slide 23: Straw Poll 2
Propose to include in SFD:
For HE trigger-based PPDU, 4 SR fields are signaled:
  For 20MHz one SR field corresponding to entire 20MHz (other 3 fields indicate identical values)
  For 40MHz two SR fields for each 20MHz (other 2 fields indicate identical values)
  For 80MHz four SR fields for each 20MHz
  For 160MHz four SR fields for each 40MHz
The exact location of each 20MHz for 80MHz BW is TBD
    Yes
    No
    Abstain

## Slide 24: Straw Poll 3
Propose to include in SFD
Adopting 4 bits for SR field in SIG A of HE SU-PPDU and HE MU-PPDU, the SR field definition is TBD
  Yes
  No
  Abstain