## Slide 1: Stacked Architecture Discussion
Date: 2016-05-17
Authors:

## Slide 2: Abstract
This presentation walks through some discussion on why, and how, we use a “stacked” architecture model in 802.11.
THIS VERSION IS A WORK IN PROGRESS, NOT COMPLETE

## Slide 3: Start with a simple problem, and view: two peer entities are communicating …
Entity of type X
Peer entities communicate by exchanging protocol. Logically, this happens directly between them …
Entity of type X
Protocol

## Slide 4: Why are these entities communicating?
Entity of type X
The model is that (other than the Application Layer), the layers do this, for the purpose of providing a Service to the layer above.
Entity of type X
Protocol
Service
Service
Upper
(Layer)
Entity
Upper
(Layer)
Entity

## Slide 5: But, of course, they don’t really communicate directly (other than the PHY)
Entity of type X
The model is that (other than the Physical Layer), the layers communicate by using services of the layer below.
Entity of type X
(Logical) Protocol Flow
Service
Service
Service
Service
Actual Protocol Flow

## Slide 6: OK, this works well for Layers. What about within a layer?

## Slide 7: It seems to work for our “stack”, at least for “end nodes”

## Slide 8: But, intermediate nodes are less intuitive

## Slide 9: Or, a more complete, but less detailed view:
Distribution System (DS)
MAC
PHY
MAC
PHY
MAC
PHY
AP STA 1
Non-AP STAs
MAC
PHY
AP STA 2
unspecified
AP
AP
MAC
PHY
Non-AP STAs
Upper
Upper
Upper

## Slide 10: Then, there’s the Baggy Pants View (Note the diagonal interfaces)

## Slide 11: And, an alternative view, being suggested
Distribution System (DS)
unspecified
MAC
PHY
MAC
PHY
MAC
PHY
DSCF
MAC
PHY
MAC
PHY
This builds on an idea that Services could be shown horizontally.
DSCF