## Slide 1: 11ax Beamformee Capabilities
Date: 2016-07-25
Authors:

## Slide 2: Authors (continued)

## Slide 3: Authors (continued)

## Slide 4: Authors (continued)

## Slide 5: Authors (continued)
Authors (continued)

## Slide 6: Authors (continued)

## Slide 7: Authors (continued)

## Slide 8: Authors (continued)

## Slide 9: Authors (continued)

## Slide 10: Authors (continued)

## Slide 11: On the Feedback Parameters
Current Spec Allows the following:
  Ng: Ng=4 or 16
  CB Size: (9,7) (7,5) for MU-Type; (6,4) (4,2) for SU-Type
Prefer to reduce the number of choices at STA:
  Ng=16 is optional at beamformee for both SU-type and MU-type feedbacks, define a capability bit for Ng=16 feedback capable for MU-type and SU-type feedbacks respectively.
  CB size (7,5) for MU-type feedback and CB size (4,2) for SU-type feedback are optional at beamformee, define a capability bit for these two cases respectively.

## Slide 12: Discussions
Ng=16 is almost not usable for MU-Type feedback due to poor performance;
  While Ng=16 performs ok for SU-type.
Typically vendors will do larger CB size to guarantee the best performances in different scenarios

## Slide 13: Ng for SU (80MHz, 4x2-2SS, MCS9)

## Slide 14: Ng for MU (80MHz, 4x[1,1]SS, MCS7)

## Slide 15: Proposal
Propose the following statements on Ng and CB size in 11ax sounding feedbacks.
  Ng=16 is optional at beamformee for both SU-type and MU-type feedbacks, define a capability bit for Ng=16 feedback capable in MU-type, and a capability bit for Ng=16 feedback capable in SU-type.
  CB size (7,5) for MU-type feedback and CB size (4,2) for SU-type feedback are optional at beamformee, define a capability bit for CB (7,5) for MU-type feedback, and a capability bit for SU-type feedback.

## Slide 16: Straw Poll 1
Do you agree to adopt the spec text changes as shown in doc 11/16-0897r1?