## Slide 1: Gamma Phase Rotation for HE PPDU
Date: 2016-07-25
Authors:
Name | Affiliation | Address | Phone | Email
Yujin Noh | Newracom | 9008 Research Dr. Irvine, CA 92618 |  | yujin.noh@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Minho Cheong |  |  |  | minho.cheong@newracom.com
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Thomas Derham |  |  |  | 
Mingyue Ji |  |  |  | 

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Feng Jiang |  |  |  | feng1.jiang@intel.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Lochan Verma |  | 5775 Morehouse Dr. San Diego, CA USA |  | lverma@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 6: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Jarkko Kneckt |  |  |  | jkneckt@apple.com
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
David X. Yang | Huawei | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Jian Yu |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
Yuchen Guo |  | F1-17, Huawei Base, Bantian, Shenzhen |  | guoyuchen@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan | +81 46 859 3135 | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  | +81 46 859 5097 | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  | +81 46 859 5107 | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  | +81 46 859 3494 | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  | +81 46 859 4233 | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  | +81 46 859 4222 | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan | +81 46 840 3759 | yamadaakira@nttdocomo.com

## Slide 10: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Sigurd Schelstraete | Quantenna |  |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quantenna.com
Narendar Madhavan | Toshiba |  |  | narendar.madhavan@toshiba.co.jp
Masahiro Sekiya |  |  |  | 
Toshihisa Nabetani |  |  |  | 
Tsuguhide Aoki |  |  |  | 
Tomoko Adachi |  |  |  | 
Kentaro Taniguchi |  |  |  | 
Daisuke Taki |  |  |  | 
Koji Horisaki |  |  |  | 
David Halls |  |  |  | 
Filippo Tosato |  |  |  | 
Zubeir Bocus |  |  |  | 
Fengming Cao |  |  |  | 

## Slide 11: Background (1/2)
The non-contiguous channel bonding will be supported in 802.11ax by: [PHY Motion 125, January 2016]
  • Transmitting using OFDMA PPDU format by nulling the tones of one or more secondary channels in 80 MHz and 160 (80+80) MHz;
  • Modes for non-contiguous channel bonding are TBD;
    TBD would be resolved in [1]
  • Non-contiguous channels within primary or secondary 80 MHz only exists at AP side.
UL OFDMA pre-HE-STF preamble(s) are sent on 20 MHz channel(s) where the HE modulated fields are located. [PHY Motion 154, March 2016]

## Slide 12: Background (2/2)
  Terminology, “Preamble puncturing”, is used in this submission is used to indicate the pre-HE-STF preamble on 20MHz channel(s) which are not sent when the HE modulated field is not present.
We analyze PAPR of the HE PPDU with preamble puncturing
  L-STF, L-LTF, L-SIG and HE-SIG-A OFDM symbols become simple repetition when some 20MHz segments are punctured in 80/160MHz.
  High PAPR signals require higher DAC resolution and may require transmit power backoff (i.e. coverage loss)

## Slide 13: Simulation assumption (1/2)
Gamma value notation [ A, B, C, D ]
  Values represent tested gamma phase rotation values applied to each 20MHz of 80MHz.
  Zero corresponds to punctured 20MHz segments.
    Example 1) For a 80 MHz channel with an UL OFDMA RU allocation of 26 to 242 tones on the first 20 MHz, ϒ80 = [1 0 0 0].
    Example 2) For a 80MHz channel in DL OFDMA where the second 20MHz segment is punctured, ϒ80 = [1 0 -1 -1].

## Slide 14: Simulation assumption (2/2)
UL OFDMA
  Tone(s) of RUs with orange color overlaps the guard tones of the first 20 MHz channel.
  In those cases, assigned RU in OFDMA on the 80 MHz channel requires a 40 MHz preamble.
RU-26 requiring a 80C preamble
RUs requiring a 80L preamble
RUs requiring a 80R preamble
80L (1st and 2nd 20MHz channels)
80R (3rd and 4th 20MHz channels)
80C (2nd and 3rd 20MHz channels)

## Slide 15: Phase Rotations Options for Preamble Puncturing
Option 1) optimized phase rotation for each puncture pattern.
  Challenging to define a phase rotation sequences for each puncture pattern.
  Lowest PAPR (results shown in the Appendix)
Option 2) one phase rotation sequence for all cases
  minimize the worst case PAPR of any preamble puncture pattern
  Limited PAPR reduction benefit in some preamble puncture patterns.

## Slide 16: Phase Rotations for 80MHz with Preamble Puncturing (DL OFDMA)
80 MHz 11ac Gammas seem to work pretty well
  Only ~1.5 dB difference in Max PAPR compared to optimized results
  Given the limited preamble puncture patterns for 80MHz, little difference between option 1 and 2
    0.3dB difference between Option 1 and Option 2.
    Option 1 results shown in the appendix.
  Option 2) Even with good candidates, the half of preamble puncturing patterns still keep high max PAPR.
HE-SIG-A PAPR (99.9% PAPR) |  |  |  | 
Gamma ϒ80 | Puncture Patterns |  | Median | Max
[1 -1 -1 -1] | 80MHz | [1 -1 -1 -1] | 8.80 | 12.87
 | 80MHz With Preamble Puncturing | [0 -1 -1 -1] | 10.79 | 15.39
 |  | [1 0 -1 -1] | 10.02 | 14.03
 |  | [1 -1 0 -1] | 10.54 | 15.00
 |  | [1 -1 -1 0] | 8.66 | 12.40
HE-SIG-A PAPR (99.9% PAPR) |  |  |  | 
Gamma ϒ80 | Puncture Patterns |  | Median | Max
[1 1 -1 -1] | 80MHz With Preamble Puncturing | [0 1 -1 -1] | 8.66 | 12.40
 |  | [1 0 -1 -1] | 10.02 | 14.03
 |  | [1 1 0 -1] | 10.02 | 14.03
 |  | [1 1 -1 0] | 8.66 | 12.40
[1 -1 -1 1] | 80MHz With Preamble Puncturing | [0 -1 -1 1] | 8.66 | 12.40
 |  | [1 0 -1 1] | 9.94 | 14.06
 |  | [1 -1 0 1] | 9.94 | 14.06
 |  | [1 -1 -1 0] | 8.66 | 12.40
Optimized Results
11ax Gamma

## Slide 17: Phase Rotations for 160MHz with Preamble Puncturing (DL OFDMA)
Again, 160 MHz 11ac Gammas seem to work pretty well
  Only ~1 dB difference in Max PAPR compared to optimized results
  Option 1)
    Maximum PAPR 14.68 dB
    Requires 22 unique gamma sequences
  Option 2)
    Even with good candidates, maximum PAPR is 16.23 dB which improves only 1dB max PAPR.
HE-SIG-A PAPR (99.9% PAPR) |  |  | 
Gamma ϒ160 | Puncture patterns | Median | Max
[1 1 -1 -1 1 1 -1 -1] | 160MHz With Preamble Puncturing | 10.68 | 16.23
[1 -1 -1 1 1 -1 -1 1] |  | 10.68 | 16.23
[1 1 -1 -1 1 1 -1 1] |  | 10.68 | 16.23
[1 -1 -1 1 1 -1 -1 -1] |  | 10.68 | 16.23
HE-SIG-A PAPR (99.9% PAPR) |  |  | 
Gamma ϒ160 | Puncture Patterns | Median | Max
[1 -1 -1 -1 1 -1 -1 -1] | 160MHz | 10.14 | 13.81
 | 160MHz With Preamble Puncturing | 10.79 | 15.39
11ax Gamma
Optimized Results

## Slide 18: Phase Rotations for 40/80/160MHz with Preamble Puncturing (UL OFDMA) (1/2)
Gamma | L-LTF (BPSK) | HE-SIG-A (BPSK) | HE-DATA (QAM) | RU allocation (# tones)
ϒ40 = [1 j] | 5.79 dB | 9.49 dB | 8.75 dB | 484
ϒ40 = [1 0] ϒ40 = [ 0 j] | 3.17 dB | 6.64 dB | 6.51 to 8.31 dB | 26 to 242
ϒ80 = [1 -1 -1 -1] | 5.40 dB | 8.78 dB | 9.16 dB | 996
ϒ80 = [1 0 0 0], [ 0 -1 0 0], [ 0 0 -1 0] and ϒ80 = [ 0 0 0 -1] | 3.17 dB | 6.64 dB | 6.51 to 8.31 dB | 26 to 242
Median PAPR
Considering preamble puncturing patterns in UL OFDMA, only 11ac Gammas is tested because its PAPR is likely to be similar to PAPRs of modified Gammas.
40MHz and 160 MHz 11ac Gammas are good enough.
80 MHz 11ac Gamma is optimal.

## Slide 19: Phase Rotations for 40/80/160MHz with Preamble Puncturing (UL OFDMA) (2/2)
Gamma | L-LTF (BPSK) | HE-SIG-A (BPSK) | HE-DATA (QAM) | RU allocation (# tones)
ϒ80 = [1 -1 0 0] | 6.15 dB | 9.02 dB | 6.51 to 8.74 dB | 26 to 484
ϒ80 = [ 0 0 -1 -1] | 6.18 dB | 9.12 dB | 6.51 to 8.74 dB | 26 to 484
ϒ80 = [ 0 -1 -1 0] | 6.18 dB | 9.19 dB | 6.69 dB | 26 (center)
ϒ160 = [1 -1 -1 -1 1 -1 -1 -1] | 6.47 dB | 10.20 dB | 9.53 dB | 2*996
ϒ160 = [1 -1 -1 -1 0 0 0 0] ϒ160 = [ 0 0 0 0 1 -1 -1 -1] | 5.40 dB | 8.78 dB | 9.16 dB | 996
Median PAPR
RED indicate a PAPR greater than QAM DATA PAPR
Gamma elements are the sign of each 20 MHz segment

## Slide 20: Conclusion
To reuse 11ac Gamma phase rotation to be applied to preamble puncturing is good enough in UL and DL OFDMA.
  Modified Gamma doesn’t give enough PAPR benefit to cover different preamble puncturing modes at the cost of implementation change.
Gamma phase rotation on the full BW is punctured depending on which the pre-HE-STF is sent.
  Simple and straightforward way to implement phase rotation
For a 20 MHz
For a 40 MHz
For a 80 MHz
For a 160 MHz

## Slide 21: Strawpoll #1
Do you agree to adopt the 11ac gamma phase rotation values for gamma rotation values for pre-HE-STF preamble of the HE PPDU. 11ac gamma phase rotation on the full BW is punctured based on 20MHz channels where the pre-HE-STF is sent?
  Note: If TG agrees the strawpoll, we should adopt the comment resolution for CID 525 and CID 293 in 11-16/0937r2.
Y/N/A

## Slide 22: reference
[1] 111-16/0903r0 BW Field in HE-MU Format

## Slide 23: Appendix

## Slide 24: Option 1 for 80MHz
CDF of PAPR with Option 1
99.9% PAPR |  |  |  |  |  | 
Gamma phase rotation | Puncture pattern |  |  |  | Median (dB) | Max (dB)
1 1 -1 -1 | 0 | 1 | -1 | -1 | 8.65 | 12.40
1 -j 1 -j | 1 | 0 | 1 | -j | 10.06 | 13.75
1 -j 1 -j | 1 | -j | 0 | 1 | 10.06 | 13.75
1 1 -1 -1 | 1 | 1 | -1 | 0 | 8.66 | 12.40
Two phase rotation sequences [ 1 1 -1 -1] and [1 -j 1 -j] are applied to provide the lowest max PAPR in 80MHz with preamble puncturing

## Slide 25: Option 1 for 160MHz
99.9% PAPR |  |  |  |  |  |  |  |  | 
Gamma phase rotation 1 -1 -1 -1 1 -1 -1 -1 | Puncture pattern |  |  |  |  |  |  |  | Max (dB)
 | 1 | -1 | 0 | -1 | 1 | -1 | 0 | -1 | 17.23
 | 1 | -1 | 0 | -1 | 1 | -1 | 0 | 0 | 17.23
 | 0 | -1 | -1 | -1 | 0 | -1 | -1 | -1 | 17.13
 | 0 | -1 | -1 | -1 | 0 | -1 | -1 | 0 | 17.13
 | 0 | 0 | -1 | -1 | 1 | 0 | 0 | -1 | 12.40
 | 0 | 0 | -1 | -1 | 1 | 0 | 0 | 0 | 12.40
22 unique phase rotation sequences are required to provide the lowest max PAPR in 160MHz with preamble puncturing
…
99.9% PAPR |  |  |  |  |  |  |  |  | 
Gamma phase rotation | Puncture pattern |  |  |  |  |  |  |  | Max (dB)
1 1 1 -1 -1 1 1 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 14.68
 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 14.45
 | 0 | 0 | 0 | -1 | -1 | 0 | 1 | 1 | 14.03
 | 1 | 0 | 1 | -1 | 0 | 1 | 0 | 1 | 13.15
-1 1 -1 -1 1 1 1 1 | -1 | 1 | -1 | -1 | 0 | 1 | 1 | 1 | 12.38
 | -1 | 1 | -1 | -1 | 1 | 1 | 1 | 0 | 11.94
…
[Optimized phase rotation sequences
for each preamble puncturing pattern ]
Max (Max PAPR)
Min (Max PAPR)

## Slide 26: HE-QAM Data PAPR