## Slide 1: Discussions on Partial BSS Color
Date: 2016-07-25
Authors:

## Slide 2: Introduction
AID assignment rule has been defined in 11ax [1].
  AID assigned by the rule is reflected in Partial AID (PAID) field in VHT PPDU, especially for SU DL case.
  The part of the PAID becomes the partial BSS color.
By using PAID field, a STA can determine whether the VHT PPDU is intra-BSS.
  Spatial reuse transmission is possible.
For certain BSSIDs, one BSS may have two partial BSS color values following the rule.

## Slide 3: Recap: AID Assignment Rule (1) [2]
AP assigns AIDs to associated STAs according to
Settings for PAID field in VHT PPDU
N = 1, 2, 3 or 4
BCB: (Partial) BSS Color Bits
A TBD IE contains N and BCB.
 Uplink
 Downlink

## Slide 4: Recap: AID Assignment Rule (2) [2]
Then the PAID(8−N+1:8) automatically becomes the partial BSS color.
Spatial reuse transmission is possible on the VHT PPDU by using PAID field.
* PAID for DL
* AID assignment rule
PAID = (dec(AID[0:8]) + dec(BSSID[44:47] XOR BSSID[40:43]) * 25) mod 29
AID[8−N+1:8] = bin[(dec(BCB[0:N−1])
+ dec(BSSID[47−N+1:47] XOR BSSID[43−N+1:43])) mod 2N, N]

## Slide 5: Ambiguity in PAID Field
One BSS may have two PAID[8−N+1:8] values.
  When the addition is performed,
    For N < 4, 1 can be rounded up from the bit position (8−N+1−1)
      For example, N = 3, if B5 of y is 1,
        B5 of AID is 0 or 1  0: No rounding / 1: Rounding  Two PAID[6:8] values
    For N = 4, there is no rounding from B4 since y[0:4] is always b00000.
      No ambiguity
* PAID for DL
* AID assignment rule
PAID = (dec(AID[0:8]) + dec(BSSID[44:47] XOR BSSID[40:43]) * 25) mod 29
AID[8−N+1:8] = bin[(dec(BCB[0:N−1])
+ dec(BSSID[47−N+1:47] XOR BSSID[43−N+1:43])) mod 2N, N]
x
y
B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
x
y
PAID
+
B8 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
00000 due to * 25
N-bit assigned by the rule
Partial BSS color (N-bit)
Higher N bits of x only depend on the BSS.
y only depends on the BSS.
mod 29
(Cutting off B9)
z
z

## Slide 6: Ambiguity Example (Details in Appendix)
Frame carrying TBD IE
VHT STA
AID[0:8]
b001100000
VHT PPDU
HE STA
AID[0:8]
b001000011
TBD IE
carrying N and BCB
N = 3
BCB[0:N−1] = b110
HE AP
BSSID
xx:xx:xx:xx:xx:5B
HE STA calculates BSS’s PAID[8−N+1:8]
PAID
Including PAID
PAID
AID[6:8] = b001
* PAID for DL
* AID assignment rule
PAID = (dec(AID[0:8]) + dec(BSSID[44:47] XOR BSSID[40:43]) * 25) mod 29
AID[8−N+1:8] = bin[(dec(BCB[0:N−1])
+ dec(BSSID[47−N+1:47] XOR BSSID[43−N+1:43])) mod 2N, N]
Different PAID[8−N+1:8]
: If the HE STA compares PAID[8−N+1:8] values, an intra-BSS frame is identified as inter-BSS.
Spatial Reuse Transmission
Interference
AP cannot receive a PPDU.
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1

## Slide 7: Discussions
Due to the ambiguity using PAID for partial BSS color, an HE STA may identify an intra-BSS VHT PPDU as inter-BSS.
  Then, the HE STA may transmit a packet using OBSS PD level which interferes the intra-BSS PPDU.
The spec should further consider the BSS color ambiguity of PAID in VHT PPDU when Partial BSS Color Length N is less than 4.

## Slide 8: References
[1] 11-15/0132r17 Specification Framework for TGax
[2] 11-16/0364r3 AID Assign Rule Based on BSS Color and HE Operation Element

## Slide 9: Appendix: Detailed Example
Frame carrying TBD IE
VHT STA
AID[0:8]
b001100000
VHT PPDU
HE STA
AID[0:8]
b001000011
TBD IE
carrying N and BCB
N = 3
BCB[0:N−1] = b110
HE AP
BSSID
xx:xx:xx:xx:xx:5B
HE STA calculates BSS’s PAID[8−N+1:8]
x
y
PAID
+
mod 29
z
Including PAID
0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
x
y
PAID
+
mod 29
z
B47 | B46 | B45 | B44 | B43 | B42 | B41 | B40
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1
AID[6:8] = bin[(6 + dec(b101 XOR 110)) mod 23, 3]
= bin[(6 + dec(b011)) mod 23, 3]
= bin[9 mod 23, 3] = bin[1, 3] = b001
* PAID for DL
* AID assignment rule
PAID = (dec(AID[0:8]) + dec(BSSID[44:47] XOR BSSID[40:43]) * 25) mod 29
AID[8−N+1:8] = bin[(dec(BCB[0:N−1])
+ dec(BSSID[47−N+1:47] XOR BSSID[43−N+1:43])) mod 2N, N]
x
y
z
Different PAID[8−N+1:8]
: If the HE STA compares PAID[8−N+1:8] values, an intra-BSS frame is identified as inter-BSS.
Spatial Reuse Transmission
Interference
AP cannot receive a PPDU.
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1