## Slide 1: Discussions on SR Fields in HE Trigger-based PPDU
Date: 2016-07-25
Authors:

## Slide 2: Introduction
HE-SIG-A includes Spatial Reuse (SR) field(s) [1].
For HE-SIG-A in HE trigger-based PPDU [2],
  4 SR fields are signaled.
  In 160 MHz UL MU operation, each SR field corresponds to each 40 MHz band.
  SR field may represent SRP (SR parameter) value.
SRP in SR field is used for OA-CCA (Opportunistic Adaptive-CCA) of an inter-BSS STA during UL MU transmission [3].
  It is required for the inter-BSS STA to find the proper SR field from multiple SR fields.
This contribution addresses issues when a STA performs OA-CCA on 160 MHz UL MU transmission of an inter-BSS.

## Slide 3: Recap: OA-CCA [3]
Spatial reuse operation based on SR field in HE-SIG-A
  STA3 (SR initiator) can initiate a spatial reuse transmission during the uplink PPDU duration after receiving the SRP
  STA3 adjusts its transmit power not to interfere with the reception of the UL MU Data.
    TXPWRSTA3 < SRP – RSSItrigger frame@STA3
SRP = TXPWRSTA2(AP) + AcceptableReceiverInterferenceSTA2(AP)
Trigger
Trigger frame carries SRP (not in SIG A) for UL STAs
SR transmission duration
TX_PWR adjusted based on RSSI and SRP
UL MU
UL MU
UL _MU
SIG A: SRP
STA1 (UL STA)
STA2 (AP)
STA3 (SR initiator)
on-going frame
Transmission
STA4 (SR responder)
RSSItrigger frame
Space Loss
STA2 (AP)
STA1s

## Slide 4: Establishing a BSS
Contiguous 20, 40, 80, and 160 MHz BSS
  The set of valid operating channel numbers by regulatory domain is defined in Annex E of the specification [4].
  When a STA detects an inter-BSS frame in any 20 MHz channel of the BSS, the STA can recognize the occupied band by the frame with BW field.
Non-contiguous 160 MHz (80+80 MHz) BSS
  Any two 80 MHz channels constitutes the BSS (with a certain condition).
  An inter-BSS STA is hard to know the whole composition of the BSS.
(Note) Without a specific signaling, an inter-BSS STA cannot differentiate between 160 and 80+80 MHz BSSs.

## Slide 5: Identifying SR Fields
To utilize OA-CCA, an inter-BSS STA (STA2) is required to match the observed band to the corresponding SR field(s)
  It is difficult for an inter-BSS STA (STA2) to find the corresponding SR field(s) only w/o the additional info.
    An inter-BSS STA does not know where the another 80 MHz exists in.
Field | Description
Spatial Reuse 1 | 40 MHz channel 1
Spatial Reuse 2 | 40 MHz channel 2
Spatial Reuse 3 | 40 MHz channel 3
Spatial Reuse 4 | 40 MHz channel 4
… | HE-SIG-A | …
 | HE-SIG-A | 
 | HE-SIG-A | 
 | HE-SIG-A | 
Contiguous or Non-contiguous
Observed band
(by STA2)
Which of SR fields corresponds to the observed band?
* SR fields in HE-SIG-A
* HE trigger-based PPDU
AP1
(BSS1)
STA1
(BSS1)
STA2
(BSS2)
… | HE-SIG-A | …
 | HE-SIG-A | 
 | HE-SIG-A | 
 | HE-SIG-A | 
STA1
(BSS1)
STA1
(BSS1)

## Slide 6: Contiguous 160 MHz Case
There is a contiguous 160 MHz channel formation rule.
If an inter-BSS STA realize that UL MU transmission is on a contiguous 160 MHz channel, the inter-BSS STA can utilize any of 4 SR fields properly.
  Indicating a contiguous 160 MHz BW would be helpful.
    For example, in HE-SIG-A
… | HE-SIG-A | …
 | HE-SIG-A | 
 | HE-SIG-A | 
 | HE-SIG-A | 
Contiguous
* HE trigger-based PPDU
… | HE-SIG-A | …
 | HE-SIG-A | 
 | HE-SIG-A | 
 | HE-SIG-A | 
40 MHz channel 1
40 MHz channel 2
40 MHz channel 3
40 MHz channel 4
160 MHz channel:
The rule defines the channel.

## Slide 7: Non-contiguous 160 MHz Case
Even if it is indicated whether a channel is contiguous/non-contiguous, an inter-BSS STA still cannot find the proper SR field for non-contiguous 160 MHz case.
Since there is a 80 MHz channel formation rule, an inter-BSS STA has ambiguity whether the observed 20 or 40 MHz channel belongs to
  40 MHz channel 1 or 3
  40 MHz channel 2 or 4
… | HE-SIG-A | …
 | HE-SIG-A | 
 | HE-SIG-A | 
 | HE-SIG-A | 
Non-contiguous
* HE trigger-based PPDU
… | HE-SIG-A | …
 | HE-SIG-A | 
 | HE-SIG-A | 
 | HE-SIG-A | 
40 MHz channel 1
40 MHz channel 2
40 MHz channel 3
40 MHz channel 4
80 MHz channel 1:
The rule defines the channel.
80 MHz channel 2:
The rule defines the channel.

## Slide 8: Possible Solutions for Non-contiguous 160 MHz Case
Tx-side solution
  SR fields include the minimum value.
Field | Description
Spatial Reuse 1 | min(SRP_40_1, SRP_40_3)
Spatial Reuse 2 | min(SRP_40_2, SRP_40_4)
Spatial Reuse 3 | min(SRP_40_1, SRP_40_3)
Spatial Reuse 4 | min(SRP_40_2, SRP_40_4)
* SR fields in HE-SIG-A
Rx-side solution
  An inter-BSS STA uses the minimum value.
* SRP_40_x: SRP value which corresponds to 40 MHz channel x
Other solutions
  Obtaining and saving operation information of neighboring BSSs with BSS color
    For example, from Beacon frame
  Including operating channel information in HE-SIG-A
Field | Description
Spatial Reuse 1 | SRP_40_1
Spatial Reuse 2 | SRP_40_2
Spatial Reuse 3 | SRP_40_3
Spatial Reuse 4 | SRP_40_4
* SR fields in HE-SIG-A
A STA uses the minimum.
A STA uses the minimum.

## Slide 9: Conclusions
When an inter-BSS STA performs OA-CCA on 160/80+80 MHz UL MU transmission, the STA needs to find the proper SR field(s).
When the STA uses the inappropriate SRP value that makes TXPWR exceed the limit, HE trigger-based PPDU may fail.
Spec should define the operation or HE-SIG-A contents to be possible to perform OA-CCA not interfering to 160 MHz UL MU transmission.

## Slide 10: References
[1] Draft P802.11ax D0.2
[2] 11-15/0132r17 Specification Framework for TGax
[3] 11-16/0699r1 Spatial Re-Use OA-CCA Mode and SR Field Discussion
[4] Draft P802.11REVmc D5.2

## Slide 11: Straw Poll
  Do you support the following text?
  When a STA receives an inter-BSS HE trigger-based PPDU with its BW subfield set to 80+80 MHz, the STA shall use min(SR Field 1, SR Field 3) or min(SR Field 2, SR Field 4).
  - min(A, B) is the minimum value between A and B.
  Y
  N
  A