## Slide 1: Mandatory ways to solicit UL MU ACK
Date: 2016-07-22
Authors:

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Albert Van Zelst | Qualcomm | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alice Chen |  | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
Rolf De Vegt |  | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com

## Slide 3
Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Thomas Derham |  |  |  | 
Mingyue Ji |  |  |  | 

## Slide 4: Authors (continued)
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 6: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Jarkko Kneckt |  |  |  | jkneckt@apple.com
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
David X. Yang | Huawei | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Jian Yu |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
Yuchen Guo |  | F1-17, Huawei Base, Bantian, Shenzhen |  | guoyuchen@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan | +81 46 859 3135 | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  | +81 46 859 5097 | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  | +81 46 859 5107 | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  | +81 46 859 3494 | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  | +81 46 859 4233 | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  | +81 46 859 4222 | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan | +81 46 840 3759 | yamadaakira@nttdocomo.com

## Slide 10: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Sigurd Schelstraete | Quantenna |  |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quantenna.com
Minho Cheong | Newracom | 9008 Research Dr. Irvine, CA 92618 |  | minho.cheong@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com

## Slide 12: Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Eldad Perahia |  |  |  | eldad.perahia@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Rongzhen Yang |  |  |  | rongzhen.yang@intel.com
Laurent cariou |  |  |  | laurent.cariou@intel.com

## Slide 13: Authors (continued)

## Slide 14: Authors (continued)
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com

## Slide 15: Authors (continued)

## Slide 16: Authors (continued)
Bo SunBo Sun | ZTE | #9 Wuxing duan, Xifeng Rd, Xi’an, China |  | SubSub.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | Yao.ke5@zte.com.cn
Weimin Xing |  |  |  | Xing.weimin@zte.com.cn

## Slide 17: Authors (continued)

## Slide 18: Authors (continued)

## Slide 19: Authors (continued)

## Slide 20: Overview
There are multiple ways to solicit a UL MU ACK/BA for DL MU transmission.
Goal: To facilitate discussion on which options should be mandatory for IEEE 802.11.ax
Raja Banerjea, Qualcomm, et. al.

## Slide 21: DL MU Sequences with UL MU ACK
DL MU PPDU with Basic Trigger followed by ACK/BA
DL MU PPDU with UL MU Response A-Control followed by ACK/BA
DL MU PPDU followed by (MU) BAR followed by ACK/BA
DL MU PPDU followed by DL MU PPDU with Trigger and BAR followed by ACK/BA
DL MU PPDU with Basic Trigger & BAR followed by ACK/BA
Details on each of the sequence in the following slides
Raja Banerjea, Qualcomm, et. al.

## Slide 22: DL MU PPDU with Trigger
Requirement in SFD/Baseline Spec:
  A unicast Trigger frame for a single user may be included in an A-MPDU for that user in the DL MU PPDU that precedes the UL MU transmission by TBD IFS. [MAC Motion 20, July 16, 2015, see [89]]
  Ack Policy field in a frame soliciting an immediate response is set to 00 (Normal Ack or Implicit Block Ack Request ) if the immediate response is carried in SU PPDU, or it is set to 01 (Trigger based UL MU Ack) if the immediate response is carried in MU PPDU.
Advantage: Simplified design, low overhead
Disadvantage: Requires repetition of Basic Trigger to improve robustness (single point of failure), Does not allow for EIFS reset at legacy STA
STA 1 (Basic Trigger + AMPDU)
STA 2 ( Basic Trigger + AMPDU)
STA 3 (Basic Trigger + AMPDU)
STA 4 (Basic Trigger + AMPDU)
01 (Trigger based UL MU ACK)
ACK/BA/M-BA (STA1)
ACK/BA/M-BA (STA4)
ACK/BA/M-BA (STA2)
ACK/BA/M-BA (STA3)
SIFS
DL
UL
Raja Banerjea, Qualcomm, et. al.

## Slide 23: DL MU PPDU with UL MU Response A-Control
Requirement in SFD/Baseline Spec:
  HE A-Control field for UL acknowledgement is optional in RX.
  Ack Policy field in a frame soliciting an immediate response is set to 00 (Normal Ack or Implicit Block Ack Request ) if the immediate response is carried in SU PPDU, or it is set to 01 (Trigger based UL MU Ack) if the immediate response is carried in MU PPDU.
Advantage: lower overhead, robust (no single point of failure)
Disadvantage: Optional in SFD, different trigger frame, Does not allow for EIFS reset at legacy STA
STA 1 (ULMURSP(A-Control) + AMPDU)
STA 2 (ULMURSP(A-Control) + AMPDU)
STA3 (ULMURSP(A-Control) + AMPDU)
STA4 (ULMURSP(A-Control) + AMPDU)
01 (Trigger based UL MU ACK)
ACK/BA/M-BA (STA1)
ACK/BA/M-BA (STA4)
ACK/BA/M-BA (STA2)
ACK/BA/M-BA (STA3)
SIFS
DL
UL
Raja Banerjea, Qualcomm, et. al.

## Slide 24: DL MU PPDU followed by MU-BAR
Requirement in SFD/Baseline Spec:
  The spec shall define a MU-BAR frame to solicit BA/ACKs from multiple STAs in UL MU transmissions. [MU Motion 13, September 17, 2015, see [171]]
  The recipient of a MU-BAR frame can transmit other data or management frame in addition to BA/ACK frame if it does not exceed the indicated UL MU duration. [MAC Motion 58, January 2016, see [113]]
Advantage: Simplified design, Robust, Allows for EIFS reset, Sequence required if BA is lost in the UL
Disadvantage: Not the lowest overhead
STA 1 (AMPDU)
STA 2 ( AMPDU)
STA 3 ( AMPDU)
STA 4 ( AMPDU)
Block ACK or No Ack
MU - BAR
(STA1,STA2, STA3, STA4)
(legacy duplicate/ HE )
SIFS
ACK/BA/M-BA (STA1)
ACK/BA/M-BA (STA4)
ACK/BA/M-BA (STA2)
ACK/BA/M-BA (STA3)
SIFS
DL
DL
UL
Raja Banerjea, Qualcomm, et. al.

## Slide 25: DL MU PPDU followed by DL MU PPDU with Trigger and BAR
Requirement in SFD/Baseline Spec:
  None
Advantage: Sequence required if BA is lost in the UL, does not need a new MU-BAR
Disadvantage: highest overhead, Does not allow for EIFS reset at legacy STA, need to clarify to differentiate between UL MU/SU ACK, do we need to sent multiple BAR for multiple TIDs?
STA 1 (AMPDU)
STA 2 (AMPDU)
STA 3 (AMPDU)
STA 4 (AMPDU)
Block ACK
SIFS
ACK/BA/M-BA (STA1)
ACK/BA/M-BA (STA4)
ACK/BA/M-BA (STA2)
ACK/BA/M-BA (STA3)
SIFS
Basic Trigger + BAR (STA1)
Basic Trigger + BAR (STA4)
Basic Trigger + BAR (STA2)
Basic Trigger + BAR (STA3)
DL
DL
UL
Raja Banerjea, Qualcomm, et. al.

## Slide 26: DL MU PPDU with embedded Basic Trigger and BAR followed by ACK/BA
Not currently allowed in the baseline
STA 1 (Basic Trigger + AMPDU + BAR)
STA 2 ( Basic Trigger + AMPDU + BAR)
STA 3 (Basic Trigger + AMPDU + BAR)
STA 4 (Basic Trigger + AMPDU + BAR)
Block ACK/01
ACK/BA/M-BA (STA1)
ACK/BA/M-BA (STA4)
ACK/BA/M-BA (STA2)
ACK/BA/M-BA (STA3)
SIFS
DL
UL
Raja Banerjea, Qualcomm, et. al.

## Slide 27: Comparison
Sequence | Pro | Con
DL MU PPDU with Trigger | Simplified design, low overhead | (single point of failure), Does not allow for EIFS reset at legacy STA
DL MU PPDU with UL MU Response A-Control | lower overhead, robust | Optional in SFD, different trigger frame, Does not allow for EIFS reset at legacy STA
DL MU PPDU followed by MU-BAR | Simplified design, Robust, Allows for EIFS reset, Sequence required if BA is lost in the UL | Not the lowest overhead
DL MU PPDU followed by DL MU PPDU with Trigger and BAR | Sequence required if BA is lost in the UL | highest overhead, Does not allow for EIFS reset at legacy STA
DL MU PPDU with embedded Basic Trigger and BAR followed by ACK/BA |  | NOT Allowed in Baseline spec
Raja Banerjea, Qualcomm, et. al.

## Slide 28: SP#1
Do you support the following:
Add to section 25.5.1.1 of the IEEE 802.11ax :
It is mandatory at the non AP HE STA to support reception of Trigger in the DL MU PPDU aggregated with Data and respond with an ACK/BA/M-BA if the QoS ACK Policy in the DL A-MPDU is set to 01 (MU ACK) and the STA has not set the UL MU Disable to 1.
STA 1 (Basic Trigger + AMPDU)
STA 2 ( Basic Trigger + AMPDU)
STA 3 (Basic Trigger + AMPDU)
STA 4 (Basic Trigger + AMPDU)
01 (Trigger based UL MU ACK)
ACK/BA/M-BA (STA1)
ACK/BA/M-BA (STA4)
ACK/BA/M-BA (STA2)
ACK/BA/M-BA (STA3)
SIFS
DL
UL
Raja Banerjea, Qualcomm, et. al.

## Slide 29: SP#2
Do you support the following: Add to section 25.5.1.1 :
It is mandatory at the non AP HE STA to support reception of DL MU PPDU with QoS ACK Policy set to Block Ack or No ACK followed by a MU-BAR within SIFS followed by transmission of the ACK/BA/M-BA appropriately if the STA has not set the UL MU Disable to 1.
Raja Banerjea, Qualcomm, et. al.
STA 1 (AMPDU)
STA 2 ( AMPDU)
STA 3 ( AMPDU)
STA 4 ( AMPDU)
Block ACK or No Ack
MU - BAR
(STA1,STA2, STA3, STA4)
(legacy duplicate/ HE )
SIFS
ACK/BA/M-BA (STA1)
ACK/BA/M-BA (STA4)
ACK/BA/M-BA (STA2)
ACK/BA/M-BA (STA3)
SIFS
DL
DL
UL